## Slide 1: EDIPO magnet assembly Flared-end block-coil designs December 12th, 2018
X. Sarasola
(EPFL - Swiss Plasma Center)

## Slide 2: Outline
Goals and design constraints
Strand and cable
Flared-end block-coil designs
  Magnet layout
  Magneto-static analysis
  Mechanical 2D model
Conclusions

## Slide 3: Goals
Main targets of the upgraded test facility:
  15 T in a large aperture
  Operation at 4.2K and 85% of short sample limit
  Homogeneous field length of 1000 mm
  Wide range of temperature: Tsample = 4.2 - 80 K
  High-current: Isample ≤ 100 kA

## Slide 4: Design constraints
The coil aperture shall fit a 3-mm-thick vacuum chamber able to host:
  SULTAN samples (94×144 mm aperture)
  A counter-cryostat to test 100-mm-OD dipole inserts at variable temperature

## Slide 5: Design constraints
The coil aperture shall fit a 3-mm-thick vacuum chamber able to host:
  SULTAN samples (94×144 mm aperture)
  A counter-cryostat to test 100-mm-OD dipole inserts at variable temperature
Overall assembly length ≤ 2500 mm
Overall assembly diameter ≤ 1420 mm
Overall assembly weight ≤ 20 t
Operating temperature: 4.2 K
Operating current ≤ 17 kA
Dump voltage to ground ≤ 1 kV (sym ground)
Allowable coil hot spot temperature: 350 K

## Slide 6: Outline
Goals and design constraints
Strand and cable
Flared-end block-coil designs
  Magnet layout
  Magneto-static analysis
  Mechanical 2D model
Conclusions

## Slide 7: Strand and cable
A 1.1 mm strand proposed for the magnets of the FCC could be also appropriate for EDIPO
The proposed cable is a high aspect ratio Rutherford cable
Strand type | FCC | 
Diameter | 1.1 | mm
Technology | RRP 108/127 | 
Cu:non-Cu | 1 | 
RRR | >150 | 
Min. Jc @ 15 T (12 T), 4.2 K | 1640 (3000) | A/mm2
Deff,max | 60 | µm
Strand parameters
Number of strands | 44 | 
Bare width* | 26.2 | mm
Bare thickness* | 1.95 | mm
Compaction | 81 | %
Insulation thickness | 150 | µm
*After reaction
Cable parameters

## Slide 8: Outline
Goals and design constraints
Strand and cable
Flared-end block-coil designs
  Magnet layout
  Magneto-static analysis
  Mechanical 2D model
Conclusions

## Slide 9: Flared-ends coil-block designs
The former EDIPO was a 12.35 T dipole based on a CICC design
The new dipole will look more like an accelerator-type magnet
The main features of the proposed flared-ends designs have been validated in HD2 and FRESCA2
The designs also rely on the conceptual design of LD1

## Slide 10: Flared-ends coil-block designs
The former EDIPO was a 12.35 T dipole based on a CICC design
The new dipole will look more like an accelerator-type magnet
The main features of the proposed flared-ends designs have been validated in HD2 and FRESCA2
The designs also rely on the conceptual design of LD1

## Slide 11: Main design drivers
Minimization of the stress in the coil windings
  Test samples of Nb3Sn Rutherford cables [1]:
    Up to 140 MPa, the degradation is almost reversible
    Beyond 160 MPa, permanent degradation observed
Particularly challenging given the shape of the aperture
[1] J. Duvauchelle, B. Bordini, et al., IEEE Trans. Appl. Supercond., 28, 2018, 4802305.
If the reluctance forces in the iron parts are included, the peak stress can exceed 300 MPa

## Slide 12: Magnet layout
1. Window frame design
2×38 + 2×50 turns
Steel spacer between coils
2. High aspect ratio rect. coil pack
3×2×32 turns
Both flared-ends designs are based in the conceptual design of LD1
Both are non-graded designs

## Slide 13: Design 2: optimization cross-section
Aspect ratio = 1.05
Aspect ratio = 2.37
A wide range of height-to-width aspect ratios (b/a) have been explored to generate the required field in the aperture, minimizing the winding cross section and conductor peak field
Optimal aspect ratio (b/a) is found between 3 and 4
Trade-off found at b/a = 2.37 (3 double pancakes of 32 turns)

## Slide 14: Bbore vs aspect ratio

## Slide 15: Magneto-static analysis
 |  | Design 1 | Design 2 | 
Number of turns / pole |  | 2×38+2×50 | 3×2×32 | 
Aconductor / pole |  | 10494 | 11448 (+9%) | mm2
Iop (0.85×Iss) |  | 14.43 | 14.11 | kA
Current density (insulated cable) |  | 242.0 | 236.6 | A/mm2
Bbore |  | 15.03 | 15.00 | T
Max Bcond |  | 15.34 | 15.42 | T
Stored magnetic energy |  | 6.5 | 6.7 | MJ/m
Homogeneous field length (1%) |  | 975 | 977 | mm
Total coil Lorentz force | Fx | 13.9 | 14.2 | MN/m
 | Fy | -7.6 | -7.2 | MN/m
 | Fz | 1.5 | 1.7 | MN
Reluctance force (Vertical pad+ pusher) | Fx | -4.3 | -3.0 | MN/m
 | Fy | -2.3 | -2.0 | MN/m
Operational
(85% × short sample)

## Slide 16: Magnetic field quality
Normalized B field along x axis
Normalized B field along y axis
The field quality of the design 1 has been optimized to accelerator quality levels
But EDIPO is a conductor test facility
  Field homogeneity of ±1 % is acceptable

## Slide 17: Magnetic field quality
Field in the aperture (3×2×32)
The field quality of the design 1 has been optimized to accelerator quality levels
But EDIPO is a conductor test facility
  Field homogeneity of ±1 % is acceptable
Rref = 40 mm
Normalized B field around Rref = 40 mm

## Slide 18: Magnetic field quality
Normalized B field along z axis

## Slide 19: Mechanical 2D model
Shell-based mechanical structure:
  Al shell preloaded with pressurized bladders and locked with keys
  Axial preload given by end-plates and rods
  Coil pre-stress minimizes motion during coil powering
Mechanical properties:
  Coil: latest agreed properties for the design of the FCC dipoles [2]:
    E = 25 GPa (at 293 K and 4.2 K)
    α = 0.38 % (between 293 and 4.2 K)
  SS, aluminum, iron and titanium: specified for EuroCirCol magnets [3]
Contacts:
  Bonded between poles and coils (detachable poles also considered)
  Standard sliding contacts elsewhere (µ = 0.2)
[2] D. Schoerling, Private email communication. 13 June 2018
[3] D. Tommasini, “Baseline specifications and assumptions for accelerator magnet: Milestone M5.2,”
https://cds.cern.ch/record/2150689/files/CERN-ACC-2016-0030.pdf

## Slide 20: Mechanical 2D model
Displacement nominal field
Displacement nominal field
Design 1 (2×38+2×50 turns)
Design 2 (3×2×32 turns)
Contact pressure nominal field
Contact pressure nominal field
<σpole-coil2> = -19.8 MPa
<σpole-coil2> = -20.0 MPa

## Slide 21: Equivalent stress in the coils
Cool-down
Cool-down
Nominal field
Nominal field
Design 1 (2×38+2×50 turns)
Design 2 (3×2×32 turns)

## Slide 22: Max equiv. stress in the coils

## Slide 23: Outline
Goals and design constraints
Strand and cable
Flared-end block-coil designs
  Magnet layout
  Magneto-static analysis
  Mechanical 2D model
Conclusions

## Slide 24: Conclusions
Both flared-end designs satisfy the stringent design requirements:
  Generate 15 T at 4.2 K with the required field homogeneity
  Minimize the stress in the coils below 160 MPa
No major drawbacks are found in either design
Operational
(85% × short sample)
 |  | Design 1 | Design 2 | 
Number of turns / pole |  | 2×38+2×50 | 3×2×32 | 
Aconductor / pole |  | 10494 | 11448 (+9%) | mm2
Iop |  | 14.43 | 14.11 | kA
Current density (insulated cable) |  | 242.0 | 236.6 | A/mm2
Bbore |  | 15.03 | 15.00 | T
Field homogeneity | x/y axes | ±0.2% | ±1% | 
 | Rref=40mm | ±0.1% | ±1% | 
Homogeneous field length (1%) |  | 975 | 977 | mm
Peak stress |  | 143 | 131 | MPa

## Slide 25: Comparison
Design 1: 2×38 + 2×50 turns
More efficient
Requires the use of a buffer plate between coils
Peak stress in high field region
Constrained to use a very wide cable (given by aperture height)
Has to be wound as 2 double pancakes
Design 2: 3×2×32 turns
9% more conductor to generate the same field
Intrinsically lower stress in the coils
Peak stress in low field region
Not constrained to use a wide cable
More winding flexibility:
  Can be wound as a set of double pancakes, but also…
  Can be wound in layers (instead of pancakes)
Layer winding (1 coil/pole):
  Minimizes manufacturing effort
  Avoids joints & interfaces btw coils

## Slide 26: Pancake vs layer winding
Winding in pancakes
Alternative (pancake + layer winding)
  1 coil per magnet pole
  Avoids joints and interfaces between coils
+
-
+
-
+
-
+
-

## Slide 27: Additional slides

## Slide 28: Max principal stress in iron poles
Cool-down
Cool-down
Nominal field
Nominal field
Design 1 (2×38+2×50 turns)
Design 2 (3×2×32 turns)