## Slide 1: MD 3308: Instability growth rate vs chromaticity at injection
D.Amorim, S.Antipov, X.Buffat, E.Carideo, J.Dalla-Costa, T. Dascalu, J.-C. Dumont,
K. Fuchsberger, N.Mounet, A. Oeftiger, B. Salvant, D. Valuch

## Slide 2: Goal: Measure instability growth rate vs Chromaticity
MD procedure:
Setting the Octupole current to 0 A
Inject nominal bunch
Trim H-V chromaticities in a range of [-35, -5] by steps of 5
Switch OFF the ADT to let the instability develop
The Rise Time is measured from the instability signal, saved with the ObsBox
Then switch back on the ADT, reinject and restart the process again ...

## Slide 3: MD overview
1
1
2
2
3
3
16:00-16:50
16:50-18:30
18:30-20:40
Machine preparation
First set of measurement
Instabilities were triggered by setting an ~0 ADT gain in LSA
Bunch was not systematically unstable: ADT was still providing some damping
Second set of measurement
ADT modules were switched off to let the instability develop
Systematic instabilities

## Slide 4: Online observations
Head-Tail signal shows clear mode 0 for all chromaticities measured
Q’= -10
Q’= -20
Q’= -30

## Slide 5: Rise times fitted from the instabilities caught by the ADT ObsBox

## Slide 6: Results of the analysis
Predictions for LHC impedance model at injection 2017 Single bunch, Bunch intensity: 1e11 ppb
Bunch length: 1.2 ns, No damper
Measured rise times are scaled to bunch intensity

## Slide 7: Conclusion
First time the growth rate vs chromaticities was systematic measured in the LHC
  Fast measurements: many points taken in the four hours of the MD
  Both beams and planes measured
  Clear instability data
First analysis comparing measurements with predictions from impedance model:
  For H plane there is a factor 2 between measurement and simulation
  For V plane we have outliers at very negative Q’

## Slide 8: Next steps
Improve the rise time analysis by carefully looking at each measurements: fit conditioning, cross-checking beam parameters, emittance effect
Extract the mode 0 tune from the instability data to study variation vs chromaticity
Possible improvements to the procedure:
  Measure the rise time multiple times for each chromaticity to have more statistics
  Perform a finer scan of the Q’ close to zero
  Measure the chromaticity more often (during the MD, Q’ was measured every two Q’ trim)

## Slide 10: Back-up slide: Results