## Slide 1: Transport Aspects
Edward Jordan
Crab Cavity International Review – CERN – 20th June

## Slide 2: Background
Anti Shock Frame - Requirement:
  “A suitable support shall be designed to safely transport the Cryomodule from assembly premises to CERN where it will be tested and installed. The solution shall reduce all forms of vibration and shock loading to as low as reasonably practicable.”
This presentation will focus on mechanical solution to reduce shock loading.

## Slide 3: STFC Experience - Wire rope isolators
Proven to reduce shock and random vibration transmission
Experience (and Data) gained at Daresbury through shipment of 12 modules to ELI-NP in Romania
Note: isolators should be at COM height for optimum performance, this position was a compromise to maximise the number of module per transport (i.e. up to 4 modules per trailer)

## Slide 4: Vertical wire rope isolator performance
Vertical Shock – Y orientation - 1.2g (@ 36Hz)
Shock from highway event – Truck bed
Lateral Shock – high frequency and low frequency present

## Slide 5: Vertical wire rope isolator performance
Vertical Shock completely isolated
Lateral 0.1g Low Frequency (@1.7Hz) Shock remains
Response on sprung frame
We concluded from this example that although the vertical excitation was isolated, it introduced harmonic motion into the transverse plane due to the offset centre of mass vs centre of friction.

## Slide 6: Lateral wire rope isolator performance
High Frequency component not completely isolated; attributed to non optimum position of springs about COM - vertical

## Slide 7: Shock from lowering equipment onto floor (in Romania)
10g
≈ 12.5 ms
Reviewing data acquired when shipping normal conducting accelerators from Daresbury Lab to Magurele, Romania, a 10g shock can be seen over a time period of 12.5 ms, corresponding to frequency of approximately 80 hz.
This shock was observed when the equipment was removed from its anti-shock frame and lowered onto the ground (i.e. with no wire-rope isolation).

## Slide 8: Mathematical Method for spring selection (1)
First - Verify spring can withstand shock load
We calculate the input energy into the spring using one of 3 cases:
  Semi-sinusoidal shock
  Instantaneous velocity change
  Drop height
If the energy input is lower than the maximum energy absorption of that spring, the spring can be used.
acceleration
time
t
ΔV
velocity
time
Δh

## Slide 9: Mathematical Method for spring selection (2)
ΔF
  Using calculated energy change, look-up on spring energy curve to find equivalent spring deflection*.
  Using identified deflection, look-up on spring force curve to find equivalent spring force.
  Calculate acceleration applied onto load using equivalent reaction force
  *Spring data acquired from product reseller.
Second, derive transmitted force input onto Cryomodule from compressed spring by:
ΔE
Δx
Δx
ΔE → Δx → ΔF

## Slide 10: Mathematical Model - Example
Using shocks identified from data shown on pages 6,7,8:
  1.2 g (@ 36 Hz) Vertical
  10 g (@ 80 Hz) Vertical
Case Load | Input Acceleration | Input Frequency | Output Acceleration | Acceleration Reduction | Stroke Utilised
 | g | Hz | g | % | %
1 | 1.2 | 36 | 0.43 | 64 | 0.18
2 | 10 | 80 | 1.08 | 89 | 2.53
Mass of Cryomodule is a primary variable!
Mass used = 3300kg

## Slide 11: Reference Designs
SLAC CM transportation to DL
(2013)
ELI Accelerating Modules to Romania (2017)

## Slide 12: Concept Design
Transportation Frame
≈ 1050kg
Transport interface arms ≈ 52kg
Wire Rope Isolators (CavoFlex) ≈ 25kg

## Slide 13
Critical Dimensions
147mm
193 mm
306 mm
326 mm
95mm
2320 mm
4000 mm
2035 mm
x
y
z
Direction | Clearance
x | 95mm + 95mm
y | 193mm + 147mm
z | 306mm + 326mm

## Slide 14: Assembly procedure – Cryomodule into transportation frame
Transport interface arms are attached to CM
Transport frame is lowered into truck trailer
CM lowered into (and fastened) to transport frame.
Wooden panels fixed to exterior

## Slide 15: Instrumentation
Accelerometer – Slamstick with individual battery pack,
  Sampling frequency at 400hz,
  Aliasing effect at chosen sample rate to be investigated,
The instrumentation will serve to verify the suitability of the frame design.
GPS tracking-
  TO be discussed with haulage company to allow location accuracy of events during journey,
Absolute distance measurement
  Device to be investigated,
Mide Slam Stick X accelerometer
LOG-0002-100G-DC

## Slide 16: Transportation frame production planning
Content of transport plan:
Transportation method
Cryomodule internal transportation tooling
Transportation frame
Loading procedure
Instrumentation and Visual Indicators
On departure: Cryomodule checks and evidence
On receipt: Cryomodule checks and evidence
Acceptance vs failure scenarios
Note on testing:
We plan to procure a concrete block with identical size, mass and mounting points as Cryomodule,
Conduct on road testing to validate transportation frame performance,
Today

## Slide 17: Thank you for your attention

## Slide 18: Reference slides
Design envelope truck: 2.6m x 2.2m x 13.3m (HWL)
Design envelope 747 400F: 2.4m x 2.6m x 61m (HWL)
2.2m
13.3m
2.6m
2.4m
2.6m
61m
Design envelope combined: 2.4m x 2.2m x 13.3m (HWL)