## Slide 1
Calculation of corrected BPM data with polynomials obtained from BpmLab: ESRF and ALBA showcases
A. Nosych, K.B. Scheidt
ESRF, DEELS-2019
Notes: BpmLab is a 2D finite element-based tool for Matlab developed at ALBA and aimed at simulating the electrode response of BPMs of arbitrary geometry to emulated beam excitation. Lately, BpmLab has been thoroughly adapted to EBS BPM geometries to analyze the nonlinear effects and the remedies around them. More complicated situations have as well been studied, e.g. imperfect positioned BPM-buttons. Finally the 2-dimensional geometry-dependent polynomials were calculated to strongly minimize errors and coupling effects that are usually produced by the traditional Delta-over-Sum algorithms for beam position, sum signal and the incoherence (Q) values. Apart from the fast-data streams, all data & buffers of the new EBS will be calculated with such polynomial families, selectable inside the device server of the (Libera and Spark) BPM electronics. Specific beam tests were performed both in ESRF and ALBA to achieve high orbit offsets and study the effects of polynomials on the BPM data to better understand their efficiency.

## Slide 2
What is BpmLab?
a FEM-based Matlab tool for BPM response simulation and treatment
Library of many real BPMs (34 and counting…)
Geometry, mesh & map settings
Geometry outlines
Final mesh &
boundary nodes precision
2D BPM slices are defined by combinations of simple shapes: circles, ellipses & polygons
ESRF, DEELS-2019

## Slide 3
250 um
NOT OK
Examples of a badly converged mesh
OK
Properly converged mesh
Meshing:
Open-source tetrahedral mesh generator
based on metric functions (DistMesh).
Uniform or non-uniform meshes
User-defined min/max mesh size
Extremely reliable inner mesh
Boundary mesh QA: by eye. Always check!
FEM Solver:
2D electrostatic Poisson solver with linear basis functions and boundary electric potential excitation (Diriclet boundary conditions):
Green's reciprocity theorem: the surface charge induced on an electrode due to a test charge at (x,y) is proportional to the potential at that same position when the test charge is absent and the electrode is excited by a potential V.
4 calculations for all beam positions
ESRF, DEELS-2019

## Slide 4
20log(δ/Σ)
diagonal
atanh(δ/Σ) (J.Chavanne, 2002)
δ/Σ
ESRF standard SR BPM
BpmLab: Response maps & DOS treatments
ESRF, DEELS-2019

## Slide 5
booster
storage ring
ALBA BPM family
ESRF, DEELS-2019

## Slide 6
Upcoming EBS BPM family
Injection: bumped beam
Injection: stored beam
Chamber 12 (4b)
Chamber 12 (2b)
Small (6 mm button)
Large (8 mm button)
ESRF, DEELS-2019

## Slide 7
How to correct?
Linear coefficient (real-time)
Polynomial families (real-time)
Specific formulae (real-time)
Lookup tables (post-process)
Voltage inversion (iterative optimization, so post-process)
ESRF, DEELS-2019
At what level? (by DS/Libera? by end-user?)
How fast? (TbT 100x kHz, FA 10x kHz, SA 10x Hz)
Perfect BPM & low noise stable electronics are still imperfect:
Linearity error

## Slide 8
Polynomial correction
Inverted voltages
Linear correction by DOS
EBS large BPM
ESRF, DEELS-2019

## Slide 9
2 polynomials need to be applied to each data sample:
A, B, C, D
ESRF, DEELS-2019
δx/Σ
δy/Σ
Px(δx/Σ, δy/Σ)
Py(δx/Σ, δy/Σ)
Polynomial correction seems to be the straight-forward solution if you want to have large beam drifts, and have fast real-time position nonlinearity suppression.
Polynomials are coupled 2D type.
Higher power = more coefficients, e.g.:
Max pwr 7: 36 terms
Max pwr 13: 105 terms
etc.

## Slide 10
Sum signal + corrected sum (3D plot)
Coherence + corrected coherence (3D plot)
Coupling
BpmLab: Coupling
Coupling (DOS positions)
Coupling improved (Poly correction)
Coupling:
Ratio of how much the position change in one dimension affect its change in the other dimension.
Using the polynomial corrected positions can minimize the coupling effect.
ESRF, DEELS-2019

## Slide 11
Sum signal + corrected sum (3D plot)
Coherence + corrected coherence (3D plot)
Coupling
BpmLab: Sum, coherence
Signal Coherence
Sum signal
Σ = A+B+C+D
Q = (A+C-B-D) / Σ
B A
C D
B A
C D
ESRF, DEELS-2019
Sum & Coherence:
Strongly nonlinear.
Can be linearized with higher-order polynomials.

## Slide 12
A polynomial is defined by its effective ROI and max power. Ho can we pick them?
Step 1) Fix max polynomial power (here: x7y7) and scan the ROI dimensions.
Accuracy starts to deteriorates as the poly needs to fit a more curvy surface:
BpmLab: Polynomial ROI fitness
ESRF, DEELS-2019

## Slide 13
BpmLab: Polynomial power fitness
Step 2) Fix the ROI (here ±20 mm x ± 10 mm) and scan the poly power.
Step 3) Choose the power/ROI combination that fits your needs
Beware: speed of calculation can increase for higher power polynomials.
ESRF, DEELS-2019

## Slide 14
Finally we have to stop somewhere, e.g.:
ALBA SR BPM
ROI = ±[22, 10] mm
max pwr = 11
ESRF SR BPM
ROI = ±[25, 14] mm
max pwr = 15
EBS BPM
Several Poly families
selectable in Libera DS.
max pwr = ??
BpmLab: Polynomial fitness
ESRF, DEELS-2019

## Slide 15
BpmLab: Post-processing real signals
Add noise (1%) to all channels: after DOS treatment
after Poly correction
ESRF SR: injection with RF off
Each dot:
position in one BPM (224 BPMs total)
Each image: turn
ALBA SR
Local bump, 4 orbit-correctors
Hor: 0 → 3 mm
Ver: 0 → 4 mm
Poly corrected
DOS
ESRF, DEELS-2019

## Slide 16
BpmLab: Button imperfections (retraction/protrusion)
Add noise (1%) to all channels: after DOS treatment
after Poly correction
300 um retracted
Poly correction: channel A compensated
Poly correction: channel A as is
ESRF, DEELS-2019
Use “perfect Poly” to correct this distortion

## Slide 17
BpmLab: Signal manipulation
Add noise (1%) to all channels: DOS treatment
Poly correction
ESRF, DEELS-2019

## Slide 18
Requires Matlab toolbox-free installation (versions range 2014b-2017)
Instruments:
meshing (DistMesh)
short 50-line 2D electrostatic FEM solver
optimization (minFunc)
Features:
Easy arbitrary geometry input & many presets
BPM response map calculation in 2D
Correction polynomial calculation (within ROI)
Direct voltage-to-position inversion (post-processing)
Introduce geometry imperfections
Signal manipulation (channel distortion, attenuation, amplification)
Import real BPM signals for studies and post-processing
BpmLab summary
Download from here:
https://intranet.cells.es/Divisions/Accelerators/RF_Diagnostics/Diagnostics/OrbitPosition/Tools/bpmlab
ESRF, DEELS-2019

## Slide 19: Now the interesting stuff… Experiments!
ESRF, DEELS-2019

## Slide 20
ESRF (Nov 26, 2018) ALBA (May 2019)
Injecting with RF off: Signal SUM & COHERENCE
Corrected Sum =
SUMRAW / (norm_coef * SUMmodel) → 1
Q Corrected = QDOS – Qmodel → 0
ESRF, DEELS-2019
Compensation in the first turns.
Then becomes very noisy, why? Sum and Q are sensitive to beam size. It deteriorates without RF (blows up, bunch charge decrease, path & energy change).

## Slide 21
ESRF ALBA
Injecting with RF off: Polynomials vs. DOS
ESRF, DEELS-2019
RF off → beam spirals inwards.
Linear formula underestimates beam offset.
Polynomial can see farther (depends on ROI).
So finally, polynomials or DOS?
Polynomial power!!!

## Slide 22
Injecting with RF off: Scraper test
Septum blade
Each jaw kills beam at ±7 mm
DOS error ≤ 2.5 mm
Poly error ≤ 0.16 mm
Last BPM
first BPM
kicker
kicker
kicker
kicker
ALBA SR injection straight, PSA May2019
~8 meters
septum
ESRF, DEELS-2019

## Slide 23
Beam kicks: vertical plane kick
ESRF MDT Nov27: big V-kick, partial loss
Note the behavior of the Sum during the V-kick
(bunch length doesn’t change?)
MAF off
Anti-smearing on
ESRF, DEELS-2019
Very nice Q suppression!

## Slide 24
Beam kicks: horizontal plane kick
ESRF MDT Nov27: moderate H-kick, small loss
View of all BPMs
ESRF, DEELS-2019
Again a very nice Q suppression

## Slide 25
Beam kicks: horizontal plane kicks
ESRF MDT Nov27: H-kicks, loss variation
3 mA → ~3 mA
3 mA → 0.5 mA
3 mA → 1.5 mA
Sum oscillates only during H-kicks! Why?
Gets under/over compensated by SumPoly correction.
ESRF, DEELS-2019
Sum jumps 5-20%!

## Slide 26: Thank you for your attention!
ESRF, DEELS-2019

## Slide 27: extras

## Slide 28
Overlaying the measured Sum with the horizontal position -> no expected correlation:
1) black dots = simulated sum, so the sum does not get higher than 1 from beam moving left and right from the center. 2) beam goes right -> sum goes up, beam goes left -> sum goes down. How is this possible. The sum is supposed to behave symmetrically, going down in both cases after crossing zero?

## Slide 29
Experimental application: ESRF (Nov 2018) kicks
MDT Nov27: H-kicks, loss variation