## Slide 1
IHEP BI Group
The design of
Bunch-by-bunch BPM
Jianshe Cao，Xinger Zhang
June 2019

## Slide 2
content
IHEP BI Group
2 Hardware of bunch-by-bunch BPM
3 data acquisition
4 next step
1 requirements

## Slide 3
requirements
IHEP BI Group
Beecube
（Commercial board ）
1、Beam diagnostics :Self-developed BPM – BBB_board to replace the commercial board – Beecube on BEPCII.
BBB_board
（self developing board）
2、Technical reserve for bunch-by-bunch BPM research of HEPS (High Energy Photon Source )

## Slide 4
IHEP BI Group
2 Hardware of bunch-by-bunch BPM

## Slide 5
Function Block
IHEP BI Group
Trigger
Buffer of bunch by bunch raw ADC data

## Slide 6
Hardware
IHEP BI Group
ADC : 500Msps - 12bits, AC coupled
ADC_a
ADC_b
ADC_c
ADC_d
clock
Sampling clock: 500MHz,free running clock or externally clock locked with beam signal
AFE
DFE

## Slide 7
IHEP BI Group
ADC_a
ADC_b
ADC_c
ADC_d
clock
AFE
DFE
Interface: SMA, Ethernet, UART, JTAG, SFP
Memory : DDR3_PL, DDR3_PS, QSPI_flash, SD_card
Hardware

## Slide 8
ADC
ZYNQ
IHEP BI Group
BPM signal inputs
clock signal inputs
Ethernet
uart
SD card
DDR3
(PL &PS)
QSPI flash
trigger
POWER
POWER
Hardware

## Slide 9
ADC CLOCK
IHEP BI Group
Clock chip Jitter ：100fs
Each clock output delay:
150ps step size ,
range from 0 to 2250ps
Automatic find the peak value of BPM signal ， No need to use a phase shifter
BPM signal
6ns
ADC CLOCK

## Slide 10
ADC signal linearity
IHEP BI Group
ADC linear range : 5mVpp to 1.8Vpp
-33dbm to 18dbm
Input signal : 500MHz sine wave
Offset count : 2048 （offset binary 1000_0000_0000）

## Slide 11
SNR
IHEP BI Group
SNR : 68dB
Input signal: 500MHz ， 13dbm
Terminated inputs: @50ohm

## Slide 12
raw_ADC data
IHEP BI Group
Input: simulation pattern of BEPCII , repetition period 6ns

## Slide 13
IHEP BI Group
3 data acquisition

## Slide 14
Data acquisition
IHEP BI Group

## Slide 15
Data acquisition
IHEP BI Group
IP core
Raw-ADC data & Control signal
DMA
AXI4 STREAM
ARM
AXI_HP

## Slide 16
Data acquisition
IHEP BI Group

## Slide 17
IHEP BI Group
4 next step

## Slide 18
NEXT
IHEP BI Group
hardware
Software of Beam diagnostics
firmware

## Slide 19
Thanks

## Slide 22
DFE POWER(√)
FPGA CONFIGURATION(√)
I2C BUS(√)
DDR3 (√)
LINUX (√)
GbE (√)
UART (√)
DFE HW
IHEP BI Group
DFE test