## Slide 1: Dual-Readout Calorimetry Signal Analysis with Neural Networks
Murali Saravanan

## Slide 2: Overview
Dual-Readout Calorimetry Recap
Current Results
  Part I: Monte Carlo Simulations
  Part II: Real Data
  Part III: hls4ml
Future Steps

## Slide 3: The LHC and Calorimetry
Calorimeters are responsible for energy measurement in ATLAS, CMS, and various particle detectors
Hadronic and Electromagnetic Calorimetry
  protons, pions, and fragmenting quarks and gluons
Notes: Need to understand where the energy is going, otherwise we can’t reconstruct what particles are coming out of batch collisions in the LJC

## Slide 4: Hadronic Calorimetry
Measure em and non-em components
  Huge fluctuations in em component (up to 40%) on event-by-event basis
Different calorimeter materials respond to em and non-em differently. Use response curves but this works on average
Notes: EM component comes from decaying pi and eta mesons that decay into photons and electrons. This em shower energy resolution is somewhat limited in current designs.
fluctuations in the em shower fraction dominate the hadronic energy resolution, making it difficult to reconstruct energy. Hard to tell what is the em and what is not the em component. (“invisible energy”)

## Slide 5: Dual Readout Calorimetry Recap
Measure both Cerenkov and Scintillation radiation to achieve em energy resolution on event-by-event basis
  Amount of Cerenkov/Scint light can be tweaked by materials and geometry of physical calorimeter
Huge improvement for hadronic energy resolution, would be useful in future colliders (FCC, ILC, CLIC)

## Slide 6: Single Channel Readout?
Single Channel saves overhead
Four parameters vary
  Ratio of Cerenkov/Scintillation Radiation (Area)
  Scintillation Decay Rate
  Photoelectron Count
  Digitizer Freq/Bin Number
Material Properties

## Slide 7: Using NN
NN is constant time
Predict two parameters
  Cerenkov pulse area
  Scintillation pulse area

## Slide 8: Part 1: Monte Carlo Simulated Data
8

## Slide 9: Monte-Carlo Generation of Data
Modify:
  Ratio
    10-> 10x more area of Cerenkov than Scintillation
    -10-> 10x more area of Scintillation than Cerenkov
  Scintillation Decay
  Photoelectron Count
  Binning
Generate a library of histograms, varying the above parameters to create different experiments
Create many events per experiment to create needed random fluctuations
9

## Slide 10: Example Pulse
Vary Ratio between -25 and 25
Vary Scint Decay from 15ns to 50ns
1k-5k photoelectrons
30, 100, 300 bins
10

## Slide 11
11

## Slide 12
Vary digitizer freq and photostatistics
  30 bins, 5k
12

## Slide 13: Part I Conclusions
Major dependence is on ratio and not scintillation decay time
Higher photoelectron count gives better results
  Gradual change over 1k-5k photoelectrons range (no tipping point)
Higher digitizer freq ≠ better prediction
  Low freq hides the effects of fluctuations
Scintillation prediction is much more stable than Cerenkov prediction
13

## Slide 14: Part 2: Real Data
14

## Slide 15: Real Data
response of Ce-doped silica fibers exposed to electrons in the 20–200-GeV
What does a realistic pulse look like? What is the actual ratio of C/S? Expected photoelectron count?
15

## Slide 16: Average Pulse
200 GeV Pulse
[1] Cova, Francesca, et al. Physical Review Applied 11.2 (2019): 024036.
PMT Voltage (arbitrary Units)
Sample number
16

## Slide 17: Photoelectron Count
7.5k for Cerenkov, 30k for Scintillation (ratio=-4)
[1] Cova, Francesca, et al. Physical Review Applied 11.2 (2019): 024036.
17

## Slide 18
18

## Slide 19: Monte Carlo results in this area
With 5,000 photoelectrons and 100 bins, possibility of less than 1% error
19

## Slide 20: Real Data NN
In progress!
Need to consistently clean data
20

## Slide 21: Part 3: Implementation on FPGAs
21

## Slide 22: Intro to FPGAs
Multiplier Units
  Does arithmetic
Flip Flops
  Short term memory registers
Wire algorithms into board
High Level Synthesis (HLS) is the language that Xilinx FPGAs use
22

## Slide 23: hls4ml
Takes NN and creates HLS implantation that provides resource usage estimates
Up to 6,000 parallel operations=# of multiplication units=max # of nodes and weights in NN if we aim for one clock cycle per analysis
Can trade latency for lower resource usage
[2] J.M. Duarte et al., arXiv:1804.06913, April 2018.
23

## Slide 24: Preliminary Results
100 bin Model with 5ns goal
24

## Slide 25: Preliminary Results
hls4ml in general provides an overestimate of resource usage
Can prune unnecessary nodes from intermediate layer to decrease resource usage
25

## Slide 26: Project Conclusions
Dual Readout Calorimetry is promising for improving resolution of em-portion of hadronic energy on an event-by-event basis
Neural Networks can be implemented into FPGAs for low latency inference in single channel dual readout calo
  Small networks are adequate
Simulated performance of NNs can be used to inform the geometry/construction of the calorimeters and the associated hardware
26

## Slide 27: Project Conclusions
Single Channel Dual Readout Calorimetry can work thanks to Neural Networks
27

## Slide 28: Future Steps
Produce NN results on real data
Look at implementation on real FPGA
28

## Slide 29: Questions?