## Slide 1: DFX safety aspects in the LHC tunnel
Vittorio Parma (vittorio.parma@cern.ch ),
CERN, Technology Department
Event, date

## Slide 2: Contents
Safety at CERN
Pressure vessels
System description
Cryogenic safety
  Preliminary risk assessment and sizing of safety
Summary

## Slide 3: Safety at CERN (https://hse.cern/content/safety-rules)
Electrical Safety Code C1 (EDMS 335725)
GENERAL SAFETY INSTRUCTION GSI-M-4 – Cryogenic Equipment (EDMS 1327191)
  “Cryogenic equipment liable to have major safety implications” because of “high-level hazard for people, the environment or other installations in the event of failure”
Safety Guideline SG-M-4-0-1
Requested compliance with European Directives:
  Pressure Equipment Directive 2014/68/EU where relevant

## Slide 4: Pressure vessel codes regulations
Article 4, paragraph 3
Category | Conf. assessment module | Comment
SEP | None | The equipment must be designed and manufactured in accordance with sound engineering practice. No CE marking and no involvement of notified body.
I | A | CE marking with no notified body involvement, self-certifying.
II | A1 | The notified body will perform unexpected visits and monitor final assessment.
III | B1+F | The notified body is required to approve the design, examine and test the vessel.
IV | G | Even further involvement of the notified body.
For vessels with non-dangerous gases, Group 2, (cryogenic liquids are treated as gas)
Pressure European Directive 2014/68/EC (PED) is a legal obligation in the EU since 2002 and CERN’s Safety Unit (HSE) requests to comply with it:
  Applies to internal pressure ≥ 0.5 bar gauge
  Vessels must be designed, fabricated and tested according to the requirements defined
  Establishes the conformity assessment procedure depending on the vessel category, which depends on the stored energy, expressed as Pressure x Volume in bar.l
 CE marking and notified body required from and above cat II
Vacuum vessels
Pressure vessels

## Slide 5: Harmonised codes and standards
Harmonised standards give presumption of conformity with the PED, within their scope. Useful codes for cryostat design and fabrication, including safety devices:
 Now replaced by ISO 21013-3
Very useful guidelines and design rules to be used!

## Slide 6: Insulation vacuum volumes
4 independent insulation vacuum per cold powering chain
Each equipped with pressure gauge, pumping port (static), pressure relief plate
MBXF
D1
DFX
DSHx
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He @ 4.5 K
Jumper D1
Jumper DFX
2 x 18 kA
2 x 13 kA
3 x 7 kA
12 x 2 kA
DFHx1
DSHx
DFHx2
PT
PT
PT
PT
LHC tunnel
UR: Service tunnel
UL: Transverse tunnel
Item | Volume [m3] | Remark
DFX |  | 
DSHx |  | 
DFHx1 |  | 
DFHx2 |  | 
DFH flex.line |  | 
Vac.barriers

## Slide 7: Helium volumes
4 independent insulation vacuum per cold powering chain
Each equipped with pressure gauge, pumping port (static), pressure relief plate
MBXF
D1
DFX
DSHx
Superfluid @ 1.9K
Liquid He @ 4.5 K
Gaseous He @ 4.5 K
Jumper D1
Jumper DFX
2 x 18 kA
2 x 13 kA
3 x 7 kA
12 x 2 kA
DFHx1
DSHx
DFHx2
PT
PT
PT
PT
LHC tunnel
UR: Service tunnel
UL: Transverse tunnel
Item | Volume [m3] | Remark
DFX |  | 
DSHx |  | 
DFHx1 |  | 
DFHx2 |  | 
DFH flex.line |  | 
Vac.barriers

## Slide 8: Cryogenic scheme (EDMS1736906)
Cryogenic boiler circuit not yet included (recently added)

## Slide 9: DFX specification (EDMS1905633)

## Slide 10: DFX Schematic

## Slide 11: DFX volumes and cold surfaces
(W.Bailey, SOTON)

## Slide 12: Scale of pressures
Pn Nominal pressure
Ps: Design pressure
Ptest: Test pressure
Pt: burst disk set press.
bar(a)
1.3 bar(a)
3.5 bar(a)
6.43 bar(a) (1.43 x (Ps+1))
< 3.5 bar(a) (2.5 barg)

## Slide 13: PED category
Article 4, paragraph 3
Ps x V = 2800 bar.L
 Cat.3 (~4)
3.5
800

## Slide 14: The pressure safety design process
Identify all circuit/enclosed volume(s) for the cryostat to be protected (as a minimum vacuum and helium vessels)
Build the scale of pressures. As a minimum:
  Nominal operating pressure (Pn), related to the operation of the device
  Design Pressure (PS), related to mechanical limits (e.g. cavity plastic limits) or to operational scenarios (e.g. magnet quench)
  Set pressure (Pt) of the relief device < PS
  Test pressure (Ptest) depending on the norms
Make risk hazard analysis & mitigation measure:
  Risk matrix: risks, likelihood vs. severity
  Identify mitigation measures (e.g. protections of exposed bellows)
  Identify the credible worst-case scenario
Design the safety relief system according to the worst-case
  The safety relief system must be designed to keep pressure rise within the limits of the Design Pressure (PS)
  Sizing of devices according to EN 13648-3 and ISO412
Pn Nominal pressure
PS: Design pressure
Ptest Test pressure
Pt: relief device set press.

## Slide 15: Risk assessment matrix

## Slide 16: Retained pressure hazards
A) Heating/vaporization of cryogens from sudden release of stored energy in SC device from arcing
B) Accidental air venting of insulation vacuum with sudden condensation on cold surfaces, helium boil-off and pressure build-up
C) Accidental release of cryogenic fluid to higher T surfaces (thermal shield and vacuum vessel), and consequent pressure increase and increased of conduction/convection heat loads to cold surfaces
D) Brake of lambda plug(s)…
Vacuum
Air
Cryogenics fluid
B)
Vacuum
Air
Cryogenics fluid
C)
Vacuum
Air
Cryogenics fluid
A)

## Slide 17: Safety devices: preliminary sizing
Bust disc for helium reservoir
  ~ DN ? burst disk + rated valve
Relief plates for vacuum vessel
  DN 150-200 (TBC)

## Slide 18: Summary

## Slide 19
1.3 m
MgB2
Plug to D1
Liquid level
Integration reservation
Concrete
Shaft
1.6 m
MgB2-NbTi splices

## Slide 20: DSH cross section

## Slide 21
Φmax = 91mm