## Slide 1: A hydrogen-filled TPC as an active target for a proton-radius measurement at CERN
Oleg Kiselev
GSI Darmstadt
EP seminar, CERN, 15.02.2019

## Slide 2: Proton radius puzzle
CODATA: ep-scattering, H- and D-spectroscopy
Too large discrepancy with muonic hydrogen experiment
Proton radius is an important value for nuclear and particle physics
J. J. Krauth et al., 2017 [arXiv:1706.00696]

## Slide 3: COMPASS apparatus
Versatile apparatus to investigate QCD:
Two-stage COMPASS spectrometer
1. Muon, electron and hadron beams with
momenta 20-250 GeV and intensities
up to 108 particles per second
2. Solid-state polarised (NH3 or 6LiD), liquid hydrogen and nuclear targets
3. Powerful tracking (350 planes) and PID systems
(Muon Walls, Calorimeters, RICH)

## Slide 4
Slope of the form factor vs radius
High beam energy is an advantage
Muon is much heavier as electron  smaller radiative corrections
Wide Q2 -range of 10-4–10-2 GeV2 to back-up possible models
Experimental challenges especially for low-Q2
With COMPASS one can measure scattering angles down to 0.1 mrad  10-4 GeV2 and muon momentum
proton form factors GE and GM, shown as ratio to the dipole form factor GD
ratio of the cross section over the prediction for the cross
section using the standard dipole form factor.

## Slide 5
High energy muons
J. Friedrich, TUM

## Slide 6: New Letter of Intent
A New QCD facility at the M2 beam line of the CERN SPS: COMPASS++/AMBER

## Slide 8
“Classical” ionization chamber, built at PNPI
Pressure up to 10 bar
Diameter of inner anodes – 20 cm, of outer – 40 cm
Normally filled with pure H2 but D2, He are also possible
6 independent detection modules in the same gas volume
Setup with ionization chamber IKAR
Successfully used at PNPI, Protvino, CERN with protons and at GSI with radioactive ions

## Slide 9
Electrodes out of Al, 140 µm
Be windows, 0.5 mm
Energy and time of drift measured by FADCs
Energy resolution – 35-40 keV
Energy threshold <100 keV
Dynamic range for protons – 5.2 MeV
Active target IKAR
Pulse shape analysis
integral - recoil energy TR
risetime - recoil angle R (R FWHM < 0.6°)
start - vertex point ZV (zFWHM < 110 m)

## Slide 10
IKAR in Cave C

## Slide 11
Active chamber ACTAF2/R3B inside calorimeter CALIFA
Investigation of low-lying dipole strength in inelastic a scattering
Experiments on stable nuclei show significant difference to (g,g‘)
Extension to unstable
nuclei in inverse
kinematics
Coincident determination of excitation and decay energy
Allows selection of decay channel
Clean separation of E1 excitation in (a,a‘g) experiments
CALIFA
active target
g
a

## Slide 12
124Xe(α,α') measurement with ACTAF2
Beam electrodes

## Slide 13
13
z
T(e) = 720 MeV
Be windows of 0.5 mm thickness
Al
stainless steel
Anode: 1.5 mm of G-10 & 0.02 mm of Cu
Cathode: 1 mm of steel & 0.02 mm of Al
96% He + 4% N2,
10 atm
Scintillators, 2 mm
4 Si Detectors 0.05 mm
(gaps of 50 mm)
ACTAF2/R3B prototype – beam test at MAMI, 2017

## Slide 14
14
E-p scattering, energy correlations
1 AU = 22 keV
Energies correspond to those calculated by SRIM

## Slide 15: Test run with COMPASS, -p scattering
TPC between 4 tracking stations
Tracking via Si microstrip detectors
Muon rate – up to 2 MHz
Eμ = 190 GeV
Wide beam (RMS ≈ 20 cm)
Duty cycle: ~20% (spill — 5 s)

## Slide 16: Scheme of feasibility test run, CERN, 2018
Beam rate studies, background
TPC as active target D = 200 mm
Scintillators (BT) 64x48 mm ×3
Si microstrip detectors (SI) 70x40 mm ×4, short baseline limits Q2  3x10-3 GeV2
TPC and the rest of the detectors use different DAQ, timestamped

## Slide 17: Test TPC structure
Gas: H₂ (purity 6.0)
p = 1, 4, 8 bar
LCG = 220 mm
VC = 18 kV
VG = 1 kV
tCG ≈ 60 s

## Slide 18: Preamplifier - shaper
Low noise preamplifier
Best (up to now) available OA (AD891) for this setup
Signal shaping for better signal/noise
16-ch boards
No gas amplification -> very small signals
PNPI, Gatchina

## Slide 19: FADC
Struck SIS3316 VME FADC
14 bit @250 MHz (we use at 25 MHz)
5×16 channels
Range: -2,5 – +2,5 V
Modes: triggering or self-triggering
Clock PLL lock
Reading of raw ADC values or 2/4/8 points averaging
Energy threshold via Moving Average Window (MAW)
Readout via VME bus or optics
Raw data readout or signal processing with imbedded FPGA

## Slide 20: Waveforms
Waveforms have all information about the noise and signal
Energy/integral, time of signal, pile-up can be extracted

## Slide 21: Timestamp/event syncronisation
32 bit «watch/clock» @100 MHz
Sending to any device, saving the timestamps
Si DAQ – linear interpolation between the timestamps
Offline time stamps matching between Si and TPC events
TS @ 1.5 Hz
VULOM4B - logic module with FPGA
Ch. Dreisbach, TUM

## Slide 22: Events syncronyzed
Timestamp sync – TPC DAQ and Si/trigger DAQ
Files recorded independently, processed and sync offline
Width of the coincidence peak - drift time of the TPC (60 µs)
Primary vertex–Z correlation with the active volume of the TPC

## Slide 23: Matched events – energy correlations
Ch. Dreisbach, TUM

## Slide 24: Count rates during the test run
* area - 10% of full anode area of TPC
TPC has a self-triggering, independent DAQ
Raw waveforms possible to store
Detector TPC S* Se Si*
Mean 16 Hz 64 kHz 640 kHz 22 kHz
Max 46 Hz 370 kHz 3.7 MHz 43 kHz
Events total: 4 600 000
With thr. 300 keV: 1 100 000 With thr. 200 keV: 3 500 000
8 bar: 4 290 000 4 bar: 310 000

## Slide 25: TPC energy resolution vs beam rate
Test pulses injected to all anodes at the same time
Measured vs beam intensity
At 300 kHz beam rate energy resolution 40 keV
Threshold 200 keV and
lower possible

## Slide 26: Gas quality check during each experiment
α-spectrum measured several times per day
Shift of the maximum ~1%/day (~1 ppm O₂)
Refilling – once per week

## Slide 27: Vertexes from the Si tracker
Ch. Dreisbach, TUM
All cuts applied All cuts except z position

## Slide 28: Main experiment at CERN
Beam size: σ ≈ 8 mm
Energy: 100 GeV
Scattering angles: 0.3 – 2 mrad (Q² = 0.001–0.04 GeV²/c²)
Base: 5 м — scattering 1.5 – 10 mm
Si detectors Δx < 10 µm (Δθ < 2 rad at 5 m)
New fast electronics fro the Si detectors
Scattering trigger («kink trigger» — SciFi detector)
New active target: diameter — 800 мм, 20 bar H₂
EU ATTRACT grant is
requested (GSI – TUM)

## Slide 29: Large TPC as active target
820 mm long, inner diameter 1000 mm
Total volume 600 liters
Internal surfaces electrically polished
Gas pressure up to 20 bar
Spherical Be beam windows
HV up to 80 kV
Ep = 0.5 – 20 MeV
HV, pressure, temperature measurements with precision 0.01%  target density precision and drift velocity with precision 0.02%
Laser system for
drift velocity control

## Slide 30: Momentum transfer requirements
Ch. Dreisbach, TUM
TPC minimum - Q² = 10-4 – 10-5 GeV²/c², depending on pressure

## Slide 31
J. Friedrich, TUM

## Slide 32: Plans and beam time request

## Slide 33: Summary
Application of ionization chamber (without gas amplification) as an active target for the elastic proton scattering at high and intermediate energies is very powerful method to study the nuclear matter distribution
Similar technique can be used for µ-p experiments aiming the measurement of the proton radius with high precision
Test experiment shown feasibility
Background and useful rate is measured and acceptable
TPC can run with independent from COMPASS DAQ, timestamp technique is proved
Large baseline for the Si tracker and using He tubes is crucial
New SciFi detectors need to be developed
New setup can be ready for the test run in 2021 and for main run in 2022 (funding dependent)

## Slide 34
Backups

## Slide 37: Proton range in hydrogen