## Slide 1
WP4-Task5: Integration
Markus Aicheler
Helsinki Institute of Physics
28.02.2019

## Slide 2
Recap: What we would like to do for XLS
Help establishing alignment and stability requirements for each component in the linac
Develop design for support structure of components for the entire length of the accelerator
Use lessons learned from CLIC module for high quality and affordable realization of support design
Use synergy in prototyping for CLIC module to improve XLS support design if necessary

## Slide 3
Task 5: Integration
Description:
Providing a framework for condensing/bringing together mechanical designs and related systems designs
Translating stability requirements of components in concrete mechanical designs for supports
Ensuring proper interfacing with adjacent injector and undulator
Establish lists of components for costing exercise
Issue space allocations?
Auxiliary systems (magnets, vacuum, cooling, …)

## Slide 4
Module layout of XLS?
Acc-Structure
Quad
Splitter
PC
Klystron/Modulator
103 cm
45 cm
Acc-Structure
Acc-Structure
…
Sector valve
30 cm
6 cm
Conn+
DN40PP
BPM
Corrector
25 cm
25 cm
103 cm
Mode converters
+ circular WG

## Slide 5
Dimension parameter list of components
Element | Active length in m | Mechanical length (approx.) in m
Accelerating strcuture | 0.90 | 1.03
AS-AS-connection (inlcuding pumping port DN40) | 0.06 | 0.06
Accelerating strcuture | 0.90 | 1.03
AS-Quad connection (including corrector + PP-DN40) | 0.25 | 0.25
Quad | 0.23 | 0.45
Quad-AS connection (including BPM + PP-DN40) | 0.25 | 0.25
Vacuum sector valves ? | 0.30 | 0.30
Module length (2 times sum) |  | 6.44
This assumes only two AS between Quadrupoles!!!

## Slide 6
Performance parameters table of components
Element | Alignment tolerance lateral | Alignment resolution | Alignment tolerance longitudinal | Alignment resolution | active?
Alignment tolerances: |  |  |  |  | 
Accelerating structures | 100 | 10 |  |  | 
BPM | 100 | 10 |  |  | 
Quad | 100 | 10 |  |  | 
Correctors | 100 | 10 |  |  | 
Other components to be considered: |  |  |  |  | 
WG network |  |  |  |  | 
PC (SLED or BOC) |  |  |  |  | 
Supports (Girders) |  |  |  |  | 
Electronics |  |  |  |  | 
Other BI (e.g. BLM, etc.) |  |  |  |  | 
Other requirements to be considered for each component: |  |  |  |  | 
Vacuum |  |  |  |  | 
Temperature stability |  |  |  |  | 
Cooling water supply |  |  |  |  | 
Mecahnical Stability |  |  |  |  | 
Radiation |  |  |  |  | 
Other: |  |  |  |  | 
C&V |  |  |  |  | 
Tunnel cross section |  |  |  |  | 
other infrastructure |  |  |  |  | 

## Slide 7
Systems
 | In charge
Accelerating structures | INFN-LNF
RF distribution | INFN-LNF
Pulse compressor | INFN-LNF
Klystron/modulator | Uppsala
Magnets | 
Beam instrumentation | 
Vacuum | 
Alignment | 
Supports | 
Power | 
Ventilation | 
Cooling | 
Radiation | 
Controls | 
Machine protection | 
Cost&Schedule | 

## Slide 8
Summary
More feedback needed on system requirements/performance of main systems
Started work on not covered systems for accelerator
Need for closer work with beam dynamics group