## Slide 1
WP4 progress meeting
Thursday Feb 28 2019
A. Gallo
INFN-LNF, Frascati, Italy
On behalf of the EuPRAXIA@SPARC_LAB RF and LINAC team (*)
(*) D. Alesini, M. Bellaveglia, S. Bini, B. Buonomo, F. Cardelli, E. Chiadroni, G. Di Raddo, R. Di Raddo, M. Diomede, M. Ferrario, A. Gallo, A. Ghigo, A. Giribono, V. Lollo, L. Piersanti, B. Spataro, C. Vaccarezza, (INFN-LNF)
and with the contribution of N. Catalan Lasheras, A. Grudiev, W. Wuensch (CERN)

## Slide 2
Unification of the RF modules of the Eupraxia@Sparc_Lab and CompactLight design studies;
Very preliminary considerations on increasing the rep rate of the RF power sources for both projects; discussion involving Toshiro Anno (Canon), Claude Van Daele (CPI) and Mikael Lindholm (Scandinova)
Progress on the accelerating section RF coupler design
SUMMARY
2

## Slide 3
Freq. of 2π/3 mode [GHz] | 11.9942
Average iris radius <a> [mm] | 3.5
Total length of the TW structure Ls [m] | 0.9
RF pulse [µs] | 1.5
Average gradient <G> [MV/m] | 65
Linac Energy gain Egain [GeV] | 1
Linac active length Lact [m] | 18
Unloaded SLED Q-factor Q0 | 180000
External SLED Q-factor QE | 21600
Iris radius a [mm] | 4.0-3.0
Group velocity vg [%] | 3.7-1.5
Effective shunt Imp. Rs [M/m] | 389
Filling time tf [ns] | 130
Input power per structure Pk_s [MW] | 9.8
Structures per module Nm (input power per module Pk_m [MW]) | 4 (39)
Total number of structures / klystrons | 20 / 5
EUPRAXIA@SPARC_Lab <a>=3.5 mm
EUPRAXIA@SPARC_Lab <a>=3.2 mm
EUPRAXIA@SPARC_Lab old working point
(optimization of RF power splitting)
Best effective shunt impedance
3
Linac active length=18 m (was 16 m of the old working-point), but 16 structure interconnections eliminated
Linac energy on crest = 1.17 GeV with 5 klystons ( in the old WP was 1 / 1.1 GeV with 4 / 5 klystrons)
Using the CompactLight accelerating section for EUPRAXIA@SPARC_LAB

## Slide 4: Using the CompactLight accelerating section for EUPRAXIA@SPARC_LAB
Potential advantages are:
Waveguide distribution network simplified (less accelerating sections per module);
Linac filling factor improvement (active length / real length)
Wider average iris radius (3.5 mm vs. 3.2 mm, larger beam stay-clear)
Larger operational gradient (65 MV/m)
Larger final energy (1170 MeV vs. 1102 MeV)
Fully synergic with CompactLight design study
while potential drawbacks are:
Fabrication of longer structures;
Larger UHV residual pressure in the center of accelerating sections;
…..
The X-band linac baseline shown in the EUPRAXIA@SPARC_LAB Conceptual Design Report is based on 4 modules hosting 8 x 50 cm long TW cavities each (16 m of active length), powered by 4 or 5 klystrons in total. We are proposing to change this baseline for a new one based on 5 RF modules of the type designed for Compact Light, hosting 4 x 90 cm long TW cavities (18 m of active length).
The proposal will be discussed in the next collaboration meeting @ LNF, on March 8th 2019
4

## Slide 5: REMINDER: CompactLight Preliminary Specification
The table separates the FEL output requirements into the two regimes of operation (soft/hard x-ray) to show which parameters are required in combination.
 | Soft x-ray | Hard x-ray
Photon energy [keV] (min-max) | 0.25 - 2 | 2 - 25
Wavelength [nm] (max-min) | 5 - 0.6 | 0.6 - 0.05
Repetition rate [Hz] | 1000 | 100
Maximum pulse energy [mJ] | Not specified | 1 (at 25 keV, less at other energies?)
Number of photons | Not specified | 2.5 x 1011 at 25 keV
Pulse duration [fs] | 0.1 – 50 | 
Polarisation | Variable, selectable | Not specified
Two-colour pulses: time separation [fs] | -20 -> +40 | 
Two-colour pulses: photon energy variation (max. of E2/E1) | 2 (270-530eV), 1.2 for the rest of the range | 1.1

## Slide 6: Compact Light FEL Specification
Low energy, high rep rate
High energy, low rep rate

## Slide 7
CPI VKX-8311A
Any klystron model is optimized by design to be operated in a specific working point characterized by 3 parameters:
Max RF power in saturation ;
Pulse duration (flat top + transient);
Repetition rate .
The tube efficiency is defined as :
and it is maximum when the tube is operated at the nominal working point.
The klystron operational rep rate can be increased at expenses of the saturated RF power (by decreasing the tube HV) and/or the pulse duration.
The main limitation for the rep rate increasing comes from the power released on the tube collector which can not exceed a limit value corresponding to the nominal working point (with some margin).
Towards higher rep rate operation of the RF power sources
7

## Slide 8
mainly depends on the modulator characteristics
Scandinova modulator pulse for C-band klystron
8

## Slide 9
Klystron collector power limits are conservatively specified by manufacturers assuming transient durations longer than those provided by state-of-the-art solid state modulators. Canon (formerly Toshiba) specifies tubes (E37113 - X band and E37212 – C band) assuming .
Assuming the same value for the CPI VKX-8311A klystron (to be verified with CPI), we got:
The amount of rep rate increase obtainable by reducing the pulse duration depends very much on the actual value of the dead time τtrans, which is a characteristics of the modulator.
Since the limit imposed by can not be overcome, the rep rate can only be increased at the expenses of the RF saturation power (HV working point) and/or RF pulse duration.
The amount of rep rate increase obtainable by reducing the HV and the RF saturation power is limited by the tube efficiency decrease.
9
Klystron efficiency vs. power derating

## Slide 10
50 MW, 1.5 µs, 100 Hz
50 MW, 140 ns, 220 Hz
SLED removed
1st scenario: pulse shortening
rep rate increase limited by modulator dead time (≈1.5 µs)
Linac energy downgraded to ≈ 45% of the max value @ 220 Hz rep rate;
Not flexible: as soon as the SLED is removed the gradient is reduced by a factor ≈2.2;
Klystron operated always at its nominal working point (good!);
Max rep rate very much dependent on modulator dead time τtrans
KLYSTRON
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
KLYSTRON
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
1 klystron x LINAC Module
<Eacc> = 65 MV/m
1 klystron x LINAC Module
<Eacc> = 30 MV/m
10

## Slide 11
1 klystron x LINAC Module
<Eacc> = 65 MV/m
50 MW, 1.5 µs, 100 Hz
1 klystron x LINAC Module
<Eacc> = 29 MV/m @ 200 Hz
<Eacc> = 20.5 MV/m @ 250 Hz
1.5 µs, 10 MW, 200 Hz
1.5 µs, 5 MW, 250 Hz
2nd scenario: klystron peak power reduced
rep rate increase limited by klystron inefficiency at reduced HV values
Linac energy downgraded to ≈ 30% of the max value @ 250 Hz rep rate;
Flexible: different compromises between rep rate and RF peak power explorable;
Klystron operated in a wide range of working points (realistic?)
KLYSTRON
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
KLYSTRON
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
11

## Slide 12
3rd scenario: high rep rate – reduced peak power klystrons
rep rate increase based on dedicated tubes, in substitution of or in addition to high peak power ones
2 klystrons x LINAC Module
<Eacc> = 65 MV/m @ 100 Hz
<Eacc> = 23 MV/m @ 1 kHz
6 MW, 1.5 µs,
1 kHz
1 kHz rep rate capability, with linac energy up to ≈ 35% of the max value;
Switching or combining 2 sources would preserve high gradient at low rep rate;
If source combination is possible, gradients > 30 MV/m available at rep rates ≤ 250 Hz;
CPI will probably announce a new tube capable of delivering 10 MW, 1.5 µs, 1 kHz (≈ 30 % gradient increase wrt E37113)
6 MW, 1.5 µs, 1 kHz operation probably possible
Canon E37113
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
CPI VKX-8311A
RF smart combiner / switch
50 MW, 1.5 µs,
100 Hz
Canon
12

## Slide 13
3rd scenario: high rep rate – reduced peak power klystrons
rep rate increase based on dedicated tubes, in substitution for or in addition to high peak power ones
2 klystrons x LINAC Module
<Eacc> = 65 MV/m @ 100 Hz
<Eacc> = 23 MV/m @ 1 kHz
6 MW, 1.5 µs,
1 kHz
Canon E37113
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
CPI VKX-8311A
RF smart combiner / switch
50 MW, 1.5 µs,
100 Hz
new CPI high rep rate kly
This study is very rough and need to be continued more rigorously, but we need:
more precise requests and specifications by FEL users
more technical data from klystron producer
more experimental data from existing power plants (high rep rate tests @ X boxes?)
maybe new creative ideas to better exploit the existing hardware …
13

## Slide 14
Study on couplers for EuPRAXIA@SPARC_LAB

## Slide 15: Slot coupler (z-type, input, 80 MV/m)
W/O racetrack
W/ racetrack
ΔT < 19° C
ΔT < 25° C
58 MW input power, 100 ns pulse length (70 MW and 130 ns for XLS)
Equivalent focusing/defocusing quadrupole gradient on the x plane at the center of the coupler:
r=2mm
a1=3.629 mm

## Slide 16: Waveguide coupler (input, 80 MV/m)
W/O wg tapering
W/ wg tapering
ΔT < 10° C
ΔT < 11° C
58 MW input power, 100 ns pulse length
waveguide
Matching cell
r=2mm
r=2mm

## Slide 17: Waveguide coupler (input, 80 MV/m)
Equivalent focusing/defocusing quadrupole gradient on the x plane at the center of the:
Waveguide
Matching cell

## Slide 18: Couplers comparison (slot vs waveguide)
 | ΔT [°C] | g_B [T/m]
slot | < 25 | -0.006
waveguide | < 11 | 0.015 (waveguide), 0.377 (matching cell)
Work in progress:
Calculate gB (and gE) along z
Calculations considering the injection phase
Calculate the integrated gradients