## Slide 2: LIU-PS Beam Dynamics WG Topics and Priorities 2019
LIU Beam Dynamics Coordination Meeting
5 February 2019
H. Damerau, M. Fraser, V. Forte, A. Huschauer, A. Lasheen

## Slide 3: Overview
Transverse studies
  Topics, priorities and milestones
Longitudinal studies and priorities
  Topics, priorities and milestones
1st half 2018
2nd half 2018
2018-2019
Colour code for timeline:

## Slide 4: Transverse studies I
Analysis of new KFA45 field measurements
  double check emittance growth estimates, in particular for the post-pulse
  check damping by transverse feedback
  Milestones:
    Review blow-up estimates made only with PSpice and current measurements
    Theoretical study of blow-up with LIU damper with field information
Prepare approach for PSB-to-PS transfer line matching after LS2 using turn-by-turn acquisitions:
  Theoretical study followed by tools and scripting
  Approach needs considering, dedicated knobs vs. brute force optimisation?
  Thought needed on constraints (transmission, steering, etc)
  Milestones:
    Theoretical study of optimisation process, leading to script/OP tool
    Follow up Run 2 data using BGI as turn-by-turn monitor for commissioning
Emittance blow-up studies
  Analysis of PSB/PS brightness curve measurements (new and old WS, TFL SEM grids):
    BCMS 0.9 eVs, BCMS 1.5 eVs and. matched TL optics for both cases
  Follow up of turn-by-turn PS injection SEM grid data taken in Run 2 adding data with deconvolution to brightness curves
  Study the importance of systematic errors
  Milestones:
    Coherent report of measurements and analysis

## Slide 5: Transverse studies II
Analytical and simulation studies
  systematic effects of filamentation (mis-steering, betatronic and dispersive mismatch) on emittance measurements in presence of dispersion (deconvolution)
  Importance of the knowledge of the underlying distribution
    Deconvolution algorithm vs. RMS quantities
  A continuation of the work Eugenio started
  Space-charge to be added in a second step
  Milestones:
    Identify the parameter range (betatronic vs. dispersive emittance, acceptable level of distortion to Gaussian distribution, role of tails) in which we can be assured our present techniques are reliable
    Propose techniques that can be applied online after LS2 to improve deconvolution and emittance measurements
Analysis of data probing sensitivity to WP and role of space-charge in first turns after injection
  MD data with WS and BGI available
  Milestones:
    Coherent report of measurements and results

## Slide 6: Transverse studies III
Space-charge simulation studies to investigate importance at PS injection
  Importance of the integer resonance
    Closed orbit perturbation, optics errors, …
  Details provided by Hannes and Haroon
  Milestones:
    Understand from simulation role and importance of space-charge in first few ms after injection
Follow-up of beam size measurements with new BI instruments
  Prototype WS
  Horizontal BGI
  Milestones:
    Towards an operational use (software, analysis algorithms,…)
Optics measurements
  Progress with data analysis for the different configurations measured in 2018
  Provide the necessary input for emittance reconstruction
  Milestones:
    Coherent report of measurements and results
    Operational tools for regular measurements after LS2
WP optimization along the cycle
  Analysis of the matrix measurement campaign
  Milestones:
    Established improved PFW control scheme

## Slide 7: Longitudinal studies I
Understand impedances sources exciting longitudinal instabilities
  Source of coupled-bunch instabilities
  Tracking simulations to understand contribution of major impedances
  Complete analysis of 2018 data with multi-bunch LHC-type beam
  Study potential improvements (e.g. impedance measurements on cavities, etc.)
  Milestones:
    Reproduce coupled-bunch oscillations (mode number)
    Proposals for impedance measurements and reductions on cavities or other objects
Performance predictions for RF upgrades during LS2
  Reduction of instabilities and transient beam-loading (parameter variation along batch)
    Upgraded 10 MHz amplifier
    Improved feedbacks for 40 MHz and 80 MHz cavities: amplifiers, air lines, etc.
  Existing 40 MHz cavities as Landau RF systems: expected performance and limitations
  Milestones:
    Longitudinal stability limits for the after-LS2 era
    Prediction of bunch-to-bunch intensity variation

## Slide 8: Longitudinal studies II
Parameter choices for post-LS2 era
  Parameter tables for post-LS2 cycles derived from beam point of view: RF voltages during ramp, longitudinal emittance along the cycle
  Choice intermediate plateau (> 2.5 GeV) energy for RF manipulations
  Improved control of longitudinal settings: constant bucket area, transition crossing, approach to splitting adjustments (high-level knobs, machine learning)
  Future of non-baseline beams: 8b4e, 80b, pure batch compression
  Milestones:
    Post-LS2 cycles optimized for longitudinal performance
    Proposal of high-level knobs for RF parameter control and setting-up procedures
Review and upgrade longitudinal Tomography (not only PS)
  Studies with simulated data to improve understanding of results from tomography, their interpretation and typical error bars
    Emittance, momentum spread, bunch length (and their definition)
  Review tomography algorithm: multi-bunch tomography, bunch parameters, etc.
  Milestones:
    Updated/upgraded tomography algorithm

## Slide 9: Longitudinal studies III
PS-SPS transfer (in collaboration with SPS)
  Review longitudinal emittance at transfer and consequences on LIU baseline
  New ideas for optimization bunch rotation?
  Milestones:
    Propose parameter set for post-LS2 bunch rotation
Longitudinal impedance model
  Comparison pre- and post LS2
  Missing elements and priorities for simulations, revisit beam measurement of impedance
  Measurements during LS2?
    Cavities: 10 MHz, 80 MHz (when turning cavity), crosscheck different measurements
    New equipment before its installation
  Milestones:
    Complete longitudinal impedance model for the post-LS2 PS

## Slide 10: Longitudinal studies IV
Tools
  Future longitudinal beam observation system
  Machine learning to optimize longitudinal settings: development and training with simulated data
  Acquisition and analysis of MD data post-LS2 (not only PS)
  Milestones:
    Bunch splitting studied as test case for machine learning
    Proposal for MD data handling after LS2
Ions in PS
  Study source of microwave instability at transition
  Emittance increase during the cycle
  Parameters for acceleration of ion species other than Pb54+? Oxygen?
  Milestones:
    BLonD simulation of transition crossing (protons and ions)
    Identification of potential source impedance for microwave instability

## Slide 11
THANK YOU FOR YOUR ATTENTION!