## Slide 1: Cooling of Bunched Beams
S. Albright, H. Bartosik, N. Biancacci, A. Saa Hernandez, M. Zampetakis

## Slide 2
Motivation
Cooling of a Coasted Beam vs. Bunched Beam
  Single Harmonic
  Double Harmonic
Exploring Parameter Space
  Tune Scan
  Intensity Scan
Future Work
Layout

## Slide 3
Motivation
PhD Thesis Title: Studies of non-linear and incoherent effects and their mitigation in low emittance rings.
CLIC’s Damping Rings:
LEIR:
Cooling Effects
Heating Effects
Synchrotron Radiation
Space Charge
IBS
Cooler
Goal: Develop a framework in order to study the interplay of all three effects and compare it to some measurements.
Space Charge
IBS
Equilibrium emittances reached in both cases.

## Slide 4
Typical Case
Cooling
Our Case
Cooling
Cooling of a Coasted Beam VS Bunched Beam 1/3
Cooling of a coasted beam.
  Damp the transverse emittances and momentum spread.
Switch off the cooler and do the RF-capture.
Cooling time is extended.
  Cooling of a bunched beam.
  Beam is damped in all 3 planes leading to complicated dynamics.

## Slide 5
When the beam is captured, beam losses and a transverse emittance blow-up associated to SC and IBS are always observed.
  A bunched beam, being more compressed, suffers from more losses.
By changing the gun voltage of the electron cooler, we can drag the ion beam to a frequency which has an offset with the RF frequency.
Cooling of a Coasted Beam VS Bunched Beam 2/3
Longitudinal dynamics due to RF cavity
Time
Frequency
Longitudinal dynamics due to Cooler

## Slide 6
When the beam is captured, beam losses and a transverse emittance blow-up associated to SC and IBS are always observed.
  A bunched beam, being more compressed, suffers from more losses.
By changing the gun voltage of the electron cooler, we can drag the ion beam to a frequency which has an offset with the RF frequency.
  Hollow distributions are created leading to less losses.
Cooling of a Coasted Beam VS Bunched Beam 3/3
:

## Slide 7
Turned off the RF-cavity.
Using the Schottky tool, we measured the revolution frequency of the ions for every value of gun voltage.
That way we can create a calibration curve of voltage with frequency.
Calibration of Frequency - gun voltage

## Slide 8
Single Harmonic 1/2
Losses between the start of RF and the start of ramping, as a function of gun voltage.
Peak Line
Density
*Best case losses ~18%

## Slide 9
Single Harmonic 2/2
Profiles for central case
Profiles for minimum losses

## Slide 10: Longitudinal Profiles – Single Harmonic
*Colorbar not calibrated.

## Slide 11
Double Harmonic 1/2
Losses between the start of RF and the start of ramping, as a function of gun voltage.
Peak Line
Density
*Best case losses ~4%

## Slide 12
Double Harmonic 2/2
Profiles for central case
Profiles for minimum losses

## Slide 13: Longitudinal Profiles – Double Harmonic
*Colorbar not calibrated.

## Slide 14
Can we get the same for high Intensities?
Some Conclusions
Optimum settings for minimum Intensity losses.
Double Harmonic.
cooler is set to lead to flattest longitudinal profile.

## Slide 15
Low Intensity - AMDOPTIC Cycle
Accumulated charges
AMDNOM Cycle
Accumulated charges
And for High Intensity… (1/3)
Best case!
Beam not well-captured losses during capture.
Well-centered beam during capture.
Much more compressed beam more losses!
Intensity (1e10 charges)
Time (ms)
Intensity (1e10 charges)
Time (ms)

## Slide 16
Losses evaluation between the (usual) times, 1440ms and 1800ms
Much more losses (~25%) due to the higher Intensity.
And for High Intensity… (2/3)

## Slide 17
Less losses (~6%) if evaluated for shorter time.
Well-centered beams suffer from less losses during capture but are affected more by SC and IBS.
Off-centered/flat beams suffer from less losses, long-term.
Intensity (1e10 charges)
Time (ms)
And for High Intensity… (3/3)

## Slide 18
Tune Scans
With skew sextupoles.
Well-centered beam Maximum cooling.

## Slide 19: Vertical Tune Scan
Blow-up…
1380ms
1800ms
Cooler is turned off…
Excited Resonance!
Sextupoles at
XSK41 = -1.5
XSK42 = 1.5
Capture…
Cooling

## Slide 20
Single Harmonic – Excited Sextupoles
Almost no intensity close the 2.66 resonance.
Not sure about the emittance blow-ups due to the “noisy” areas.

## Slide 22
Single Harmonic – Excited Sextupoles
Bunch length follows the intensity behavior No evidence that IBS affects the beam longitudinally.

## Slide 23
Double Harmonic – Excited Sextupoles
Almost no intensity close the 2.66 resonance.
Much smaller “noisy” areas.

## Slide 24
Intensity Scan
Single Harmonic.
No skew sextupoles.
Bare working point.
Well-centered beam Maximum cooling.

## Slide 25
Intensity Scan
Done by changing the position of a corrector magnet (“BHN10”) in the transfer line.

## Slide 26
Intensity Scan

## Slide 27
Next Steps…
Further investigation of the “noisy” areas.
Study in more detail the bunch length and the SC Tune Spreads.
Start implementing a tracking code with IBS and SC to see if similar results will be produced.
Maybe there will be a distinction between the IBS or SC dominance in our cases.

## Slide 28
Thanks for your attention…

## Slide 29
Reserve…

## Slide 30
Comparison

## Slide 31
Single Harmonic– Excited Resonance

## Slide 32
Double Harmonic – Excited Resonance

## Slide 33: Single Harmonic - No Sextupoles

## Slide 34
Tune Scan – Bunched beam – Single Harmonic

## Slide 35
Initial VS Final Emittance

## Slide 36
Tune Scan – Bunched beam

## Slide 38
Tune Scan – Bunched beam

## Slide 39
Tune Shift Evolution

## Slide 40: Double Harmonic – No Sextupoles

## Slide 41
Tune Scan – Bunched beam – Double Harmonic

## Slide 42
Initial vs Final Emittance

## Slide 43
Emittance Blow-up

## Slide 44
Emittance Blow-up – Intensity Scan