## Slide 1: Triplet string kinematics reminder
F.Micolon – 06/02/2019

## Slide 2: Introduction
The supporting scheme of the triplet is not common to the rest of the LHC cells
The jacks of the triplets proposed by Survey are a modified version of the LHC jacks
The installation of the triplets was subject to several iterations until the very end
The aim of this presentation is to recall briefly what we have in the tunnel currently

## Slide 3: The LHC Jacks
The LHC jacks is based on a tilting column principle – with two bearing on each end.
It allows the position control in the vertical direction and one transverse direction (the other transverse direction is free by design – see next slide).
Tilting is controlled by tightening the side nut
In the LHC triplets, the side nut is removed. So this becomes a free transverse direction (no control).
Top bearing
Tilting column
Bottom bearing
Jack piston
Jack frame

## Slide 4
The LHC Jacks
Top bearing
Tilting column
Bottom bearing
Jack piston
Jack frame
This transverse direction is free by design with a range of +/-10mm.

## Slide 5: The triplet string – general layout
IP (Atlas, CMS, Alice, LHCb)
~35m
Q1
Q2
Q3
DFBX
Q1Q2 Interconnection
Q3DFBX Interconnection
Q2Q3 Interconnection

## Slide 6
The triplet string – jack support scheme
Longitudinal
Radial
Q2
Jacks A&B are used to adjust the radial position of the magnet.
The magnet longitudinal position cannot be adjusted with the jacks (since the nut of jack D are removed).
All jacks can be used to adjust the vertical position of the magnet.
Longitudinal jack with nut removed

## Slide 7
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
Bellow (flexible)
Spiders (considered free longitudinally)
Jacks (all free in the longitudinal direction)
Vacuum vessel
Magnet cold mass
Fixed point
Side view
When the jack nuts are removed the longitudinal position of the magnet is indeterminate (except for bellow stiffness)

## Slide 8
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
Tie rods
Tie rod ears
Bellow (flexible)
Spiders (considered free longitudinally)
Jacks (free in the longitudinal direction)
Vacuum vessel
Magnet cold mass
Fixed point
Tie-rods are added at the interconnection level to transmit any longitudinal load to the DFBX (=longitudinal fixed point).
Side view

## Slide 9
The triplet string – simplified axial kinematics
Q1/Q2
Tie-rod ear
Tie-rod
W bellow
Tie-rods transmit the load in the compressive direction only (non-IP direction).

## Slide 10
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
Tie rods
Tie rod ears
Bellow (flexible)
Spiders (considered free longitudinally)
Jacks (free in the longitudinal direction)
Vacuum vessel
Magnet cold mass
Fixed point
Since the spiders were not strong enough longitudinally – cartridges were added to link the Q1 & Q3 cold mass to their vacuum vessel (not the case of Q2).
Cartridge

## Slide 11
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
When the insulation vacuum is emptied, the vacuum force applied to Q1 is 80 kN.
This force is transmitted through the tie-rods to the DFBX.
This leads to a cumulative displacement of the vacuum vessels in the non-IP direction (with the top displacement on Q1).
Vacuum force
80 kN
Vacuum force
80 kN**
** Valid at point 1 and 5 (no superconducting D1)
Q1 non-IP motion
Q2 non-IP motion
Q3 non-IP motion

## Slide 12
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
When the cold mass are filled with liquid Helium under pressure (nominal) pressure forces are generated when the cold mass flanges are not symmetrical (this is the case on Q1 & Q3).
Vacuum force
80 kN
Q1 He pressure
22 kN*
Q3 He pressure
4 kN*
*Forces corresponding to the nominal operational conditions
** Valid at point 1 and 5 (no superconducting D1)
Vacuum force
80 kN**

## Slide 13
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
When at cold, the cold mass will shrink
This stretches the interconnection bellows
 Which produces a pulling force on the cold mass
When we sum up all operational forces acting on each cold mass :
Vacuum force
80 kN
Q1 He pressure
22 kN*
Q3 He pressure
4 kN*
Bellow stretch
Q1Q2 – 22 kN*
Bellow stretch
Q2Q3 – 22 kN*
Bellow stretch
Q3DFBX – 10 kN*
* Force values corresponding to the operational conditions
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
Vacuum force
80 kN
Q1 net force = ~0 kN
Q2 net force ~0 kN
Q3 net force = -8kN
Vacuum force
80 kN**
Vacuum force
80 kN**

## Slide 14
Conclusion
The triplet kinematics results from a large set of operational factors
  Insulation vacuum
  Cryogenic parameters (pressure and temperature)
  Bellow stiffness
  Tunnel temperature
In the nominal operational conditions the cold mass pressure and bellow force cancel out – so the main contributor to the triplet kinematic is the vacuum.

## Slide 15
Spare slides

## Slide 17: Jack fixation to ground

## Slide 20
Test in 2017 - From M.Guinchard EDMS 868314