## Slide 1: The triplet string test design What it can/cannot do
F.Micolon – 02/2019

## Slide 2: Introduction
The triplet string test was designed for two purpose :
To understand the issue encountered in the tunnel (without making “risky” test on the LHC hardware itself)
To study the consolidation solutions in order to mitigate the associated risks of implementation
The purpose of this presentation is to detail the main design features of the triplet string test before discussing the test program.

## Slide 3: Triplet string test setup
? What are the main contributors to the triplet longitudinal Stiffness
? Why did we see a drift in the longitudinal position (if any)
? Why do we see high load variation during realignment ?
? How can we consolidate the triplet so they can be realigned in the future
We make a string test to try to answer the following questions :
‘DFBX’ skeleton
End cover
Q1
Q2
Q3
WPS/DOMS structure
WPS structure
End cover

## Slide 4: The “DFBX” skeleton
Will act as a fixed point for the triplet string test.
 Same role as the DFBX in the tunnel
Designed so it can withstand the full 8T of vacuum force pushing on the vacuum end cover with limited deflection.

## Slide 5: Magnet realignment
The Q1 magnets will be equipped with the spare motorized adapters
In order to make vertical realignment on the other magnets, simplified manual realignment systems were designed and procured.
All magnet can be realigned with precision.
  Q1 with the motorized actuators
  Q2 and Q3 with the manual actuators

## Slide 6: In-situ Instrumentation Position
Measurement of magnet longitudinal position with 3x DOMS sensors (EN/SMM)
Measurement of magnet vertical/radial position
At each jack plane with the WPS system (14x sensors - 2x wires) – EN/SMM
+ punctual measurements using dial gauges
The DFBX skeleton deflection will be measured with DOMS

## Slide 7: In-situ Instrumentation Force
Measurement of the magnet load on each jack (EN/SMM)
Measurement of the longitudinal force transmitted by each tie-rod ear (12x)
Using strain gauges (EN/MME)

## Slide 8: In-situ Instrumentation Acquisition
All data (position, load) + a vacuum gauge shall be stored on Timber through an acquisition system currently being prepared by EN/SMM (Adriaan, Kevin).
This will be highly useful for future investigation

## Slide 9: A glimpse of B181 as of today
You are welcome to come and take a look anytime in building 181 !

## Slide 10
Conclusion
The triplet string test will allow a better understanding of the longitudinal load sharing in the triplets and overall triplet kinematic.
It is designed for vacuum only (no feeding of the cryogenic lines) with the idea in mind that vacuum is the main longitudinal force contributor.
This test requires multiple input from various specialist (Instrumentation, acquisition, survey, vacuum, transport).

## Slide 11
Spare slides

## Slide 12
The triplet string – simplified axial kinematics
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
When at cold, the cold mass will shrink
This stretches the interconnection bellows
 Which produces a pulling force on the cold mass
When we sum up all operational forces acting on each cold mass :
Vacuum force
80 kN
Q1 He pressure
22 kN*
Q3 He pressure
4 kN*
Bellow stretch
Q1Q2 – 22 kN*
Bellow stretch
Q2Q3 – 22 kN*
Bellow stretch
Q3DFBX – 10 kN*
* Force values corresponding to the operational conditions
Q1/Q2
Q1
Q2
Q3
DFXB
IP
Legend
Vacuum force
80 kN
Q1 net force = ~0 kN
Q2 net force ~0 kN
Q3 net force = -8kN
Vacuum force
80 kN**
Vacuum force
80 kN**