## Slide 1: Highlights from the 9th LHC Operations Evian Workshop (January 30th to February 1st, 2019)
C. Wiesner, M. Mentik, D. Wollmann
February, 28th 2019

## Slide 2
Five Sessions:
  Overview of Run 2
  Systems Overview
  Systems Overview (with some beam dynamics)
  Beam Performance during Run 2
  A Preliminary Look Ahead
33 Presentations accumulating to 11 hours
6 hours of discussions
Slides for all presentations (and proceedings/minutes) can be found at: https://indico.cern.ch/event/751857/timetable/#20190130.detailed
9th LHC Operations Evian Workshop
Personal, not complete, summary focusing on machine-protection relevant questions

## Slide 3: The LHC Beam Dump System
15 MKD: extraction kickers
MSD: extraction septa
TCDS: septa protection
MKB: dilution kickers
TCDQ: Q4 protection & TCSP
TDE: Beam dump
C. Bracco, LBDS Performance in Run II

## Slide 4: Run II Performance
Chart: # Failures
| 2010* | 2011 | 2012 | 2015 | 2016 | 2017 | 2018
MKD | 0 | 0 | 0 | 1 | 0 | 0 | 0
MKBH/V | 0 | 0 | 0 | 5 | 2 | 0 | 1
 | 3.5 | 3.5 | 4 | 6.5 | 6.5 | 6.5 | 6.5
MKD/MKB Erratic/Flashover with beam at top energy
LS1
31st May 2015
4th October 2016
From C. Bracco, LBDS Performance in Run II
A few kicker failures per year (erratics and flashover) occurred and will continue to occur, especially when operating at higher energy (higher voltage)
Weaknesses and new kicker failure types (type 2 MKD erratic, ~3 “missing” MKBs) were identified during past Runs  impact on beam load for dump protection elements and TDE

## Slide 5: LHC Dump Layout
beam
LHC vacuum
N2 dump sector
Upstream window (CfC + SS316L foil)
Downstream window (TiGr2 plate)
Dump core
beam

## Slide 6: Interferometer measurements
Large displacements measured

## Slide 7: Upstream Window under 1.8E+11 ppb
Chart: 
| HiLumi - 1.8E+11 p+/bunch - Normal Operation | HiLumi - 1.8E+11 p+/bunch - Failure Scenario 6V2H
Safety Factor Against Yielding | 2.28 | 1.09
Lower limit Below, the material deforms permanently
Necessary Margin Below, safe operation is not guaranteed
Energy per proton: 7TeV
Number of protons per bunch: 1.8E11
Emittance: 1.7µmrad
Bunch length: 25E-9s
Beam Pattern: HL-BCMS 6V2H with 2604 bunches
Material parameters and yield strength determination according to EDMS 2029814
LS-Dyna Version: 11.0, double precision
Too high risk of failure!
Ti Gr5 required
To be done
not before YETS 21/22
In collaboration with TE/VSC

## Slide 8: Rad-levels in RRs
Radiation levels in RRs in P1 & P5 dependency on TCL6 settings
Reduction of ~4x for IP1 & ~2x for IP5 in 2018 vs. 2017 but increase in P7 due to betatron losses.
The ARC rad-levels increased due to open TCL6 impacting MPE equipment in DS (increase in cell8).
From the R2E perspective: preferable post-LS2 configuration will be TCL6 closed, owing to radiation hardness of RR EPC equipment.
R2E failures 2017 vs. 2018
OP question: Replace more Power Converters affected by zero-volt crossing?
Power Converters

## Slide 9: QPS Hardware
Item | Count
EE13kA | 32
EE600 | 202
HDS | 6084
QDSRB | 1232
Magnet detector | 2464
QDSRQ | 392
Magnet detector | 1568
nQPS | 436
Magnet detector | 1632
Bus-bar detector | 4096
QDSIPX | 76
IP magnet detector | 360
IT magnet detector | 48
Current lead detector | 1124
QDS600 | 114
Magnet detector | 624
Rad-tol magnet det. | 212
Current lead detector | 1672
Total | 8568
Interlocking | 13800
13800 hardwired means to stop LHC
T. Podzorny, Quench Protection System

## Slide 10: QPS availability
Chart: 
| 2017 | 2018
QPS availability | 0.9874 | 0.9811
R2E faults | 0.0004788 | 0.0064449
General faults | 0.012121 | 0.012455
From T. Podzorny, Quench Protection System
Overall, excellent availability of QPS
TCL collimator settings in 2018 significantly affected QPS downtime
Comment Rende: “Before LS1 everybody was impressed about the number of faults now we are all impressed by the excellent availability”

## Slide 11
Protons
2012
2015
2016
2017
2018
Introduction
The multi-stage LHC collimation system aims to control the regular and abnormal losses to reduce the risk of quenches of the superconducting magnets.
Circulating
beam
Primary halo
Secondary halo
Tertiary halo
+ hadronic shower
Primary
Collimators
(TCP)
Secondary
Collimators
(TCSG)
Absorbers
(TCLA)
Tertiary
Collimators
(TCT)
Bottleneck
IP
Arc
Insertion
Thanks to D. Mirarchi
No magnet quenches from circulating proton beams with stored energy close to 300 MJ accommodating all machine configurations! Thanks to the good performance of the collimation system
and also to the very good beam lifetime and orbit stability!
N. Fuster-Martínez, Collimation
Collimation
Notes: No quenches from circulating beamNo quenches from circulating proton beam with stored energy close to 300 MJ!
What is limiting the intensity now?

## Slide 12: Collimation
Commissioning
From N. Fuster-Martínez, Collimation
Collimator Alignment
Circulating
beam
Primary halo
IP
Arc
Insertion
Secondary halo
+ hadronic shower & Dechanneling
Deflected halo
Massive Absorber
Bent crystal
Crystal Collimation

## Slide 13: Machine Protection System
For most cases we lost only 1 protection layer
We should become more rigorous and in the future for each such case produce a “major event report”

## Slide 14: Intensity ramp-ups Run 2
2015: commissioning year
    50 ns & 25 ns ramp-up
    Increase of intensity until end of proton run
2016/17/18: 7 steps to reach 2000+ bunches
    3/12 - 75 - 300 - 600 - 900 - 1200 – 1800
    2016  2018: reduction ramp-up length by 35 %
* 2015: 25 ns up to 1825 b
Establish cycle
MP dominated
Intensity dominated

## Slide 15: Machine Configuration
The Run 1
“Aperture Platinum Mine”
is depleted
R. Bruce

## Slide 16: Comparison: 2018 vs LHC design
Some keys to good peak performance:
  Small emittance
    See talks H. Bartosik, S. Papadopoulou
  Small β* at collision point
    Focus of this talk
Parameter | 2018 | LHC Design
Energy [TeV] | 6.5 | 7.0
No. of bunches | 2556 | 2808
Max. stored energy per beam (MJ) | 312 | 362
β* IR1/5 [cm] | 3025 | 55
Half crossing angle IR1/5 [µrad] | 160130 | 142.5
Normalized beam-beam separation | 10.67.9 | 9.4
p/bunch (typical value) [1011] | 1.1 | 1.15
Typical normalized emittance [μm] | ~1.9 | 3.75
Peak luminosity [1034 cm-2s-1] | 2.1 | 1.0

## Slide 17: Machine Configuration
R. Bruce

## Slide 18: Transverse Emittance Blow-up
Emittance growth studies well advanced as simulations and calculations can be compared to measurements. No measurement available for the ramp
Largest blow up during ramp
A potential
Lumi Gold Mine

## Slide 19: Special Losses (UFO – ULO – 16L2 – 10 Hz)
What about the deconditioning and level of UFOs in 2021 ?
10 Hz: origins of phase shift identified, but real cause not yet !!!

## Slide 20
2015
2017
2016
2018
S12
vented
25 ns physics fills with >600b
Heat loads in S12, S23, S81 much larger than for the other sectors
  close to cryo-plant design capacity
These differences are very reproducible and were observed in all 25 ns fills over 4 years (2015-18)
Heat loads: differences among sectors
G. Iadarola, Electron clouds and heat loads

## Slide 21
Heat loads: distribution along the ring
B1 alone B2 alone B1&B2
Sector 12 (MD 2018)
Q
Dipole
Dipole
Dipole
50 W
20 W
3 W
70 W
30 W
8 W
At 6.5 TeV:
At 450 GeV:
25 W
5 W
Cell 31L2 (equipped with extra thermometers)
Especially in the high load sectors, we observe large differences from cell to cell
Heat loads can be different for the two apertures of the same cell
Differences are present even among magnets of the same cell
G. Iadarola, Electron clouds and heat loads

## Slide 22: MDs per category [hours]
Collimation wins – lots of new hardware in prep for HL
Followed by collective instabilities, lumi and lifetime, …
2015, 2016, 2017, 2018
Comment Rende: “MDs are an excellent investment for (future) machine performance”

## Slide 23: What to expect from the injectors during Run 3
What will the LHC and Experiments be able to swallow during run 3 ?

## Slide 24
BCMS is preferred and if
necessary complement
with some 8b4e
Brian Petersen, Experiment Requests and Constraints for Run-3

## Slide 25: Deliverables & Equipment Group Constraints
Very clear forecast from LIU for the commissioning plan:
  Gradual intensity ramp up over Run-III.
At the LHC, can we inject, accelerate, collide and safely dump such a beam?
H. Bartosik, G. Rumolo, et al.
 | 2021 | 2022 | 2023* | Comment
# bunches | Up to 2748 (BCMS) |  |  | 
 | 1.3 | 1.3 | 1.3  1.55 | Intensity Ramp Up
 | 0 1.4 | 1.4 1.8 | 1.8  2.1 | Max intensity at the end of each year
 | 2021 | 2022 | 2023* | Comment
# bunches | Up to 2748 (BCMS) |  |  | 
 | 1.3 | 1.3 | 1.3  1.55 | Intensity Ramp Up
 | 0 1.4 | 1.4 1.8 | 1.8  2.1 | Max intensity at the end of each year
* Not including 2024 when the LHC is in shutdown but the injectors are fully operational.
M. Barnes, K. Brodzinski, B. Goddard, A. Lechner, J. Maestre Heredia, A. Mereghetti, D. Missiaen, F.X. Nuiri, B. Salvant, H. Timko, J. Uythoven, J. Wenninger, et al.
End of
2021
End of
2022
End of
2023
System | 1.7e11 | 1.8e11 | Comment
MKI | OK | OK | One new MKI prototype to be installed in 2022/2023 in IR8. should be within reach with 1.3ns  Studies are on-going for 1.2
RF | OK | OK | Klystron power limitation at INJ:  out of reach with Q22, ok for Q20 with >1.2ns in RAMP.
Alignment | NA | NA | Vertical realignment of LSS5 (Q10-Q10) by up to -3 mm
Cryogenics | OK | OK | Total heat load measured at 306W  at 7.0 TeV. Impact of running the triplet at the cryo limit is marginal (<2%) on the cooling capacity of the beam screen in the adjacent arcs.
System | 1.7e11 | 1.8e11 | Comment
MKI | OK | OK | 
RF | OK | OK | 
Alignment | NA | NA | Vertical realignment of LSS5 (Q10-Q10) by up to -3 mm
Cryogenics | OK | OK | 
N. Karastathis, Report from the LHC Run-III Configuration Working Group

## Slide 26: Deliverables & Equipment Group Constraints
Very clear forecast from LIU for the commissioning plan:
  Gradual intensity ramp up over Run-III.
At the LHC, can we inject, accelerate, collide and safely dump such a beam?
H. Bartosik, G. Rumolo, et al.
 | 2021 | 2022 | 2023* | Comment
# bunches | Up to 2748 (BCMS) |  |  | 
 | 1.3 | 1.3 | 1.3  1.55 | Intensity Ramp Up
 | 0 1.4 | 1.4 1.8 | 1.8  2.1 | Max intensity at the end of each year
 | 2021 | 2022 | 2023* | Comment
# bunches | Up to 2748 (BCMS) |  |  | 
 | 1.3 | 1.3 | 1.3  1.55 | Intensity Ramp Up
 | 0 1.4 | 1.4 1.8 | 1.8  2.1 | Max intensity at the end of each year
* Not including 2024 when the LHC is in shutdown but the injectors are fully operational.
The LHC should be available to accept a max bunch population
of
Especially, after the TDE downstream window upgrade.
M. Barnes, K. Brodzinski, B. Goddard, A. Lechner, J. Maestre Heredia, A. Mereghetti, D. Missiaen, F.X. Nuiri, B. Salvant, H. Timko, J. Uythoven, J. Wenninger, et al.
End of
2021
End of
2022
End of
2023
System | 1.7e11 | 1.8e11 | Comment
TCDQ | OK | OK | For 2.5mm gap and safety factor up to 2.5. Studies on-going for other gap values (2.0mm). TCDQ leveling MD successful!
TCDS | OK | ? | Already designed for , but in plastic deformation already  Studies on-going.
TDE | ? | ? | New downstream window installed in LS2. Not sufficient margin for the upstream window  YETS 2021/2022. Material re-characterization needed for the body at 2500οC . Study on-going.
Collimation | OK | OK | No issue on finding suitable settings for Run-III (with the help of partial upgrade in Run-III and thanks to dedicated telescopic optics).
System | 1.7e11 | 1.8e11 | Comment
TCDQ | OK | OK | 
TCDS | OK | ? | 
TDE | ? | ? | New downstream window installed in LS2. Not sufficient margin for the upstream window  YETS 2021/2022. Material re-characterization needed for the body at 2500οC . Study on-going.
Collimation | OK | OK | No issue on finding suitable settings for Run-III (with the help of partial upgrade in Run-III and thanks to dedicated telescopic optics).
N. Karastathis, Report from the LHC Run-III Configuration Working Group

## Slide 27
Thank you for your attention!

## Slide 28: Et bon appetit !

## Slide 30: Power Converters and their control
Massive FGClite deployment during LS2
Lessons learned and experience gained

## Slide 31: ADT and ObsBox
As well as normal operation, 15 MDs in the last 2 years relied on the ADT and ObsBox
ObsBox is instrumental for instability studies
“Any specific new requirements have to be communicated now”
Changes during LS2:

## Slide 32: Luminosity, lifetime and modelling

## Slide 33: Luminosity, lifetime and modelling

## Slide 34: Transverse Instabilities

## Slide 35: Longitudinal dynamics
Further improvement of quality and performance
Batches