## Slide 1: First results of UFO type 1 dynamics studies Measurements and initial observations
M Väänänen, B Lindström, D Wollmann
CERN
2nd TE-MPE-PE section meeting – 28 February 2019

## Slide 2: Beam-macroparticle interaction
Dust particle falls into beam
Intense Beam losses, duration ~1 ms
Premature beam dumps and superconducting magnet quenches
  -> up to 12 hours downtime!
beam
UFO
+
e-
e-
+
beam losses
beam loss monitor (BLM)

## Slide 3: UFO induced beam losses
Dust particle falls into beam
Intense beam losses, duration ~1 ms
Premature beam dumps and superconducting magnet quenches
  -> up to 12 hours downtime!
Courtesy of A. Lechner

## Slide 4: UFO impact on availability
LHC first proton accelerator to suffer from their impact
Still many unknowns, impact expected to increase in future (higher beam energy, higher beam intensity...)
Understanding their dynamics important clue for employing countermeasures
In 2017, new type of UFO at specific magnet interconnect
  different loss pattern
  67 premature beam dumps (out of ~350 total)
  significant impact on availability
  Also seen in 2018
A. Lechner

## Slide 5: UFO types
A. Lechner
~ 1 ms
second phase ~3 to 100’s ms
Type 1
Type 2
p+
solid nitrogen
nitrogen gas
beam
very fast beam instability develops

## Slide 6: UFO types
Type 1
Traditional type, present since high-intensity operations
Short loss spike (~1 ms)
Sporadic
Along the entire length of the LHC
Type 2
Present at specific magnet interconnect (16L2)
Hypothesis: caused by frozen nitrogen macroparticle
  Contamination of beam vacuum by air at 16L2 confirmed
Fastest observed beam instability in the LHC

## Slide 7: UFOs at end of run 2 proton physics
Special beam configuration during ~3 weeks of normal physics fills
  In non-colliding 12b train, two blown-up bunches: one horizontally, one vertically
Number of events during this time: 14
  Confirmed by existing UFO detection system: 7
3 at top energy, rest at 1096-4522 GeV

## Slide 8: Beam loss monitors
icBLM
  Good signal to noise ratio
  3600 distributed around ring
  40 µs temporal res
icBLM
dBLM
  Low signal to noise ratio, fluctuating signal
  2 per beam at primary collimators
1.5ns temporal resolution
~1 cm2

## Slide 9: icBLM vs dBLM correlation (30 Sep 2018)
icBLMs are a trusted system
dBLM signal integrated in 40 us bins correlates well with icBLM data

## Slide 10: Turn by turn, bunch by bunch losses (30 Sep 2018)
Elevated losses in horizontally blown-up bunch
High amplitude, long event
Best signal we had

## Slide 11: Bunch-by-bunch losses (30 Sep 2018)
Losses highest and longest-lasting in horizontally blown-up bunch

## Slide 12: Turn by turn, bunch by bunch losses (17 Oct 2018)
Elevated losses in vertically blown-up bunch
Losses in other bunches very low
At the limit of what we can observe

## Slide 13: Bunch-by-bunch losses (17 Oct 2018)
Longest event with increased losses from vertically blown-up bunch
Note: factor ~10 lower signal than in previous event

## Slide 14: Insight into UFO dynamics
Aim is to study UFO dynamics
We want to reconstruct dust particle trajectory
Losses proportional to proton density
Proton density proportional to distance from beam center
If we know bunch-by-bunch losses and proton distributions, we can derive location of UFO

## Slide 15: Possible locations in both planes
Location based on losses from horizontally blown-up bunch
Location based on losses from vertically blown-up bunch

## Slide 16: Possible locations in both planes
Intersections are possible UFO locations

## Slide 17: Applying the method to measurements
Correlating BLM signal to number of protons lost difficult
A single lost proton should still always give the same signal
Thus, correlate ratio between loss signals of blown-up and nominal bunches to proton distributions of blown-up and nominal bunches
Still some challenges remain:
  Signals not clean, low signal-to-noise ratio, erratic loss spikes

## Slide 18: Ratio of proton densities between bunches
The ratio of losses between normal and blown-up bunches are measured
This is correlated to the ratio of the proton distributions, assuming they are Gaussian
-> allows deriving the UFO location within the beam, despite not knowing the absolute loss values from each bunch

## Slide 19: Trajectory reconstruction (30 Sep 2018)
Turn 8
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 20: Trajectory reconstruction (30 Sep 2018)
Turn 9
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 21: Trajectory reconstruction (30 Sep 2018)
Turn 10
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 22: Trajectory reconstruction (30 Sep 2018)
Turn 11
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 23: Trajectory reconstruction (30 Sep 2018)
Turn 12
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 24: Trajectory reconstruction (30 Sep 2018)
Turn 13
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 25: Trajectory reconstruction (30 Sep 2018)
Turn 14
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 26: Trajectory reconstruction (30 Sep 2018)
Turn 15
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 27: Trajectory reconstruction (17 Oct 2018)
Turn 19
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 28: Trajectory reconstruction (17 Oct 2018)
Turn 20
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 29: Trajectory reconstruction (17 Oct 2018)
Turn 21
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 30: Trajectory reconstruction (17 Oct 2018)
Turn 22
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 31: Trajectory reconstruction (17 Oct 2018)
Turn 23
Blown up proton distributions divided by nominal bunch distributions
Reference bunch proton distribution with estimated UFO location
Note: just one possible
trajectory within error bars!

## Slide 32: Outlook
Comprehensive parameter scan with simulation model
  Compare with measurements
Error quantification
Look into the full beam
  Eg. PACMAN bunches with orbit offset

## Slide 33: Conclusions
UFOs have an important effect on LHC
  Studied with bunch-by-bunch resolution and blown-up bunches
  14 events recorded with blown-up bunches
With bunch-by-bunch losses and knowing proton distributions and bunch sizes, we can reconstruct UFO trajectories
Large error bars from fluctuating signals, background losses, uncertainties in proton distributions
Nevertheless: observed one event with interaction mainly in the horizontal plane and one with mainly in the vertical plane
  Analysis ongoing
Gravity alone is not enough to explain the observations
  Dust particle can likely be negatively charged and attracted to the beam

## Slide 34: Thank you!

## Slide 35: Backup slide 1: UFO rate in 2018

## Slide 36: Backup slide 2: Bunch intensities

## Slide 37: Backup slide 3: Possible trajectories
Physical model of beam-macroparticle interaction to study UFOs
  Partially validated against UFO type 1 events (temporal loss pattern, # inelastic collisions; assuming ~20-30 µm particles, Cu, C)
Comparing measured # of inelastic collisions with simulated:
  Estimate of macroparticle size -> radius 15-30 µm (nitrogen, density 1.029 g/cm^3)
B. Auchmann

## Slide 38: TITLE AND TWO CONTENT WITH SUBTITLES

## Slide 39: TITLE