## Slide 2: From LHC statistics to AvailSim modelling
M.Vekaria, A.Apollonio, T.Cartier-Michaud
6/06/2019

## Slide 3: Introduction
Data sources
Introduction to LHC Operations
  Fault statistics in BModes
Injection Investigation
  Physics and Probe
AvailSim inputs

## Slide 4: LHC Cardiogram

## Slide 5: Availsim
Monte-Carlo simulation tool
  Simulate the operation of accelerators eg. LHC
Inputs based on observed performance
  Works using different reliability measures (Mean Time To Repair, Mean Time To Fail) from faults
  These change depending on the beam mode they occur in.
Also requires Beam Mode durations as an input

## Slide 6: LHC Operation Breakdown
LHC Operations
OPERATIONAL MODES
No Beam
Setup
Beam In
Stable Beams
Pre-Cycle
BEAM MODES
No Beam
Cycle
Setup
Injection Probe
Injection Physics
Ramp
Pre - Ramp
Adjust
Squeeze
Stable Beams
Aim is to calculate Beam Mode durations and calculate failure rates and repair times based on beam mode
E-Logbook

## Slide 7: Data Sources
Timber
  Fill number timings
  Beam modes
  Beam Intensity
AFT
  Fault data
Post Mortem
  Injection scheme

## Slide 8: Injection Statistics
Tasked with looking into Injection inefficiencies.
  Looked at “injection physics” and “injection probe” for year 17-18 for AvailSim
  One of the least reproducible modes in LHC operation
    Why isn’t theoretical minima (28mins) reached?
      42*20*2/60 = 28
      Variety of discrepancies between injections that cannot be explained by faults
  Failures should be expected to correlate to beam intensity
    Looked at 25ns spaced 2556b

## Slide 9
Cut-off for successful Injections
Cut-off for successful Injections

## Slide 10: Why Categorise?
When looking through E-Logbook, these
are the most common
What is “no explanation”?
  There is no clear explanation in the logbook
All of this takes into account registered blocking faults, unregistered are noted as “minor hardware error” e.g.. Faulty QPS circuit board
(╯°□°）╯︵ ┻━┻

## Slide 11: Some examples
Upstream
No explanation
Losses
Hardware
Intervention

## Slide 12
16L2
Cleaning
Steering
Tuning
Correction
(injector complex faults or issues)
UFO, ADT Blowups
Arrows are hyperlinks to E-Logbook

## Slide 13
Cut-off for successful Injections
Cut-off for successful Injections

## Slide 14
Cleaning
Steering
Tuning
Correction
(injector complex faults or issues)
UFO, ADT Blowups
LINAC2 missed shots

## Slide 15
Cut-off for successful Injections
Notes: Same binning across all graphs

## Slide 16
mins
Correction
Calibrations
SPS
LINAC 2
PSB
PS
Chroma correction
Hyperlinked arrows again

## Slide 17
Cut-off for successful Injections
mins

## Slide 18
mins
Correction
Calibrations
CPS
SPS
LINAC 2
PSB
PS
No explanation
Hyperlinked arrows again
mins

## Slide 19: Review
There’s a lot of “no explanation”
  This isn’t necessarily a bad thing!
  This introduced a new task that would follow up from this (recommended by Bartosik and Rumolo), which is the first 12 bunch train.
  Expect largest variance because of the required synchronisations and corrections between injectors and LHC
Could not apply filter to such a large dataset, but 12b injection should be consistent across beam parameters.

## Slide 20
to log10
This doesn’t show the variance we expected to see, next steps would be to plot the variance of the whole of the injection process
More analysis to come

## Slide 21: AvailSim
Fault and beam mode statistics calculated and output into the ‘common input format’.
System Fault
Beam Mode B
Beam Mode A
Beam mode B experiences 2 faults, while A experiences 0.
MTTF given by Mode duration, ergo: MTTF in A ≡ ∑A/0 = inf
MTTF in B ≡ ∑B/2 = val
Beam Mode B
Beam Mode A
MTTR
Notes: Include sc of common input

## Slide 22: Process
Attribute beam mode and Index location of beam mode using data from AFT and Timber
Beam Mode
Index
Mode durations must discount fault time for MTTF
Output
AFT
Timber (LDB)
Notes: Animate the bits

## Slide 23: Moving Statistics
QPS CRISIS
16L2

## Slide 26: AWG Review

## Slide 27: Results

## Slide 28: Conclusion
Continued work on data for AvailSim
  Currently refining both Fault and Beam Mode statistics
  Ideally matching AWG reports
  Extend to other Accelerators (statistics started)
  Predictive tool for unknown scenarios (HiLumi)
  GAN Network as a pose to regular Neural Network
  Translate for SWAN package?
Goal - Complete model of CERN accelerator complex

## Slide 29: ┬┴┬┴┤ ͜ʖ ͡°) ├┬┴┬┴
♪~ ᕕ( ͡° ͜ʖ ͡°) ᕗ

## Slide 30: Extra Slides

## Slide 31: Injections reaching stable beams
How are any of these bars possible?
No other data, but we can hypothesise ¯\_(ツ)_/¯

## Slide 32: Failure distributions