## Slide 1: Fast Failures in the High Luminosity LHC
Björn Lindström
CERN and Uppsala University
With input from:
L. Bortot, M. Valette, C. Wiesner, R. Schmidt, A. Verweij,
E. Ravaioli, M. Mentink, P. Bélanger, M. Väänänen
4th April 2019

## Slide 2: Outline
Project definition and motivation
Failures
CLIQ
Beam Beam Kick
Triplet Quench

## Slide 3
1.52 MJ deposited energy
Beam induced damage
Courtesy of F. Burkart

## Slide 4: SPS vacuum leak
2 MJ lost in 15 ms
LHC is cryogenic: SPS downtime ~3 days – LHC downtime ~3 months
K. Li – 168th MPP meeting

## Slide 5: Scope of project
Study of failure scenarios causing uncontrolled beam losses
  Source of failures
  Effect on the beam
  Subsequent beam losses (intensity, location)
  Time scales
Detection of failures
  How to limit time between detection of failure and beam dump → time sufficient before critical losses occur?
Identify new failures, e.g. due to new equipment
Goal: Understand criticality of failures to determine protection strategy / how to design safer system
(current machine protection system sufficient? new interlocks required? other mitigation strategies?)

## Slide 6: High Luminosity LHC (HL-LHC) changes
To attain higher luminosity, higher bunch intensity and smaller beam size in collision point
New layout and new HW (crab cavities, triplets, 11T dipoles)
 | LHC (6.5 TeV) | HL-LHC
# bunches | 2556 | 2748
Protons per bunch | 1.15e11 | 2.2e11
Beam size collision [µm] | 95 | 60
Stored Beam energy [MJ] | 306 | 678
Peak luminosity cm^-2 s^-1 | 2.2 * 10^34 | 17 * 10^34
Increased stored beam energy important parameter, but also the smaller beam size in collision point!

## Slide 7: Beta function
Beam size related to emittance and beta function
emittance, statistical measure of the deviation of the position and momentum of all particles in a bunch from its average
  initially determined by particle source, then it grows
beta function is determined by the optics lattice (focusing + defocusing quadrupoles)
  when beam is focused, size decreases but transverse momentum increases
  emittance is (quasi-)constant, beam size modulated by beta function
Beta function determines sensitivity to perturbations:

## Slide 8: Beta function
: is beta function in IP
Small → large beta function in Triplets, implying large effects on beam due to errors

## Slide 9: Methodology
Observe an event in LHC
  Understand the failure
  Simulate in HL-LHC optics to determine future criticality
  Verify with experiments
New Hardware
  Study how it can malfunction and what would happen to the beam
  Simulate and determine criticality
  Verify with dedicated experiments when possible
→Determine mitigation and interlock strategies

## Slide 10: Outline
Project definition and motivation
Failures
CLIQ
Beam Beam Kick
Triplet Quench

## Slide 11: Overview of Fast Failures
Magnets/Circuits
Active Equipment
Others
Triplet Quench
D1, D2 power loss
Quench Heaters
CLIQ
ADT
Crab Cavities
Beam-Beam Wire Compensator
UFO
UFO type 2
Beam-beam Kick

## Slide 12: Overview of Fast Failures
aa
Failure in/due to: |  | Time to critical losses
Triplet Quench | Quench in final focusing magnets | > 50 LHC turns (4.5 ms)
D1,D2 | Power Failure in the dipoles next to the collision points | > 10 LHC turns (0.9 ms)
QH | Quench protection for magnets | > 1 LHC turn (0.1 ms)
CLIQ | Quench protection for magnets | ~1 LHC turn (0.1 ms)
ADT | Transverse beam damper | > 10 LHC turns (0.9 ms)
Crab Cavities | Required for counteracting loss in luminosity due to Xing angle | > 10 LHC turns (0.9 ms)
BBCW | Long Range Beam-Beam compensating wires | > 100 LHC turns (9 ms)
UFO | Dust-particles interacting with beam | ~3 LHC turns (0.3 ms)
UFO type 2 | Beam instability driven by remaining gas cloud after UFO interaction | > 10 LHC turns
Beam-beam kick | Loss of beam-beam kick due to dumping only one beam | ~2 LHC turns (0.2 ms)

## Slide 13: Failures covered below
aa
Failure in/due to: |  | Time to critical losses
Triplet Quench | Quench in final focusing magnets | > 50 LHC turns (4.5 ms)
D1,D2 | Power Failure in the dipoles next to the collision points | > 10 LHC turns (0.9 ms)
QH | Quench protection for magnets | > 1 LHC turn (0.1 ms)
CLIQ | Quench protection for magnets | ~1 LHC turn (0.1 ms)
ADT | Transverse beam damper | > 10 LHC turns (0.9 ms)
Crab Cavities | Required for counteracting loss in luminosity due to Xing angle | > 10 LHC turns (0.9 ms)
BBCW | Long Range Beam-Beam compensating wires | > 100 LHC turns (9 ms)
UFO | Dust-particles interacting with beam | ~3 LHC turns (0.3 ms)
UFO type 2 | Beam instability driven by remaining gas cloud after UFO interaction | > 10 LHC turns
Beam-beam kick | Loss of beam-beam kick due to dumping only one beam | ~2 LHC turns (0.2 ms)

## Slide 14: Outline
Project definition and motivation
Failures
CLIQ
Beam Beam Kick
Triplet Quench

## Slide 15: Magnet protection
High current in magnets (up to ~16 kA)
Quench – loss of superconductivity
Risk of cable damage
Need active system to protect magnet
Active system changes current – magnetic field in beam region
In LHC, magnet protection did not consider effects on beam

## Slide 16: Coupling Loss Induced Quench (CLIQ)
Up to 2.5 kA discharged directly into magnet coil!
Q1 electrically same as Q3, but Q2 different
Q2: Symmetric discharge (opposite poles, same current change)
Q1/Q3: Asymmetric discharge (one pole increased current, three poles decreased)
Need circuit and beam simulations
I_nominal
I_CLIQ

## Slide 17: CLIQ – spurious discharge of single unit
Three magnets – two different connection schemes
Dipolar field → beam kick
Octupolar field → beam size
Beams 1 & 2
Beams 1 & 2
Courtesy of E. Ravaioli

## Slide 18: Spurious discharge – Beam orbit change
Beam loss threshold
Physical aperture (TCPs)
Time to dump beams: min 10 turns
Magnet protection design must take effects on beam into account!

## Slide 19
Solution?
19
Ensuring CLIQ can never fire spuriously
  Cannot be 100 % failsafe, expensive, and increased complexity
Use Q2-like connection scheme
  New triplet circuit baseline
Courtesy of E. Ravaioli

## Slide 20: Q2-like connection – beam orbit change
Beam loss threshold
17 turns until threshold
Can safely dump within 10 turns
Little margin – still critical

## Slide 21: Outline
Project definition and motivation
Failures
CLIQ
Beam Beam Kick
Triplet Quench

## Slide 22: Beam beam kick
The two beams are charged and, thus, interact around collision points
  Transverse kick (orbit change, main issue for Machine Protection)
  Beam size growth
  Tune spread
  ...
.
+++++++
+++++++
Repulsive force
Collision point

## Slide 23: Beam beam kick
The two beams are charged and, thus, interact around collision points
  Transverse kick (orbit change, main issue for Machine Protection)
  Beam size growth
Beams cannot be dumped simultaneously:
.
Remaining beam is distorted due to loss of BBK!

## Slide 24: Dump animation
The order in which the BBK is lost in different IPs matter
.

## Slide 25: Measured BBKs
Since Aug 1 2017:
  b1: 27 observations
  b2: 21 observations
  Up to 3 turns of offset measured in both beams
  Dump reasons: RF trips, EOF programmed dumps, collimator temperature, SIS interlock, BPMS interlock
Beams have separate beam permits, and some systems only remove permit of one beam. Even when both permits removed, there are delays in the communication and beam synchronization.
fill 7217

## Slide 26: Comparison with simulations
BBK proportional to bunch intensity → normalize the measurements
Dark blue line: average of all measurements
Light blue shade: standard deviation of measurement
  all fills very consistent!
Red line: estimate from simulations
  good agreement!

## Slide 27: Run III and HL-LHC projections
Bunch intensity increase significantly
Small beta star in HL, but increased crossing angle
In Run III worst case, kick is significant but within threshold
In HL-LHC, kick is above limit on second turn
Flat optics would be better from this perspective, but is not baseline
In HL-LHC, both beams should be dumped with minimum delay (one turn is unavoidable)
orbit excursion [σ]

## Slide 28: Outline
Project definition and motivation
Failures
CLIQ
Beam Beam Kick
Triplet Quench

## Slide 29: Triplet Quench observed 2018-06-03
Vertical orbit offset only in b1
~180 µm change in center of MQXA.1R1 (Q1)
~180 µm

## Slide 30: ”Slow” kick – Closed orbit change
The kick was fitted to all BPM measurements
Black dots are BPMs
Two BPMs in IP5 consistently lower value, otherwise good fit

## Slide 31: Origin of kick
Plotting two consecutive turns around IP1 shows discontinuity at Triplet location
Together with RQTX.R1 circuit data, confirm kick originates in MQXA.1R1

## Slide 32: Kick time evolution
Due to cryo issue, quench propagation speed was abnormally fast
From circuit simulations, magnetic field expected to be ~0.23 mT at dump, but beam kick implies 0.7 mT
Emmanuele showed discrepancy possibly due to current redistribution in the wire
In HL-LHC, due to larger beta functions, critical limit could be reached in ~50 LHC turns
Quenches by themselves can have significant impacts on the beam but not critical due to long time-scales

## Slide 33: Conclusions and Outlook
Criticality of failures in Magnets/Circuits, Active Elements, and other scenarios has been determined
CLIQ would create the fastest failure in the LHC – mitigation method has been proposed and implemented
Simulations validated by dedicated experiments / beam observations
Proposed & validated novel method for studying UFOs – strong indication UFO movement also horizontal
First Machine Protection experiments with Crab Cavities in a hadron beam were prepared, executed and analysed – observations confirm expectations, fast interlocks are required
UFO dynamics studies ongoing (with Philippe)
Wrap-up failure studies
  PRAB paper summarizing most failures nearly ready for submission
  UFO paper together with Philippe in preparation

## Slide 34: Run III and HL-LHC optics

## Slide 35: Beam sensitivity to perturbations
Constant area:

## Slide 36: Beam sensitivity to perturbations
Ellipse at location with smaller beta function, area is the same

## Slide 37: Beam sensitivity to perturbations
A particle receives a kick

## Slide 38: Beam sensitivity to perturbations
Particle traces out ellipse in phase space

## Slide 39: Beam sensitivity to perturbations
Particle at other location traces out different ellipse

## Slide 40: Beam sensitivity to perturbations
Observe Red particle at Blue location, transforms the ellipse
Amplitude of particle kicked at Red location smaller than particle kicked at Blue location. This is because of the beta function