## Slide 1: Introduction to OPC-UA Ben Farnham (BE-ICS)

## Slide 2: Agenda
1. OPC-UA overview
2. How OPC-UA is used at CERN
3. Building an OPC-UA server
4. Current collaborations

## Slide 3: 1. OPC-UA overview
Industrial standard
  Communication protocol for industrial communications.
  IEC 62541
  opcfoundation.org
Widely adopted in many industrial sectors.
Client-Server model.
  Any OPC-UA client can read/write information to/from any OPC-UA compliant server.
Many products have OPC-UA clients built-in.
  Many devices come with OPC-UA servers.
OPC-UA client
OPC-UA server
Generic
Device

## Slide 4: 2. How OPC-UA is used at CERN
Supervision
(SCADA)
Process
Management
(middleware)
Field
Experimental equipment (power supplies)
LAN
OPC-UA
Fieldbus
protocols
IP
protocols
SCADA Layer
  Unified view of (sub)-detector
  Highly integrated control systems
  WinCCOA SCADA
Process Management Layer
  OPC-UA servers
  One per device-type generally
  Middleware: communications between SCADA and field devices.
Field Layer
  (Your) hardware
  Communicates with dedicated OPC-UA server
    IP network.
    Fieldbus (e.g. CANbus).
OPC-UA servers

## Slide 5: 3. Building an OPC-UA Server
Base requirement (vendor provides)
  Hardware Access Library (+API).
  Windows (WS2016) + Linux (Centos7).
Generic
Device
Firmware
Hardware Access Library
Clear API
OPC-UA server generation framework
  Quasar (OS: see github.com/quasar-team).
  Collaboration (shared source code).
  Model -> code generation.
And hence connection to all OPC-UA clients (WinCCOA, LabView, etc.)
OPC-UA server (based on quasar framework).
A collaboration.
OPC-UA clients

## Slide 6: 4. Current collaborations
CAEN & ISEG
  Collaboration agreements signed (with CERN’s Knowledge Transfer group).
  Collaborative development work.
    Test and optimize hardware access library in large scale deployments.
    Build OPC-UA server on top of library.
  OPC-UA servers running in 2018 in production environments.
  Mass roll-out during 2019.
Wiener
  Collaboration agreements signed.
  Very active collaborative development ongoing.
  Mass rollout foreseen for 2019.

## Slide 7: End. Thank you.