## Slide 1
Stefano Corradetti
National Institute for Nuclear Physics– National Laboratories of Legnaro (Italy)
stefano.corradetti@lnl.infn.it

## Slide 2: ISOLPHARM Project
Main objective of the ISOLPHARM project:
Production of carrier-free radionuclides
Production of non conventional radioisotopes (difficult to produce with traditional techniques)
Same target, different radionuclides (flexibility)

## Slide 3: Overview
⚛ The SPES project at LNL
⚛ The ISOLPHARM Project: SPES radionuclides for medicine
⚛ ISOLPHARM experimental activities
⚛ ISOLPHARM_Ag: a case study
⚛ Conclusions

## Slide 4: The SPES project at LNL-INFN
SPES is: 1) A second generation ISOL facility (for neutron-rich ion beams)
2) An interdisciplinary research center (for p,n applications)

## Slide 5: The New SPES/ISOLPHARM Infrastructure
Project financied by INFN
New infrastructure for:
Application Facility
Cyclotron
RIB facility (2th generation ISOL)
New Building:
Bunker layout
Laboratory layout

## Slide 6: The New SPES/ISOLPHARM Infrastructure
Production bunker
Experimental halls
Control room
Cyclotron
Resonant Ionization
Laser Ion Source

## Slide 7: RIBs facilities in the word
The ISOL method is a technique to produce Radioactive Ion Beam for Nuclear Physics, Nuclear Astrophysics, Physics of Solid State and Nuclear Medicine
ISOLDE @ CERN
SPES @ LNL
ISAC @ TRIUMf
Main RIB facilities :
ISOLDE (CERN)
ISAC (TRIUMF)
RIKEN
SPIRAL1 (GANIL)
FAIR now under construction: (GSI)
SPES now under construction: (LNL)
SPIRAL2 now under construction: (GANIL)
FRIB now under construction: (MSU)
SPIRAL2
FRIB
FAIR
RIKEN

## Slide 8
The ISOLPHARM method
The ISOLPHARM method is capable of selecting and isolating a
SINGLE RADIO-ISOTOPE
Borgna et al, Appl. Radiat. Isot., 2017, 127: 214–226
Borgna et al, Molecules., 2018, 23, 2437
Step 1
Secondary target development and ions recovery
Step 2
Chemical Purification Processes
Development
Step 3
(Radio)pharmaceutical development

## Slide 9: RIB Source

## Slide 10: Radionuclides that will be produced at LNL-INFN
Instrinsecally carrier-free radionuclides can be produced
With the same target numerous radionuclides can be produced only by changing the mass separator settings
Designing specific targets a wide range of radionuclides can be prodcued, including radionuclides which can be hardly produced with the traditional techniques
Production yields are lower than those of cyclotrons and nuclear reactors

## Slide 11
ISOLPHARM
Experimental activities

## Slide 12: Experimental activities: The proton driver
At SPES the chosen primary driver is the 70p commercial cyclotron manufactured by the BEST Cyclotron Systems Inc., a member of TeamBest™. Such machine is able to deliver up to two simultaneous energetic proton beams (maximum energy 70 MeV – 49 kW) with a maximum overall intensity of 700 μA .

## Slide 13: Experimental activities: Production targets development
UCx target already developed and tested on-line
One material, many radioactive ion beams (fission)
Neutron-rich nuclides
UCx target
UCx

## Slide 14
In target production

## Slide 15: Experimental Activities: Secondary Target
Sodium Chloride
Activated Carbon
Used for I2
Sodium Nitrate
Used for Ag
Used for Sr, Y and Cu
Powder compression
AC/PVA blend 50% w/w
Granulation process
Drying and sieving (<300 mm)
Powder compression
Secondary target requirements
Chemical compatibility with the element
Absence of metal contaminants
No incompatibilities with the production of a radiopharmaceutical for human administration
No intereference with purification processes

## Slide 16: Experimental Activities: Stable ion beams production and recovery
Iodine deposition
AC/PVA disk
Sr, Y and Cu deposition
Sodium Chloride disk
Sr
Y
Cu
Silver deposition
ICP-OES
Analysis
GF-AAS
GF-AAS
GF-AAS
Titration
Current research activities:
Terbium ionization and deposition

## Slide 17: ISOLPHARM Production
Cyclotron
Front-End
Experimental halls
Proton beam
Radioactive beam

## Slide 18
ISOLPHARM_Ag:
A case study

## Slide 19: ISOLPHARM_Ag
The ISOLPHARM_Ag collaboration project is aimed to evaluate the feasibility of the production of a 111Ag-based radiopharmaceutical according to the ISOLHARM method.
β- emitter (average energy 360 keV)
Medium half-life (7.45 days)
Medium tissue penetration (1.8 mm)
Low energy γ rays (245 (1.24%) and 342 (6.7%) keV – SPECT
111Ag

## Slide 20: Traditional production Routes for 111Ag
Neutron irradiation of Palladium target
production of carrier-free 111Ag is not possible except the case in which enriched 110Pd is used as a target:
Sideproduct during 225Ac production by proton induced spallation reactions on thorium targets
Expensive target cost
Low yield (1 GBq/mg)
Associated γ radiation (1 week to short lived co-produced activities decay)
110Pd (n, γ) 111Pd (β─) 111Ag

## Slide 21: Production Routes for 111Ag: ISOLPHARM Method
111Ag can be produced not only at high purity, but also with high production rate: up to 2 Ci in target after 5 days (SPES UCx target)
All the isotopic contaminants with a different mass number will be removed thanks to the on-line mass separation.
Only 111Ag and low amounts of its stable daughter 111Cd, mostly produced by the decay of silver, will be collected on the secondary target.
Isotopes | t½ | Decay | Stable isotope
111Cd | Stable |  | 111Cd
111Ag | 7.45 days | β─ | 111Cd
111Pd | 23.4 min | β─ | 111Ag → 111Cd
111In | 2.8 days | Electron capture | 111In → 111Cd

## Slide 22: ISOLPHARM_Ag
μ
TASK1 (Physics/Computing)
Simulations of production, release and transport of 111Ag produced with the SPES target using the Monte Carlo codes.
TASK2 (Chemistry/Ag production):
Study of silver production (ionization and acceleration) & purification from 111Cd2+ using stable isotopes.
Development of possible chelators for silver. Characterization of complexes produced.
Task 3 (Molecular Biology):
Development of targeting agent for Cholecistochine (small molecule-based ligands and linker moiety) and development of targeting agent for calreticulin as potential target for proton therapy combined with targeted radionuclide therapy

## Slide 23: Ionization and deposition of stable Ag+
Ionization and acceleration of stable Ag+ using the SPES Front End in off-line modality.
natAg (51.84/48.16)
107
109
Ionization efficiency:
15 %

## Slide 24: Ag+ deposition tests
Deposition tests were performed collecting the silver ions in a proper secondary target made of sodium nitrate.

## Slide 25: Development of novel bifunctional chelators for Ag(I)
DOTETE
Chiral derivatives
DOTETE Derivatives
Development of a library of potential bifunctional chelators for 111Ag
DOTETE
Derivative1
Ag(I)-BFCs complexes studies:
Thermodynamic
characterization

## Slide 26
Development of novel bifunctional chelators for Ag(I)
NMR measurements:
1H, 13C
NOESY, COESY, HMQC
Derivative1
X-ray
DFT calculations

## Slide 27
New ligands for activate targeting of CCK2R
Due to the lipophilic nature of the targeting agent Z-360, appropriate spacers were chosen and synthesized in order to enhance the solubility of ligands and improve their biodistribution.
Radiolabeling of new synthesized ligands with 68Ga
Stability in PBS buffer solution and blood over time
IP1_1 hour in blood
IP2_1 hour in blood
Targeting agents development
CCK2R

## Slide 28
Realization of a suitable 3D scaffold for in vitro tissue mimiking
Evaluation of the translocation of CRT in cell membrane after radiation exposure (immunofluorescence)
Targeting agents development
CALRETICULIN (CRT)

## Slide 29: Conclusion
At SPES it will be possible soon to produce radionuclides for medical purposes using the ISOL technique.
The ISOLPHARM method is focused on the production of radiopharmaceutical precursors with high specific activity using a proton beam ad intermediate energies.
The ISOLPHARM collaboration has started 4 years ago. An increasing experimental activity is under development.
Some radionuclides (as 111Ag , 43Sc, etc) are extremely interesting and could be used as precursors for new radiopharmaceuticals.

## Slide 30
THANK YOU
ISOLPHARM
People