Piotr P. Nikiel
The SoC workshop at CERN
OPC-UA, quasar and SoCs
14-Jun-2019

---
Part 1
Making a simple OPC-UA server
on a laptop
to play with

---
Making a simple OPC-UA server (1)
- Plan:
  - Make an empty quasar-based server,
  - Build, run; connect with an OPC-UA client
  - Design some simple monitoring and control: switch, LED, analog sensor monitoring (with fake data)

---
Making a simple OPC-UA server (2)
Make an empty quasar-based server
- Create the empty server:
  - cd $QUASAR
  - ./quasar.py create_project ~/gitProjects/SoC_Workshop_Quasar
  - cd ~/gitProjects/SoC_Workshop_Quasar
  - ./quasar.py set_build_config $QUASAR/open62541_config.cmake
  - ./quasar.py enable_module open62541-compat v1.1.2
  - git init .
  - git add *
  - git commit -a -m “Initial version”
- Build and run it:
  - ./quasar.py build
  - cd build/bin
  - ./OpcUaServer
- Connect using UaExpert

---
Making a simple OPC-UA server (3)
Look around
- We recommend Eclipse CDT
  - … because we will need its XML tools etc.
- Integrate a quasar project into Eclipse:
  - create an empty C++ project from the project path
- Relevant files for a developer:
  - Design/Design.xml
    Entry-point to modeling!
  - Server/src/QuasarServer.cpp
    Server init/ shutdown and “main loop”
  - Device/src for Device logic classes
    will add them later

---
Making a simple OPC-UA server (4)
Enter design!
- Open Design in Eclipse
  - Eclipse is pretty good for schema-based XML editing
- Design can be easily visualized
  - ./quasar.py generate diagram 3
    (number is the detail level)
- General principle:
  - classes represent types of control system objects
  - variables are to exchange information
    (writing, reading, monitoring)
  - variables belong to classes
  - classes can be nested in tree-like hierarchies

---
Making a simple OPC-UA server (5)
Let’s add a simple class...
- Adding a Switch quasar class
  - for hardware guys: we will use it to monitor real switches – via digital inputs – on the board
- Add a quasar cache-variable state
  - it will follow the switch state in runtime
- Since one class will cover many objects,
  I will add a switch identifier on the board
  - using quasar config-entry
- Refresh the design visualization
- Rebuild …
- Add objects in the config file …
- Rerun ...

---
Making a simple OPC-UA server (6)
… let’s exchange information ...
- In quasar servers, the integration with developer’s code usually goes to Device Logic
  - there are other ways too ...
- Our design:
  - add Device Logic to Switch class
- Generate device class
  - ./quasar.py generate device Switch
  - and build the server… (because we changed the Design)
- Let’s have a good look at the Device class ...
- Let’s add a method update that will poll the switch state and publish it via OPC-UA
  - … for the moment with fake (i.e. random) data:
    bool state = rand() & 1;
    getAddressSpaceLink()->setState(state, OpcUa_Good);

---
Making a simple OPC-UA server (7)
… let’s exchange information ...
- The update method might be called from the server’s main loop for simplicity:
  for (Device::DSwitch* sw : Device::DRoot::getInstance()→switchs())
  sw→update();
- Build, run the server and see in UaExpert
- To polish up:
  ./quasar.py check_consistency --ask
- Commit & tag, e.g. as v1
  git commit -a -m ‘Fake readout of the switch’
  git tag -a v1

---
Making a simple OPC-UA server (8)
… note ...
- The build & deployment strategy you just saw is
  appropriate for:
  - desktops and servers (Windows and Linux)
  - cross-compilers distributed as SDKs (with rootfs/sysroot)
    - quasar can be told to use a chosen cross-compiler
  - embedded systems with native compilation
- For Yocto/PetaLinux:
  - software design & development procedure is identical
  - building is different – quasar server integrates as Yocto recipe/PetaLinux app

---
Questions?
( … so far …)
… and 1-minute break ...

---
Part 2
Towards the demo
PetaLinux + quasar
On
Zybo Z7-20 development board

---
PetaLinux + quasar (1)
Plan
- Build our earlier project in PetaLinux
  (still with fake data)
- Deploy on real hardware, connect, etc…
- Integrate real I/O

---
PetaLinux + quasar (2):
Reference versions and settings
- PetaLinux 2017.4
- Zybo Z7-20 BSP: v2017.4-3
- quasar: v1.3.4
- open62541-compat: v1.1.2 (!)
- Host OS:
  CentOS Linux release 7.6.1810 (Core)
- source /opt/pkg/petalinux/settings.sh
- export QUASAR=~/gitProjects/quasar
- alias zybo_package='petalinux-package --boot --fpga images/linux/system_wrapper.bit --u-boot --force'

---
PetaLinux + quasar (3):
PetaLinux step-by-step
- In our quasar project dir:
  - Deploy CMake Epilogue (will tell PetaLinux what are server deliverables):
    cp -v $QUASAR/Extra/yocto/CMakeEpilogue.cmake .
    git add CMakeEpilogue.cmake
  - Deploy build configuration for Yocto/PetaLinux:
    cp -v $QUASAR/Extra/yocto/yocto_open62541_config.cmake .
    git add yocto_open62541_config.cmake
    ./quasar.py set_build_config yocto_open62541_config.cmake
  - Force quasar CMake headers as source:
    ./quasar.py generate cmake_headers
    cp build/AddressSpace/cmake_generated.cmake AddressSpace
    cp build/Device/generated/cmake_header.cmake Device/generated
    git add AddressSpace/cmake_generated.cmake -f
    git add Device/generated/cmake_header.cmake -f
  - Tag it all together
    git commit -a
    git tag -a v2
  - The project should still build on the host after this ;-)

---
PetaLinux + quasar (3):
PetaLinux step-by-step
- Note: using vanilla built image of PetaLinux. (Otherwise we’d need 30-60 minutes to get it built from scratch…)
- Step 1 – create the app in PetaLinux:
  petalinux-create -t apps --template install -n opcua-server --enable
- Step 2 – replace the recipe (BB file) with one shipped by quasar
  cp $QUASAR/Extra/yocto/my-opcua-server.bb project-spec/meta-user/recipes-apps/opcua-server/opcua-server.bb
- Step 3 – you might need extra recipes, depending on PetaLinux versions (all shipped with quasar). I need:
  - python-enum34, xsd,
    cp $QUASAR/Extra/yocto/xsd_4.0.0.bb project-spec/meta-user/recipes-apps/opcua-server/
    cp $QUASAR/Extra/yocto/python-enum34_1.1.6.bb project-spec/meta-user/recipes-apps/opcua-server/
  - python-six is broken in PL2017.4 so take fixed one and fix layer prio to 8:
    cp ~/SoC_Workshop/Extra/python-six_1.10.0.bb project-spec/meta-user/recipes-apps/opcua-server/
    emacs ./project-spec/meta-user/conf/layer.conf ( change to e.g. 8)
- Step 4 – fix where the path of the quasar project is
  - emacs ./project-spec/meta-user/recipes-apps/opcua-server/opcua-server.bb
  - Fix SRC_URI to:
    SRC_URI = "git:///home/pnikiel/gitProjects/SoC_Workshop_Quasar;branch=master;tag=v5"
- Step 5 – build the PetaLinux user image (i.e. the target image) – should take about 18 minutes
  - petalinux-build
- Step 6 – package the image and stuff as bootloader binary, copy to the SD card
  - zybo_package
  - zybo_cp_boot

---
PetaLinux + quasar (4):
PetaLinux step-by-step
- Boot the development board
- Use minicom as the console
- Connect with OPC-UA client

---
Part 3:
Integrating real monitoring and controls

---
Integrating real monitoring and controls
simple example (1)
- so far, we published switch status from from random number → we want real I/O
- generally analog digital I/O interfacing is a vary varied topic → out of scope
- I’ll use a simple GPIO library for GPIO handled by /sys/class/gpio subsystem (e.g. compatible with Xilinx GPIO driver)
  - covers few types of both PS and PL GPIOs of Zync

---
Integrating real monitoring and controls
simple example (2)
- I deploy the GPIO library to my project:
  cp ~/SoC_Workshop/Switch/gpio.h Device/include/
  cp ~/SoC_Workshop/Switch/gpio.cpp Device/src/
  git add Device/include/gpio.h
  git add Device/src/gpio.cpp
  and add src/gpio.cpp to CMakeLists.txt
- I know that GPIO base of Zync PS in Zybo is at 906 → I put that into a header file
- Buttons bound to Zync PS have ids of 50 (BTN4) and 51 (BTN5) → those will come via config file

---
Integrating real monitoring and controls
simple example (3)
- GPIO must be opened and initialize prior to use → I do it via initialize() of QuasarServer
  if( open_gpio_channel(ZYBO_GPIO_BASE) < 0)
    throw std::runtime_error("couldnt open GPIO interface");
- Direction must be configured to input → I do it via Device constructor
  set_gpio_direction(ZYBO_GPIO_BASE + config.pinId(), 1, "in" );
- We can finally do our readout in update():
  int value = get_gpio_value(ZYBO_GPIO_BASE + pinId(), 1);
  if (value<0)
  getAddressSpaceLink()->setNullState(OpcUa_Bad);
  else
  getAddressSpaceLink()->setState(value>0, OpcUa_Good);
- Check if it compiles fine on laptop
- Update our config file (we added new config entry: pinId)
- If yes, commit and tag
- Rebuild the PetaLinux image and test

---
A note on peripheral integration
- quasar is agnostic on how you produce/consume sensor/actuator info
- overall we successfully built OPC-UA servers with different interfaces (CAN, SNMP, …), hardware access layers (IIO – e.g. Xilinx XADC), shared memory interfaces (VME monitoring) and so on …
- different communication patterns are supported:
  - publishing
  - read on request
  - writing, with optional delegates
  - method calls with N arguments and M return values, N and M arbitrary
- all “basic” data types are supported. Arrays are supported as well as BLOBs (“byte-strings”).

---
Part 4:
What about integration in the DCS systems?
(SCADA, WinCC OA)

---
Integration into DCS
- quasar-based OPC-UA solutions enjoy simplified integration
- WinCC OA basic concept regarding OPC-UA
  - create your DPTs (Data Point Types)
    e.g. Sensor, Crate, Branch, TriggerProcessor etc.
  - create DPs (Data Points)
    they are particular instances of DPTs, e.g.:
    Processor1/Sensor4A
  - assign so called peripheral addresses “binding” given parts of DPs to the information in your OPC-UA server
    - So you start to “see” information from your front-end or can control it
- fwQuasar is a framework for WinCC OA enabling very quick (order of minutes) integration of quasar-based monitoring and controls into DCS

---
Integration into DCS
let’s try it
- Requirements:
  - An existing WinCC OA projects with JCOP framework installed
- fwQuasar is very well documented
  (multiple entry-level developers successfully used it)
- Clone Cacophony into your OPC-UA server project:
  git clone ssh://git@gitlab.cern.ch:7999/pnikiel/cacophony.git Cacophony
- Install fwQuasar in your WinCC OA project
- Run the OPC-UA client
- Run the dialog and follow the path. Proposed settings:
  - prefix = SOC
  - server name = SOC_Server
  - subscription = SOC_Subscription
  - driver num = 69

---
Links, references ...
- quasar:
  https://github.com/quasar-team/quasar
  Numerous references in:
  https://github.com/quasar-team/quasar/wiki
  After cloning, see Documentation/yocto.html
- fwQuasar:
  https://gitlab.cern.ch/atlas-dcs-fwcomponents/fwQuasar

---
Backup slides

---
Additional ...

---
- C++ OPC-UA clients …
- Integration of OPC-UA servers as components in Python