## Slide 1: PhD proposal
Effect of fast transients in sc. Magnets on circulating beams
Motivation:
Fast rise kicks observed during main dipole quenches with circulating beam: rise time 3 turns, ~60% of static max. field reached after 1 ms  currently not explained by the models
  LHC studies show that time constants and peak field change with beam screen temperature (qualitative, but not quantitative agreement)
  Observed behavior implies two processes with different time constants (very fast rise, followed by slow increase)
SM18 measurements on MQXF short model:
  Measurements not conclusive for quench heater firing due to limited bandwidth of pick-up coils
  Analysis & simulations of CLIQ impact ongoing, but measurements setup seems also to have limitations during high current experiments
  Next SM18 measurements with beam screen will be performed with a rotating coil  even smaller bandwidth, not expected to give more insight on QH or CLIQ behavior
Beam screen shielding is generally important for accelerators
  Effect of power converter ripples on the beam
  Effect of flux jumps on the beam
  …
PhD should cover dedicated experiments, where the different effects/components can be studied independently and combined. In parallel the effects should be modelled in STEAM and the models validated with the experiments.