## Slide 1: International Review of the HL-LHC Collimation System
Review Panel
Ralph Assmann (DESY), Wolfram Fischer (BNL), Mike Lamont (CERN), Mike Seidel (PSI, Chair), Alban Sublet (CERN), Walter Venturini (CERN).
Mandate
The main objective is to review the collimation system of HL-LHC in view of the LHC Run 1 and Run 2 experience and the suitability for installation in the LHC. The review will examine the upgrades in the experimental and cleaning insertion regions as well as the new cleaning systems in the dispersion suppressor regions of P7 and P2.
11-12 February 2019

## Slide 2: General comments
The excellent performance of the collimation system has contributed directly to the success of LHC thus far, particularly the increase of luminosity via the reduction of beta* over time.
The efficiency of operation was strongly improved by automated methods and the use of integrated BPMs.
The availability of the system has been excellent.
Particle tracking, impedance calculation and radiation transport simulations were improved over time, showing good agreement with measurements.
With the development of MoGr collimators and low impedance coating important improvements were achieved.
The baseline scenario provides beam stability with a margin dictated by present experience and compatible with sufficient dynamic aperture.

## Slide 3: Charge Questions I
Is the collimation system in the present baseline addressing the design criteria required for the HL-LHC operation?
Are the original design criteria of the collimation system validated by the LHC Run 1 and Run 2 experience and by the various tests carried out on each component?
Is there room for modifications or simplification after the LHC Run 1 and Run 2 evaluation and what would be the resulting risk implications?
What should be learnt in Run 3 as feedback to the LS3 plans?

## Slide 4: Strategy well elucidated

## Slide 5: Findings
Design criteria from LHC used for HL (x 2 Intensity)
Normal Operation
  Slow losses
   Continuous: 1 h Beam Life Time (BLT)
   Peak: 0.2 h BLT during 10 s
Accident Scenarios
  Beam Injection Error: impact of 288 bunches at 450 GeV, impact parameter up to 5 σ (σ = 0.7 mm)
  Asynchronous beam dump: impact of 8 bunches at 7 TeV on TCSPM, TCPPM, impact parameter up to 5 σ
  Asynchronous beam dump: impact of 1 bunch at 7 TeV on TCTPM, impact parameter up to 5 σ

## Slide 7: Findings
Excellent and stable cleaning performance over the years
  Key to reduction in beta*
  Peak losses in ADJUST phase (when putting the beams in collision)
  Critical limiting loss location still in DS
  Cleaning efficiency improved over the years with tighter collimator settings
  Excellent availability
Operational experience shows low probability of lifetime below 1 hour
  for intensity above 2e13 protons we have 0 cases with lifetime below 0.2 hours, 28 s < 1 hour with 400+ bunches
  No operational experience with LIU beams before Run 3
Only one asynchronous dump so far
Impact tests done with 55% HL bunch intensity (but equivalent density)
Design choices for collimation upgrade in the cleaning insertions driven by impedance reduction
  Some discrepancies (factor 2 in Mo tune shift, factor 2 in LO strength to ensure stability, factor 3 on observed loss signal in BLM, quench limits)
DS losses addressed with TCLD  needs 11 T dipoles
IR cleaning with metal jaws, TCT W, proposed to be replaced with CuCD

## Slide 8: Comments
FLUKA simulations/BLMs:
  considering the complexity of simulation, a factor 2-3 agreement with measurements is a impressive achievement given the 7 orders of magnitude
TCDQ possibly limiting further reduction in beta*
  upgrade not in baseline…

## Slide 9: Answers/Recommendations I
Is the collimation system in the present baseline addressing the design criteria required for the HL-LHC operation?
Yes
Are the original design criteria of the collimation system validated by the LHC Run 1 and Run 2 experience and by the various tests carried out on each component?
Yes, all concepts have been validated by Run 1 and Run 2 experience and tests
  Upgraded HW: TCP.C6L7.B1, TCSPM tests in beam OK
  In jaw BPM fully validated + (fully automatic) alignment,
  Impedance
  Outgassing
  Quench limits
  Beam loss through the cycle (pp & ions) characterized
Quench tests are necessary to validate the simulations and should be given adequate priorities, in particular for the 11 T
HiRadMat tests with HL intensities still to be performed

## Slide 10: Charge Questions II
Review the observed hardware performance during the present prototype production:
Are there non-conformities and how relevant are they for the HL-LHC operation and could they limit the HL-LHC performance reach (or the LHC performance for the collimator installed in Run 3)?
Are the observed hardware characteristics compatible with the HL-LHC operation requirements?
Review in particular the motivation for using coated MoGr as collimator material [robustness, likelihood of damage and impact of damage on the rest of the machine] also based on the LHC Run 2 operation:
Is the use of MoGr as collimator material well justified or could other materials with better conductivity or other combination of jaw bulk material with coating be used instead?

## Slide 12: Findings
MoGr bulk material is close to vacuum acceptance limit, in some case a factor 2 above acceptance. Mitigated by NEG cartridges.
Impedance question well addressed, first from material point of view with the use of MoGr less resistive material + Mo-coating for the secondary collimators, and second from geometrical aspect by implementing tapering.
Coating complies with vacuum standards of adherence.
Mo-coated MoGr was tested for vacuum with one surface coated. Vacuum performance was a factor 2-3 worse than without coating. An additional heat treatment of coated MoGr at 400°C allowed the recovery of uncoated MoGr outgassing level.
5th axis with +/- 10 mm range in case of “soft damage” of the jaw allowing longer operation time without impacting too much the impedance budget for secondary collimators

## Slide 13: Comments
The committee is impressed by the presented results on R&D, design, prototyping and production of advanced jaw materials, optimized collimators and critical hardware components for the system.
We congratulate the teams on the careful follow-up on the prototyping and production, carefully addressing non-conformities and developing mitigation measures.
In particular we acknowledge the outstanding performance of the collimator controls including the sensors and actuators. The availability of the system is remarkable.

## Slide 14: Answers I
Review the observed hardware performance during the present prototype production: are there non-conformities and how relevant are they for the HL-LHC operation and could they limit the HL-LHC performance reach (or the LHC performance for the collimator installed in Run3)?
  The speakers presented the status of collimator production. Several non-conformities or potential issues were identified, e.g. in the roller screw quality, measured resistivity of material, vacuum outgassing.
  All of them were carefully analyzed and solutions were implemented.
  A few studies are still ongoing, in particular on radiation hardness of the final material.
  For the presented results we conclude that the ongoing collimation upgrade has no evident short-comings, it can be expected to fully deliver the specified hardware improvements and it will therefore maximize collimation performance reach for the next decades of LHC operation.

## Slide 15: Answers II
Are the observed hardware characteristics compatible with the HL-LHC operation requirements?
  The presented collimation upgrade plan includes novel hardware components that address several critical issues for HL-LHC operation, namely:
    a reduction of both resistive and geometric impedance,
    materials for improvement of cleaning efficiency,
    a new local collimator in the dispersion suppressors,
    a hollow electron lens for limiting power in the beam tails,
    improved controls for longer component lifetime,
    a crystal assistance system for ion operation
    NEG cartridges for vacuum optimization.
  The presented hardware specifications and results are fully compatible with the HL-LHC requirements. As only residual major worry we identify the radiation hardness of the MoGr material with coating.

## Slide 16: Answers III
Review in particular the motivation for using coated MoGr as collimator material [robustness, likelihood of damage and impact of damage on the rest of the machine] also based on the LHC Run2 operation: Is the use of MoGr as collimator material well justified or could other materials with better conductivity or other combination of jaw bulk material with coating be used instead?
  The Mo coating of the jaws with MoGr bulk material reduces the collimator-induced impedance and therefore directly maximizes performance reach of the LHC.
  The speakers presented careful investigation of the coating in terms of resistivity, adherence, robustness against damage and vacuum performance.
  The committee is impressed with the quality and completeness of the studies.
  The choice of MoGr material with Mo coating is supported, subject to successful radiation robustness tests.

## Slide 17: Recommendations I
The presented high level of quality control during production should be maintained.
Above tolerance heat induced flatness deformations in the design should be accepted for the short periods of times concerned and not be addressed by reducing the collimator length. However the improved cooling and machining approach should be pursued as a first alternative.
Review the radiation hardness once the data on the MoGr material is available, both for bulk MoGr material and MoGr coated with Mo.
Complete and present the studies for radiation impact of the upgraded collimation system with the new materials installed, e.g. on peak doses to personnel.

## Slide 18: Recommendations II
Think about a vacuum test to quantify outgassing in conditions that resembles the machine configuration with one surface coated by Mo and compare with the case of uncoated surface (bare MoGr), taking into account local heating sources in operation and closure of surfaces when installed.
Try a real destructive coating test with prototype in IR7 and under the LHC vacuum conditions.

## Slide 19: Charge Questions III
Is the cleaning upgrade envisaged for the DS still justified and good enough for both proton and ion beams at their maximum intensities or are there alternative solutions?
Is the IR cleaning envisaged for the HL-LHC well justified or are there alternative solutions?
Is the choice of installing collimators in the dispersion suppressors of point 7 still adequate taking into account the results of proton and ion operation in Run 1 and 2 including crystal tests.

## Slide 21
Pb: No cases below 1 hour during 2018

## Slide 22
Protons
Ions

## Slide 24: Findings
The presented scheme of DS collimators in-between a pair of 11 T magnets in IR7, and in a connection cryostat in IR 2 leads to just acceptable heat deposition in s.c. magnets, both for proton and ion operation
The development of the 11 T magnet prototype is sufficiently advanced and performance requirements are in line to be met
The upgraded IR cleaning schemes for IP1/5 provide sufficient suppression of losses; the situation appears well understood
HL-LHC optics v1.3, including matched MKD-TCT phase advance, allows the recovery of beta*=15 cm after the 2016 re-baseline

## Slide 25: Comments
The power deposition for the case of 0.2 h lifetime of 50 mW/cm3 in the 11 T magnet coil is just below the calculated limit of 70 mW/cm3; for such critical parameters margins should be specified and potential mitigation measures be established
In case of operational problems going back to the original baseline (2 assemblies/side) could be considered as a long term solution
The schedule for the 11 T magnet production is tight and presents a risk that installation in LS2 cannot be achieved; the possibility of installation in EYETS is a backup. In extremis, operation in Run 3 should be possible without 11 T (possible ion intensity limit).
Situations with 0.2 h lifetime were not observed in Run 2 with significant intensity; however, with higher intensity and crab cavities conditions might change and it is recommended to maintain this limit as the reference

## Slide 26: Comments/Recommendations
IR 1&5 Incoming Beam
  Additional bottleneck observed in Q4-Q5 region demands an additional pair of TCT in cell 6 to protect them while keeping TCT in cell 4 for triplet protection
  TCTs in cells 4 and 6 made either from W or CuCD are fully safe over a realistic range of setting; thus W can be chosen as cost effective solution; in the unlikely case of a single bunch impact the collimator had to be exchanged. If CuCD should be pursued, the case should be strengthened
IR 1&5 Outgoing Debris
  Less effective TAXN, but looks OK with movable TCL and fixed masks (TCLX4, TCLM4, TCLM6)
  Cleaning will be less constrained in HL era due to absence of Roman Pots. To be re-considered carefully if re-proposed.
Crystal collimation shows excellent performances, this option should be further developed especially for ions but not be considered as a replacement for DS collimators

## Slide 27: Answers/Recommendations
Is the cleaning upgrade envisaged for the DS still justified and good enough for both proton and ion beams at their maximum intensities or are there alternative solutions?
Yes, the IR7 DS collimator upgrade and proposed position required for ions, represent a reasonable compromise and should be executed.
Is the IR cleaning envisaged for the HL-LHC well justified or are there alternative solutions?
The proposed IR1/5 cleaning with TCLX collimator and masks provides a good solution with sufficient margin for power deposition.
Is the choice of installing collimators in the dispersion suppressors of point 7 still adequate taking into account the results of proton and ion operation in Run 1 and 2 including crystal tests.
The DS upgrade in point 7 is still adequate, taking into account the results from Runs 1 and 2.

## Slide 28: Further comments and recommendations
Overpopulated beam tails (5% beyond 3.5 sigma) were measured using collimators;
  Note that measurements were performed after 5 to 9 hours in collisions
  improved diagnostics should be made available for monitoring the tail distributions during the run
It not known how overpopulation of tails will scale with intensity
Perform an accelerator physics study trying to develop a diffusion model for the LHC that reproduces the observed amount of beam in the tails.
Using the hollow electron lens would allow to remove tails in a controlled way and would widen the impact parameter distribution on primaries; the committee supports the realization of the electron lens concept.

## Slide 29: Further comments and recommendations
Provide an overview on power loss to elements around the ring during different operating phases (how many watts to collimators, walls, magnets, dump, …).
Explore the limit of beta* for HiLumi LHC with the collimator upgrade, exploring all capabilities of the upgraded system. Find the limiting device (TCDQ?) and develop mitigation strategies for this limit.
Perform a simulation of cleaning efficiency and energy deposition taking into account a multiple imperfection model (jaw flatness, gravitational sagitta, angles, aperture imperfections).

## Slide 30: Comments on jaw length reduction
Permanent reduction of efficiency and power absorption of the reduced length collimator in all operating conditions. Significantly more secondary and tertiary halo leaks out.
Reduced impedance: gain is linear with the length. Unclear if this is needed. If needed one could instead also open a little bit the jaws for a longer collimator (gain with third power of gap), giving up some of the better efficiency. I would say neutral, if impedance is really an issue.
Reduced maximum sagitta of the jaw for shorter collimator jaw, only in case of low lifetime and heating. Even if the sagitta is smaller (depends on curvature and length), the local curvature might still the same. I would expect that for most cases the curvature of the beam close to the beam matters for scattering length, protection etc. Longer jaw still help for deformed jaws for capturing showers, also on the opposite jaw.
Overall benefits are not evident, were not really presented – speculative suggestion
And cost gains must be quite limited...
RA

## Slide 31: Conclusions
Impressive collaboration
  high level of technical, engineering, applied physics expertise
Huge amount of experience gained in Runs 1 & 2
  material++, simulations, control, operations, beam physics, machine protection, loss rates, vacuum, impedance
All very effectively used to address the HL challenges
Resulting in robust design respecting the specified criteria
  Not unexpectedly still some issues to be addressed (some of which we have hopefully identified above)
Main schedule and technical risk in the medium term would appear to be in the deployment of the TCLD/11 T assemblies.

## Slide 32: Thanks!
To the organizers for their hospitality and an intense, but very interesting program!
Speakers for excellent presentations and full coverage
Very good minutes from Alessio Mereghetti and Stefano Redaelli
For demonstrating the obvious commitment of the extended community!