## Slide 2: LHC Injectors Upgrade Workshop
Montreux, 13-15 February 2019

## Slide 3: Session 1 findings and actions

## Slide 4: Findings

## Slide 5: Session 1 – Findings
LHC standard beam remains baseline for HL-LHC luminosity production, other variants are back up
Operational efficiency and reliability of injectors
  10-14’ turnaround time are worth as much as 1010 p/b or 0.2-0.4 um emittance for integrated lumi target
  Scenarios optimised with shorter fill lengths (e.g. ultimate HL-LHC) increase the impact of the injectors’ reliability and affect non-LHC physics
  Flexibility of injectors for producing mixed schemes in operation is required
Challenging specs in terms of bunch-by-bunch variations provided by the experiments (should be as good as now, ~3%)  Emphasis on
  Linac4 reproducibility
  Beam loading compensation in PS during bunch splittings
  Mitigation of losses/blow up on flat bottoms
  Mitigation of intra-train incoherent loss/blow up effects (e.g. e-cloud)

## Slide 6: Session 1 – Findings
LIU proton beam intensity reached up to PS extraction
First experience in SPS with high intensity proton beams (LHC)
  Losses at flat bottom due to protons out of the bucket and momentum aperture
    Simulations show that in the future these losses should decrease significantly with increased power and new LLRF
    Lower longitudinal emittance (-15%) from PS could help for a better capture and fewer losses, and beam is stable at flat bottom
    Removal of momentum aperture limitation with new prototype flange not successful in 2018
  Horizontal instabilities observed for closely spaced trains with intensity above 1.8 ∙ 1011 p/b
  Flat top 800 MHz voltage set to 25% of the present 200 MHz voltage, but in the future 16% will be enough for beam stabilisation – pulsing of 800 MHz of little interest beyond 2.4 ∙ 1011 p/b

## Slide 7: Session 1 – Findings
LIU proton beam brightness depends on success of
  PSB brightness line with Linac4 as simulated
    25 mA with 0.3 mm are enough for LIU beams and all pre-LS2 beams
    LBE run necessary to demonstrate beam loading compensation for beam quality as well as debuncher parameter range
    Emittance measurements maybe overestimating present brightness line
  Space charge reduction at PS injection
    2 GeV injection
    Large longitudinal emittance in PSB
      Not yet demonstrated to be beneficial in PSB-PS transfer, but maybe due to other blow up effects at 1.4 GeV and presently unmatched transfer line
  SPS emittance blow up and losses in spec (10%) also for longer trains and higher bunch intensities

## Slide 8: Session 1 – Findings
LIU ion beam parameters reached up to PS extraction
Potential to further increase the intensity out of LEIR by ~20%, but limited interest due to PS transition crossing instability and scaling of SPS transmission with bunch intensity.
Ion beam longitudinally unstable in SPS
  Emittance blow up at transition crossing
  Instabilities at energy of plateau for slip stacking
Final reach depends on beam stabilisation and deployment of slip stacking, but mitigation in place (75 ns) to produce ~70% of target lumi even without

## Slide 9: Actions and timelines

## Slide 10: Session 1 – Action plan
Linac4  L4 BD WG and L4 CWG
  LBE run (12/2019) aiming to demonstrate
    25 mA with 0.3 mm within reproducibility specs
    Beam loading compensation (LLRF)
    Debuncher parameter range for all pre-LS2 beams
    Reliability > 98% with typical supercycle
    Longitudinal painting (low priority)
  Continuous cesiation and autopilot for the source with 3 MeV tests + LBE run (12/2019)
  Get ready for smooth 2020 recommissioning

## Slide 11: Session 1 – Timeline for Linac4
Q3-4/2020
Q1-2/2021
Run 3
LS2
Q1-2/2019
Q3-4/2019
Q1-2/2020
Start recommissioning:
Recover beams of LBE run (most likely no longitudinal painting)
Final commissioning for operation
End of LBE run:
Achieve 25 mA, 0.3 mm reliably and reproducibly
Test continuous cesiation

## Slide 12: Session 1 – Action plan
PSB  LIU-PSB BD WG
  Re-establish production schemes for all pre-LS2 beams with H- injection
    Low intensity: Longitudinal emittance blow up and longitudinal shaving for PROBE and INDIV or alternative scheme (06/2019)
    Medium intensity, i.e. LHC beams (12/2019)
      Brightness line with injection errors, optics imperfections, space charge
      Impact of emittance measurements on future brightness line
    Pre-LS2 high intensity: Losses at injection, need of longitudinal painting for ISOLDE and MTE beams (06/2019)
    For all beams (06/2020)
      Working point optimization with space charge
      Confirm that transverse damper cures instability from impedance
  Longitudinal stability with Finemet cavities (12/2019)
  Confirm that 2 transfers within <1.1 s are possible after LS2 (low priority)

## Slide 13: Session 1 – Timeline for PSB
Run 3
LS2
Q1-2/2019
Q3-4/2019
Q1-2/2020
Q3-4/2020
Q1-2/2021
Start beam
recommissioning
Longitudinal blow-up parameters low-intensity beams
Check if longitudinal painting not immediately required (including ISOLDE and MTE)
WP optimization
Complete simulations with TFB
Brightness curve for LHC beams
Longitudinal stability with Finemet
Tool for alignment
Validate KFA14 kicker impedance reduction measures

## Slide 14: Session 1 – Action plan
PS  LIU-PS BD WG
  2 GeV injection (12/2019)
    Space charge simulations to validate tune spread scaling also with respect to LIU longitudinal parameters (large longitudinal emittance)
  Flat top horizontal instabilities (12/2019)
    Interpret old data with e-cloud multi-bunch simulation model
    Cross-check with 2018 experience and extrapolate to future parameters (LIU parameters, 72 bunch trains)
  Performance predictions for LS2 RF upgrades (06/2019)
  Longitudinal instabilities with small longitudinal emittance (06/2020)
    Assess PS performance with full LIU upgrade and margin for production of lower longitudinal emittance to mitigate losses in SPS
    Study means to limit longitudinal halo production during longitudinal emittance blow up or bunch splitting in PS

## Slide 15: Session 1 – Timeline for PS
Run 3
LS2
Q1-2/2019
Q3-4/2019
Q1-2/2020
Q3-4/2020
Q1-2/2021
Start beam recommissioning
Complete longi-tudinal instability studies
Understand blow-up with large longi-tudinal emittance
Long. impedance source identification
Predictions RF upgrades post-LS2
PS-SPS transfer parameters
Potential reduction of halo
Study longitudinal emittance below baseline
2 GeV injection and flat-bottom
predictions

## Slide 16: Session 1 – Action plan
SPS
  Decision on new flanges for removal of momentum aperture restrictions (03/2019  LIU-SPS LS2 TC)
  Decision on 630 MHz HOM damper (06/2019  LIU-SPS LS2 TC)
  Injection losses (12/2019  LIU-SPS BD WG)
    Continue longitudinal simulations to confirm beam stability and reduced flat bottom losses with long trains of low longitudinal emittance bunches
    Stability along the ramp
  Longitudinal instabilities (12/2019  LIU-SPS BD WG)
    Prove 800 MHz requirements also along the ramp
  Horizontal instabilities (06/2020  LIU-SPS BD WG)
    Identify the source (impedance and/or e-cloud) by matching machine measurements with models
    Define strategy to cope with it in the future operation

## Slide 17: Session 1 – Timeline for SPS
Run 3
LS2
Q1-2/2019
Q3-4/2019
Q1-2/2020
Q3-4/2020
Q1-2/2021
Start beam recommissioning
Longitudinal injection losses (long batches)
Decision on aperture restrictions
Decision on 630 MHz HOM dampers
Define 800 MHz requirements
Define strategy to mitigate with horizontal instability
Identify source of horizontal instability

## Slide 18: Session 1 – Action plan
Ions
  LEIR modeling (12/2019  LIU-ION PS Injectors BD WG)
    Simulations including space charge, IBS, electron cooling
    Further impedance identification for future reduction
  PS microwave instability (12/2019  LIU-PS BD WG)
    Modeling with present PS impedance model to explain instability at transition and devise mitigations
  SPS longitudinal instabilities (09/2019  LIU-SPS BD WG)
    Complete data analysis from 2018
    Define strategy to cope with it in the future operation (use of 800 MHz and/or longitudinal emittance blow up)
  Define strategy for slip stacking (2020,  LIU-SPS BD WG)

## Slide 19: Session 1 – Timeline for ions
Run 3
LS2
Q1-2/2019
Q3-4/2019
Q1-2/2020
Q3-4/2020
Q1-2/2021
Start beam recommissioning
Capture loss studies in LEIR
Simulate long. ion instability in SPS
Define scenario for slip stacking
Study max. int. in LEIR
Simulate transition crossing in PS

## Slide 20: Summary
Major milestones on path to LIU proton performance
  Linac4: Achieve 25 mA, 0.3 mm reliably and reproducibly
  PSB: Re-establish production schemes for all pre-LS2 beams
  PS: Injection of large momentum spread Smaller longitudinal emittance for transfer to SPS
  SPS: Longitudinal injection losses Stability with small longitudinal emittance Horizontal stability at high intensity
Major milestones on path to LIU ion performance
  SPS: Longitudinal stability Slip-stacking

## Slide 22: Key studies in PSB
 | Activity | Timeline
Transverse | Conclude on transverse emittance measurements as input for brightness curve | Q2/2019
 | Establish common model for space charge simulations, including imperfections, to define optics choices at injection | Q3/2019
 | Study impact of unmatched termination of extraction kicker (horizontal instability) | Q3/2019
 | Prepare tool to optimize alignment of all rings after LS2 | Q1/2019
Longitudinal | Controlled longitudinal blow for longitudinal shaving | Q3/2019
 | Definition of longitudinal parameter sets for all beams | Q3/2019
 | Renovation and possible upgrade of longitudinal Tomography | Q1/2020
 | Longitudinal emittance model after LS2 | 2020

## Slide 23: Key studies in PS
 | Activity | Timeline
Transverse | Analysis of KFA45 field measurements | Q2/2019
 | Conclude on emittance blow-up measurement (systematic errors) | Q2/2019
 | PSB-PS transfer line matching using turn-by-turn acquisitions | Q4/2019
 | Simulations to understand relevance of space charge after injection | Q4/2019
Longitudinal | Identify impedance source exciting longitudinal instabilities | Q2/2019
 | Performance predictions for RF upgrades during LS2 | Q2/2019
 | Review longitudinal parameters at PS-SPS transfer | Q4/2019
 | Longitudinal impedance model after LS2 | Q4/2019

## Slide 24: Key studies in SPS
 | Activity | Timeline
Transverse | Removal of momentum aperture restrictions (MBB-SSS), decision on installation | Q1/2019
 | Benchmarking of bunch-by-bunch tune shift measurement with impedance model | Q2/2019
 | Horizontal instability at SPS injection, identification of source | Q4/2019
 | Impact of bunch-by-bunch tune shift on incoherent tune footprint of different bunches for working point optimization | 2020
Longitudinal | 630 MHz HOM damper (shift of fundamental mode), decision on installation | Q2/2019
 | Beam loss at flat-bottom and beginning of ramp, smaller longitudinal emittance | Q3/2019
 | Impact of smaller longitudinal emittance during acceleration | Q4/2019
 | Impact of installing 200 MHz cavities for eSPS (for PBC and CLIC) | Q4/2019

## Slide 25: Key studies with ions
 | Activity | Timeline
Transverse | Space charge and IBS studies of capture beam losses | Q2/2019
 | Maximum accumulated intensity in LEIR (injection process, cooling) | Q4/2019
 | Analyse beam stability versus intensity in LEIR (impedance and cooling) | 2020
 | Injection optics to reduce losses from Linac3 to LEIR | 2020
Longitudinal | Optimum longitudinal emittance from LEIR | Q4/2019
 | Microwave instability at PS transition crossing, impedance source identification | Q4/2019
 | Simulate longitudinal ion instability in SPS and propose mitigation | Q3/2019
 | Definition of scenario for slip-stacking in SPS | 2020

## Slide 26: Challenges on the path to LIU performance
Protons | Mitigation | Activity
Large momentum spread transfer PSB-PS | Matched transfer line optics | In depth analysis of 2018 data and simulations
PS-SPS transfer | Smaller longitudinal emittance from PS | Simulation studies of transfer and long. stability in SPS
Transverse stability and e-cloud in SPS | Landau damping, wideband feedback system, scrubbing | Identification of instability source
Beam losses at SPS injection | Lower longitudinal emittance from PS, enlarge momentum aperture | Analysis of efficiency and margins, lift momentum aperture restrictions
Ions | Mitigation | Activity
Longitudinal stability in SPS (for slip-stacking) | Controlled emittance blow-up before transition | Simulation studies

## Slide 27: Progress summary
Linac3
LEIR
PS
SPS
HL-LHC parameters reached with lead ion at PS extraction
Linac2
PSB
PS
SPS
Linac4
Intensity
Brightness
(studied with BCMS)
Protons
Ions