## Slide 1: The Advanced Virgo detector: control, noise hunting and data quality to improve its sensitivity
David Cohen dcohen@lal.in2p3.fr
Supervisor: Nicolas Arnaud
Laboratoire de l’Accélérateur Linéaire, Orsay, France – Groupe Virgo
CNRS/IN2P3, Université Paris-Sud
Tuesday the 28th of May, 2019
stability?

## Slide 2: The Advanced Virgo detector: control, noise hunting and data quality to improve its sensitivity
David Cohen dcohen@lal.in2p3.fr
Supervisor: Nicolas Arnaud
Laboratoire de l’Accélérateur Linéaire, Orsay, France – Groupe Virgo
CNRS/IN2P3, Université Paris-Sud
Tuesday the 28th of May, 2019
Help develop a web page interface to list all the losses of lock (control) of the automatic control system.
Optomechanical parametric instabilities study for Virgo
with:
Annalisa Allocca, Pisa/INFN Pisa
Paola Puppo, INFN Roma
Gilles Bogaert, Artemis
Thibaut Jacqmin, LKB

## Slide 3: Introduction
Gravitational waves basics
How to detect gravitational waves
Detections

## Slide 4: Gravitational waves (GW): basics
Ripples of the curvature of spacetime: ‘space tells matter how to move […] matter tells space how to curve’ (Misner, Thorne & Wheeler, in Gravitation, 1973).
Emitted by accelerating massive bodies; travel at the speed of light.
Stretch and squeeze an object; the larger the object, the more it stretches as:
where L0 is the length of the object, the length variation due to the GW, and h the GW strain amplitude.

## Slide 5: Gravitational waves (GW): basics
Transverse waves; 2 polarisations.
+ polarisation
polarisation

## Slide 6: Gravitational waves (GW): basics
Transverse waves
similar to tidal effect
+ polarisation

## Slide 7: GW strain amplitude
Einstein formula:
with
 h is… ridiculously small!!

## Slide 8: Sources luminosity
The gravitation luminosity of a source can be written as:
where ε is the source asymmetry, the Schwarzschild radius, R the source radius, and v its velocity.
 to be a good GW emitter, a source needs to be asymmetric (ε 1), compact (RS/R 1), and relativistic (v/c 1).

## Slide 9: Outline
Introduction
  Gravitational waves basics
  How to detect gravitational waves?
  Detections
Three-mode parametric instabilities

## Slide 10: Ground-based interferometer for GW detection

## Slide 11: What is Virgo?
Michelson interferometer (ITF) → direct detection of gravitational waves
3 km arms with Fabry-Perot cavities to increase the light path
Working point @ dark fringe (destructive interferences)
Power Recycling mirror that reflects the light back to the ITF increasing the power in the ITF
Real-time active control of the working point: Sensing: photodiodes Actuation: mirrors, suspensions, laser
Large optics (mirrors) contained in superattenuator towers (inverted pendulums)
Small optics (telescopes, photodiodes) on suspended benches
Laser: wavelength = 1064 nm input power = 12-25 W continuous

## Slide 12: Outline
Introduction
  Gravitational waves basics
  How to detect gravitational waves?
  Detections
Three-mode parametric instabilities

## Slide 13: Observation Runs
For any GW detector, observation phases last for a certain time, called an Observation run.
Between two Observation runs, GW detectors are upgraded.
All the events recorded so far come from the Observation run 2 (O2) that lasted from 30 November 2016 (Virgo joined on 1 August 2017) to 25 August 2017.
Since 1 April 2019, O3 has started and will last for a whole year. At present, only potential candidates to GW events have been recorded and one will need several months for confirmation.
http://www.virgo-gw.eu/#news_o3_start

## Slide 14: Detections
GW170814: the first triple detection (LIGO + Virgo) of a binary black hole merger

## Slide 15: Three-mode parametric instabilities
AKA only ‘parametric instabilities’ (PI)

## Slide 16: 3-mode interaction

## Slide 17: 3-mode interaction
Anti-Stokes process: cooling
Stokes process: heating

## Slide 18: Mechanical and optical modes overlap
Mechanical mode
Optical mode

## Slide 19: Parametric gain
spatial overlap between optical mode and mechanical mode
optical gain (function of mechanical mode frequency, cavity lengths, Gouy phase, mirror reflectivities)
power travelling through the arm (Fabry-Perot cavity)

## Slide 20: Mechanical modes computation

## Slide 21: Homemade code for PI computation
Analytical method taken from Evans et al. "A general approach to optomechanical parametric instabilities." Physics Letters A374.4 (2010): 665-671
Matlab Oriented Object Programming (OOP) code
+
Graphical User Interface (GUI)

## Slide 22: What kind of results do we get?
We make the mirrors radii of curvature vary to take uncertainties into account.
White arrows: 24.381 kHz
Black arrows: 24.629 kHz

## Slide 23: What kind of results do we get?
Mecha mode @ 24.381 kHz
Mecha mode @ 24.629 kHz
Main contributing optical mode

## Slide 24: Ongoing and next steps
Various simulations w/ different configurations…
  With thermal effects
  With real maps of mirrors
… to foresee the next upgrades following the current observation phase:
  Laser power increase
  Another mirror will be added, thus creating a new optical cavity to take into account in the computation of the instabilities

## Slide 25: Spare slides

## Slide 26: Virgo’s eyes
The redder the map, the better the reception; the bluer the map, the blinder Virgo.
All the ground-based interferometers for GW detection have a similar antenna map: best receptions orthogonal to the ITF, worst ones on the plan of the ITF particularly those from the internal and external bisectors.

## Slide 27: Detections
GW170817: the first discovery of a binary neutron star coalescence followed the observation of its optical counterpart, thanks to the accurate 3D LIGO-Virgo localisation of the source

## Slide 28: Multimessenger detection

## Slide 29: The importance of volume x time
observable volume {observable range}3
GW event duration order of magnitude 1s

## Slide 30: Binary Black Hole merger

## Slide 31: LISA motion

## Slide 32: Other results
Maybe real mirrors, SRC, thermal
Or/and the maps of the real mirrors
The q factors plot
…. On verra

## Slide 33: Optomechanical parametric instabilities study for Virgo
David Cohen dcohen@lal.in2p3.fr
Supervisor: Nicolas Arnaud
Laboratoire de l’Accélérateur Linéaire, Orsay, France – Groupe Virgo
CNRS/IN2P3, Université Paris-Sud
Tuesday the 28th of May, 2019