## Slide 1: S/W Preservation & Legacy Issues at LEP (CERN)
Jamie.Shiers@cern.ch
Former Developer / Librarian: CERNLIB
Currently: Data Preservation in HEP
Paper and much background info:
https://indico.cern.ch/event/801649/

## Slide 2: Introduction
CERNLIB: some 3MLOC, mainly Fortran, some Assembler(s), C(++), Pascal etc.
Many contributors over several decades
Source code marked up for multi-platform support (a bit like C pre-processor)
Built for many platforms, different byte (word) length / order, FP operations, character sets
Regular binary multi-platform releases OR
Access to source code with build “suggestions”
In its dying days: migrated to CVS, cpp, gmake
Now “unsupported” but still in use, still being built, still used for published papers (Oct. 2018)…

## Slide 3: Preservation or Deletion?
“Obsolete” routines were first de-activated then later deleted (active) / not carried forward (passive)
No systematic archiving of source matching each published release
Release notes documented in Computer Newsletters (scanned; available) up to early 90s
MANY copies distributed around the world, mainly on 1600 bpi tapes (so lost???)
LEP (1989 – 2000) data: ~100TB / experiment (4)
[ LHC (2009 – 2040?) data: getting on for 100PB (av.) per experiment ]
Now 2 tape copies & 1 disk copy at CERN, plus numerous copies at outside labs
Would it really have been impossible to have systematically archived all s/w releases?
N.B. at the start of LEP, no managed storage: users bought and managed their own (200MB) tapes!

## Slide 4: Reviving old data
Of course, you need the data (“bits”) itself
But this is not enough:
  Source code; build procedures; validation suite …
Still not enough:
  calibrations, field-maps, basic documentation …
In some cases, source was in PL no longer supported
  Non-standard, e.g. CDC Fortran, Mortran, Sheltran, VAX Fortran, …
Can you revive code when you don’t really know what it is supposed to be doing?
With few / no comments, 1-2 character variables?

## Slide 5: A Holistic Approach (“Space”)
I contend that source code preservation, without build and validations systems, without basic documentation, as well as the necessary “environment” is close to useless for large-scale projects such as LEP, LHC, …
The “environment” is much more than the “VM” in which the code runs AND includes necessary configuration files, DB snap-shots, magnetic field-maps etc.
Even this may not be enough for reproducibility, e.g. HEP uses “triggers” (AKA filters) where much data is DISCARDED!

## Slide 6
Dear Jamie:
Reading the articles on open data and re-use in the last issue of the
CERN Courier has revived one of my worries which had remained
latent for some time:
How do we document convincingly trigger design and performance.
The concern is not so much that what we did not select is lost for ever,
but what are the biases in the raw data we retain.
Understanding the trigger performance is mandatory if outsiders,
by data re-use, produce important discoveries exposed to scrutiny
by the scientific community.
The LHC experiments are making a laudable effort to make their data
available but I have the impression the issue of documentation /
knowledge is not addressed vigorously enough at its roots,
i. e. real time trigger.
I feel that validity and limitations of data re-use for discovery should
be the subject of a thorough and humble analysis.
I am available for coffee if you wish to discuss this issue.
Cheers, Pier Giorgio

## Slide 7: A Holistic Approach – Time
OAIS tells us that we have to be aware of – and plan for – changes in technology
But this applies also to services, to programming languages, operating systems, compilers, code repositories etc.
It will also apply to PID systems etc!
Real experience with migrations show that they are expensive, often uncover hidden bugs, often data / knowledge is lost in the process
And this is during the “active” phase of a project!

## Slide 8: Holistic in Space & Time
Time – addressing service / technology / personnel changes and associated migration, adaption, re-validation, …
Space – addressing s/w and its complete eco-system, including also the data for which it is intended / associated