## Slide 1: A root macro for tracking sim
F. Bedeschi
FCC-ee Physics Meeting
CERN, February 28, 2019
Outline
The need
The core
Implementation
Examples
Fast simulation
Examples
Conclusions

## Slide 2: The need
IDEA tracking system still evolving
Need fast turn around in evaluation of various options
  Easy implementation of modified geometry
  Easy change of detector performances
Need realistic input for fast simulation
  Full covariance matrix
  Dependence on pt and polar angle

## Slide 3: The core (1)
Track fit c2 linearized in the fit parameters:
  d/d* = predicted/measured distance of track from wire or pixel
  p = track parameters
  S = covariance of all measurements: resolution & MS
    MS  worse resolution and non diagonal correlation terms
Track parameter resolution depends on S and derivatives:

## Slide 4: The core (2)
Use full track helix for trajectories/acceptance, but
  Keep only first outgoing branch
    f(R) = f0 + ArcSin{[RC+(1+CD)D/R]/(1+2CD)}
    z(R) = z0+ ArcSin
Some approximations in the calculation of derivatives;
  CD<<1, |D| <<R
  OK also for low momentum track

## Slide 5: Implementation (1)
SolGeom class:
  Fills geometry and draws it
    Draws also the material
  Each sub-detector can be turned on or off
  All layers either:
    Measurement or inert (for MS)
    Measurement is axial (Rf), small angle stereo or 90 deg. (Rz)
    Cylinder shell (const R) or disk (constant z)
  Can write geometry to a text file
  Can be initialized by reading text file

## Slide 6: Implementation (2)
Typical SolGeom geometry block

## Slide 7: Examples (1)
Initialize geometry and draw it
 material plot

## Slide 8: Implementation (3)
SolTrack class
  Initialize with a geometry (SolGeom type) and two possible parameterizations (with automatic conversion):
    : postion and momentum vectors
    C, f0, D, cot(q), z0: helix parameters
  Finds intersection with any given layer (acceptance)
  Calculates helix parameter covariance matrix
    Include multiple scattering contributions with correlations

## Slide 9: Examples (2)
Draw a track:

## Slide 10: Examples (3)
Compare resolution plots with full simulation (red = fast)
90 deg
45 deg

## Slide 11: Make it faster
SolTrack calculation of covariance matrix slow
  Involves inversion of matrix ~ 120x120
Solution:
  Store pt-polar angle grid of matrices in .root file
  Get any matrix by interpolation over 2D-grid
Implementation with class SolGridCov

## Slide 12: SolGridCov
Methods:
  Creates TTree with covariance matrix branches
  Calculates covariance matrices at nodes with SolTrack
  Interpolates covariance matrix for any pt–polar angle
    C = C11(1-tpt)(1-tth)+C12(1-tpt)tth+C21tpt(1-tth)+C22 tpt tth
    tpt = (pt-ptmin)/(ptmax-ptmin), tth = (th-thmin)/(thmax-thmin)
    Protect positive definitness
  Write/Read covariance matrix grid to file

## Slide 13: Examples (4)
Resolution comparison (90 degree)
From grid
From SolTrack

## Slide 14: Application to simulation
Class ObsTrk:
  Takes input perfect track  observed track
    Conversion to helix parameters
    Smear helix parameters according to appropriate covariance matrix
      Use Choleski decomposition

## Slide 15: Example (5)
Application in invariant mass calculation in Pythia generated events

## Slide 16: Example (6)
Higgs recoil from HZ (Zm+m-) – 0.1% COM energy s

## Slide 17: Conclusion (1)
Simple ROOT based classes to simulate tracking system resolution
  Easy to change configuration
  Perfect to compare options
Used to feed Fast Sim a realistic covariance
  Could be included inside DELPHES
Validated on full simulation
Demonstrated on specific physics process

## Slide 18: Conclusions (2)
Additional work:
  Agree on baseline geometry and resolutions
  Generate several geometry/covariance files for comparisons
    CLD, CepC baseline, variations of IDEA baseline for optimization purposes
  Use for physics studies involving tracking only
Quite possible now for Oxford and FCC week
Need dedicated student to converge rapidly
All software described here can be found in
  https://www.pi.infn.it/~bedeschi/RD_FA/Software/