## Slide 1: Experimental Area Beam Intercepting Devices – Motion control and actuation
Mark Butcher and Mario Di Castro for EN/SMM
15/03/2019

## Slide 2: Introduction
EN-SMM responsible for the motion control systems of the motorised Beam Intercepting Devices (BIDs) in the North and East areas
EN/EA or EN/STI are responsible for the mechanics depending on device

## Slide 3: Devices
NA Targets
XCSH/V
XCON
XCHV

## Slide 4: Devices
XCMH/V
XCBV
Microcollimator
MultiTarget

## Slide 5: Devices
XSPL
XABS
XTDV
XTAX

## Slide 6: North Area
>110 Devices in the North Area Complex
  15 ‘XTAX-type’ Large AC Motor (2-4 kW) devices
    15 motorised axes
  20 Smaller AC Motor (≈ 0.2 kW) devices
    50 motorised axes
  65 Brushed DC Motor devices
    155 motorised axes
  Others
    6 XTDVs
    Micro-collimator
    1 Dump Control
    1 XTAX Cooling Monitoring
  4 Target stations (3 main axes each)
All consolidated since 2008

## Slide 7: East Area
9 Brushed DC motor devices (XCON and XCHV)
  30 motorised axes
2 MultiTargets (designed by EN/STI)
To be consolidated during LS2.

## Slide 8: Typical Control Architecture
Control system:
Low-level real-time either:
  Siemens PLC
  National Instruments PXI
High-level communication level:
  FESA class
Actuators:
  AC, DC and Stepper motors
Position sensors:
  Potentiometers
  Resolvers
  LVDTs (like LHC Collimators)
Features:
Positioning precision of +/-100µm
Remote diagnostics
Full remote control
Alarms
Logging to CALS

## Slide 9: Typical North Area Control Racks
Control systems of DC devices in TT81 and TT82
Racks RA0230 to RA0233

## Slide 10: Status
North Area
  Majority of devices already consolidated, annually maintained and supported by EN/SMM piquet✔
  Spare levels at 25% ✔
  During LS2:
    Investigate target LVDT interference
    Microcollimator to be consolidated in 2020 to use same control architecture as other NA devices
    XTAX (P4 TAX 043.018/20 and P6 TAX 062.052/54) will be modified to be compatible with the new access system

## Slide 11: Status
East Area:
  XCHV, XCON control system to be consolidated during LS2 to have similar architecture to North Area
  2 new MultiTargets will be built (by EN/STI) and installed during LS2 and the control system consolidated.
  Planning coordinated with the East Area consolidation project organisation.

## Slide 12
Thank you!