## Slide 1
  klystron E37113(C) with different operation conditions for variable repetition rate is available (repetition rate limited by collector dissipation )
  6.2 MW peak power, 175 kV, 115 A
  received proposal of the specifications for X-band 6 MW klystron and accessories
  pulse changes with variable repetition rate :
 | 400 pps | 500 pps | 750 pps | 1000 pps
Pulse width 1 | 7.5 us | 6.0 us | 4.0 us | 3.0 us
Pulse width RF 2 | 5.0 us | 3.5 us | 1.5 us | 0.5 us
1 Pulse width (duration) measured between the 75% points of the beam voltage pulse.
2 Pulse width RF is measured between the 3 dB points of the RF output pulse.
WP4: Task3 - Modulator and Klystron technology
Update
Discussion with T. Anno from CANON ETD

## Slide 2
JEMA interested in development higher rep rate modulators
2 modulators for IFIC Valencia (S-band, but for the modulator the frequency of the tube is not an issue)
Specifications:
  150kV 110A , 16.5 MW peak power , 10us maximum pulse length, rep rate 400Hz
They could consider TWIN modulator but point out the it saves mainly space :
  One control
  One pulse transformer (somewhat larger but not twice the size)
  Smaller oil tank
  Power electronics only a small benefit

## Slide 3
Soft FEL
Linac energy gain : 2 GeV
Repetition rate 1000 Hz
Smart solution : use the same 20 high-power RF units as in Hard FEL case
… but as studies of Frascati groups shown it does not scale well
Rep rate increase is limited by klystron inefficiency outside working point
WP4: Task3 - Modulator and Klystron technology

## Slide 4
Soft FEL
Linac energy gain : 2 GeV
Repetition rate 1000 Hz
Repetition rate can be increase based on dedicated tubes,
in substitution of or in addition to high peak power ones
WP4: Task3 - Modulator and Klystron technology
Same modulator for 2 tubes only possible is the voltage is the same for both
Means 2 klystrons and 2 modulators per Linac module

## Slide 5
Smart solution might be out of reach
We should prepare two schemes
Soft FEL
High repetition rate achievable with Canon tubes (or CPI when they appear)
WP4: Task3 - Modulator and Klystron technology
Pulse shortening will reduce the compression rate, but the flexibility with repetition rate of the tube is big advantage

## Slide 6
Hard FEL
Baseline for RF unit:
1 modulator
1 klystron -> 50 MW, 1.5 us
1 SLED compressor -> ~160 MW
4 ACS modules -> 65 MV/m gradient
Repetition rate 100 Hz
Linac energy gain : 4.5 GeV
Power per single structure from klystron 10 MW
Total: 20 RF units
WP4: Task3 - Modulator and Klystron technology

## Slide 7
Alternative if we want to use the same tubes
low rep rate … modular system à la X-Box3 switching
X-Box3
We should push for dual-X-band modulator
WP4: Task3 - Modulator and Klystron technology