## Slide 1
WP4 Status Overview
Baseline linac rf system well established
  rf parameters, power source choice, etc.
  Moving toward detailed layout of waveguide system etc.
Longitudinal layout and dimensions written down, now being evaluated with beam dynamics
  In this step we need to make assumptions about other systems such as magnets, beam instrumentation etc.
PBS (Project Breakdown Structure) draft made for linac for cost model
  PBS to be used also for dimensions and power consumption
  Consistent with CLIC PBS to allow direct comparison
  Can be expanded to larger portions of CLIC
Dual mode operation, high energy/low repetition rate and low energy/high repetition rate, under active study
Baseline design established for 2 MW gyroklystron design for 3rd harmonic linearizer.
  Higher power and 48 GHz system under study
Work on Deliverable to start soon.
  First step is draft table of contents and identify responsibility for chapters

## Slide 2
Freq. of 2π/3 mode [GHz] | 11.9942
Average iris radius <a> [mm] | 3.5
Total length of the TW structure Ls [m] | 0.9
RF pulse [µs] | 1.5
Average gradient <G> [MV/m] | 65
Linac Energy gain Egain [GeV] | 1
Linac active length Lact [m] | 18
Unloaded SLED Q-factor Q0 | 180000
External SLED Q-factor QE | 21600
Iris radius a [mm] | 4.0-3.0
Group velocity vg [%] | 3.7-1.5
Effective shunt Imp. Rs [M/m] | 389
Filling time tf [ns] | 130
Input power per structure Pk_s [MW] | 9.8
Structures per module Nm (input power per module Pk_m [MW]) | 4 (39)
Total number of structures / klystrons | 20 / 5
EUPRAXIA@SPARC_Lab <a>=3.5 mm
EUPRAXIA@SPARC_Lab <a>=3.2 mm
EUPRAXIA@SPARC_Lab old working point
(optimization of RF power splitting)
Best effective shunt impedance
2
Linac active length=18 m (was 16 m of the old working-point), but 16 structure interconnections eliminated
Linac energy on crest = 1.17 GeV with 5 klystons ( in the old WP was 1 / 1.1 GeV with 4 / 5 klystrons)
Using the CompactLight accelerating section for EUPRAXIA@SPARC_LAB
S. Gallo

## Slide 3
3rd scenario: high rep rate – reduced peak power klystrons
rep rate increase based on dedicated tubes, in substitution for or in addition to high peak power ones
2 klystrons x LINAC Module
<Eacc> = 65 MV/m @ 100 Hz
<Eacc> = 23 MV/m @ 1 kHz
6 MW, 1.5 µs,
1 kHz
Canon E37113
SLED
MODE CONVERTER
MODE CONVERTER
CIRCULAR WAVEGUIDE
MODULATOR HALL
LINAC HALL
CPI VKX-8311A
RF smart combiner / switch
50 MW, 1.5 µs,
100 Hz
new CPI high rep rate kly
This study is very rough and need to be continued more rigorously, but we need:
more precise requests and specifications by FEL users
more technical data from klystron producer
more experimental data from existing power plants (high rep rate tests @ X boxes?)
maybe new creative ideas to better exploit the existing hardware …
3
S. Gallo

## Slide 4
Module layout of XLS?
Acc-Structure
Quad
Splitter
PC
Klystron/Modulator
103 cm
45 cm
Acc-Structure
Acc-Structure
…
Sector valve
30 cm
6 cm
Conn+
DN40PP
BPM
Corrector
25 cm
25 cm
103 cm
Mode converters
+ circular WG
M. Aicheler

## Slide 5
C. Rossi

## Slide 7
Thank you!
CompactLight is funded by the European Union’s Horizon2020 research and innovation programme under Grant Agreement No. 777431.
CompactLight@elettra.eu www.CompactLight.eu