## Slide 1: Possibility to suppress the installation of MS in Q10 in IR1 & 5
F. Plassard, R. De Maria
Thanks to: X. Buffat, S. Fartoukh, M. Giovannozzi,
S. Kostoglou, E. Maclean, T. Persson, F. Van der Veken
WP2 Meeting 19/03/2019

## Slide 2
Introduction
The HL-LHC foreseen the installation of an additional sextupole at Q10, named MS10 on each side of the IP 1 & 5 in order to preserve the DA (Baseline optics).
Alternative optics have been optimized without MS10 and their performances were addressed.
Baseline
No MS10
No MS14F
No MS14F MS14D
Additional MS10 in IR1&5
LHC configuration
No MS10 and no MS14F
+ MS12D to IP
No MS10, no MS14F and no MS14D
Disp. Corr. Bumps
Option 1
Disp. Corr. Bumps
Option 2
New Δ IP1-5
Same ATS factor
Larger ATS factor
All the simulations performed on the HL-LHCv1.4 optics, = 15 cm without Beam-beam and on Beam 1

## Slide 3
Baseline optics
MS10F
MS10D
The additional MS10 in each side of IP1&5 restore an even number of sextupoles allowing the cancellation of geometrical aberrations
Arcs | Circuit (strong)
B1: 81, 45 | SF1 (10), SD2 (12)
B2: 81, 45 | SF1 (10), SD2 (12)
B1: 12, 56 | SF1 (10), SD2 (12)
B2: 12, 56 | SF1 (10), SD2 (12)
IP5
IP1

## Slide 4
Observations: No MS10 optics
Arcs | Circuit (strong)
B1: 81, 45 | SF1 (9), SD2 (12)
B2: 81, 45 | SF1 (10), SD2 (11)
B1: 12, 56 | SF1 (10), SD2 (11)
B2: 12, 56 | SF1 (9), SD2 (12)
Odd number of sextupoles on each side of IP1&5
Less compensation of the sextupole geometrical aberrations
No MS10: Same sextupole configuration as in LHC
IP1-5 (B1)
9 SF
11 SD

## Slide 5
Observations: No MS10 optics
Very large geometric aberrations from MS scaling with ATS factors:

## Slide 6
Observations: No MS10 optics
Very large geometric aberrations from MS scaling with ATS factors:
RDTs computed from PTC, with orbit bumps
MO = 0 A
MO = -570 A

## Slide 7
Observations: No MS10 optics
Lower DA than Baseline:
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 8
Observations: No MS10 optics
Lower DA than Baseline:
xing = 295 rad, = 62.31 / = 60.32, = 2.7, with imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 9
Observations: No MS10 optics
Lower DA than Baseline in all possible cases:
 | Off-momentum (= 2.7) |  |  |  |  | On-momentum (=0) |  |  | 
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
DA simulations performed without imperfections, on/off momentum, with/without octupoles and orbit bumps for the dispersion correction.
Large decrease of DA for on-momentum beam showing a clear impact of the geometrical aberrations

## Slide 10
Observations: No MS14F optics
New phases in IR1 & 5 : = -
12 strong defocusing & 11 local defocusing sextupoles
Arcs | Circuit (strong)
B1: 81, 45 | SF1 (8), SD2 (12)
B2: 81, 45 | SF1 (10), SD2 (12)
B1: 12, 56 | SF1 (10), SD2 (12)
B2: 12, 56 | SF1 (8), SD2 (12)
No additional sextupole and MS14F disconnected (in 81 & 45)
Change of phase and optics rematch (in 12 & 56)
Even number of strong sextupoles on each side of IP1&5  geom. aberr. Cancellation
Orbit and dispersion correction knobs have been modified accordingly
(see backup slides)
No MS14F
No MS10F
No MS10D

## Slide 11
Observations: No MS14F optics
Disp. Corr. Bumps Option 1
Larger β-beating than Baseline due to the orbit bumps
Same β-beating than Baseline
Disp. Corr. Bumps Option 2
No MS14F
No MS14F
Only option 2 optics is considered in the following simulations

## Slide 12
Observations: No MS14F optics
Good cancellation of geometric aberrations (comparable to Baseline)

## Slide 13
Observations: No MS14F optics
Some octupolar RDTs were not properly compensated (No MS14F optics)

## Slide 14
Observations: No MS14F optics
Some octupolar RDTs were not properly compensated (No MS14F optics)
Fine tuning on the IP1-5 phase to correct these aberrations  No MS14F New Δ IP1-5 optics

## Slide 15
Observations: No MS14F optics
Optimizing the IP1-5 phase for the no MS14F optics increase DA by 0.4 σ but there still 2.1 σ DA reduction w.r.t Baseline
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 16
Observations: No MS14F optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles
Optimizing the IP1-5 phase for the no MS14F optics increase DA by 0.3 σ but there still 1.8 σ DA reduction w.r.t Baseline

## Slide 17
Observations: No MS14F optics
 | Off-momentum (= 2.7) |  |  |  |  | On-momentum (=0) |  |  | 
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
No MS14F (diff w.r.t Baseline) | 18.8 (-25%) | 21.7 (-24%) | 9.5 (-21%) | 13.5 (-6%) |  | 25.8 (-19%) | 37.7 (-3%) | 12.3 (-20%) | 16.9 (-10%)
No MS14F New IP15 (diff w.r.t Baseline) | 18.1 (-27%) | 20.5 (-28%) | 9.9 (-18%) | 14.2 (-1%) |  | 23.9 (-25%) | 30.2 (-22%) | 13.1 (-15%) | 18.1 (-4%)
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
No MS14F (diff w.r.t Baseline) | 18.8 (-25%) | 21.7 (-24%) | 9.5 (-21%) | 13.5 (-6%) |  | 25.8 (-19%) | 37.7 (-3%) | 12.3 (-20%) | 16.9 (-10%)
 | 18.1 (-27%) | 20.5 (-28%) | 9.9 (-18%) | 14.2 (-1%) |  | 23.9 (-25%) | 30.2 (-22%) | 13.1 (-15%) | 18.1 (-4%)
Decrease of DA w.r.t Baseline for off and on-momentum beams when the orbit bumps are ON
With octupoles ON and disp. corr OFF  similar DA for ON/OFF momentum
With octupoles ON and disp. corr ON  DA reduction for ON/OFF momentum
Stronger feed-down at the octupoles for the No MS14F optics?

## Slide 18
Observations: No MS14F optics
MO = 0 A
MO = -570 A
No larger RDTs feed-down from octupoles and dispersion correction compared to the Baseline

## Slide 19
Observations: No MS14F optics
Larger amplitude detuning at same octupole current (10 σ, disp. corr ON)
Can be explained by the larger at the Strong sextupole and at the octupoles induced by the vert. phase change in 12 and 56
(On-momentum footprints)

## Slide 20
Observations: No MS14F optics
Larger amplitude detuning at same octupole current (10 σ, disp. corr ON)
Can be explained by the larger at the Strong sextupole and at the octupoles induced by the vert. phase change in 12 and 56
(On-momentum footprints)

## Slide 21
Observations: No MS14F optics
Smaller from MO
Larger cross term amplitude detuning from MO and sextupoles
The difference of the terms and comes from the larger at the Strong sextupole and at the octupoles induced by the vert. phase change in 12 and 56
Without orbit bumps for dispersion correction

## Slide 22
Observations: No MS14F optics
Smaller from MO
Larger amplitude detuning and from MO
The feed-down to sextupole from MOs tends to compensate the octupole contribution to the amplitude detuning
Smaller compensation on for the no MS14F optics
With orbit bumps for dispersion correction

## Slide 23
Past MS14F optics DA simulations (HL-LHCv1.3)
Courtesy of R. De Maria and D. Pellegrini
    Previous DA studies show that the No MS14F optics (HLLHCv1.3 optics) miss the DA target of 6σ by about 0.5 σ

## Slide 24
Observations: No MS14F MS14D optics
Arcs | Circuit (strong)
B1: 81, 45 | SF1 (8), SD2 (12)
B2: 81, 45 | SF1 (10), SD2 (12)
B1: 12, 56 | SF1 (10), SD2 (10)
B2: 12, 56 | SF1 (8), SD2 (10)
No change in phases & even number of sextupoles
Requires an increase of ~20% of the sextupole strength for chromaticity correction
Strong family strength in IR15 kept constant and weak sextupoles family strength increased in 23, 34, 67, 78
Option 1: Same ATS factor
No MS14F
No MS14D
IP1-5

## Slide 25
Observations: No MS14F MS14D optics
ATS squeeze starts at = 60 cm (instead of 50 cm for option 1)
Option 2: Larger ATS factor
Peak at SD increased by 20% from option 1 to 2
Same sextupole strength as for the Baseline for chromaticity correction
Option 2 allows to restore minimization of off-momentum beta-beating
IP1-5
IP3
IP5
IP7
IP1
IP3
IP5
IP7
IP1
IP3
IP5
IP7
IP1

## Slide 26
Observations: No MS14F MS14D optics
MO = 0 A
MO = -570 A
Good correction of the sextupole RDTs for both options without MS14F&D w.r.t the Baseline

## Slide 27
Observations: No MS14F optics
Similar footprint w.r.t the Baseline with Octupoles (with same ATS factor)
(On-momentum footprints)

## Slide 28
Observations: No MS14F optics
Similar footprint w.r.t the Baseline with Octupoles (with same ATS factor)
(On-momentum footprints)

## Slide 29
Observations: No MS14F optics
Larger footprint w.r.t the Baseline with Octupoles (with same octupole current)
(On-momentum footprints)

## Slide 30
Observations: No MS14F MS14D optics
For the No MS14F & MS14D optics with larger ATS factor, the DA has been computed for similar amplitude detuning by reducing the octupole strengths by 20% (MO = -456 A)

## Slide 31
Observations: No MS14F optics
Similar footprints (with MO=-456 A for the larger ATS factor optics)
(On-momentum footprints)

## Slide 32
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570/-456 A, turns, 60 angles
Difference of -0.4σ for Option 1 and -0.5σ for Option 2 (with same amplitude detuning) w.r.t to Baseline

## Slide 33
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, with imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570/-456 A, turns, 60 angles
Difference of -0.7σ for Option 1 and -0.5σ for Option 2 (with same amplitude detuning) w.r.t to Baseline

## Slide 34
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 35
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, with imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 36
Conclusions
No MS10 optics results in strong DA degradation due to the large sextupolar geometrical aberrations  difference of -3.4σ w.r.t Baseline  not advisable
Baseline optics (+MS10) gives in overall the best performances
No MS14F optics :
  Good correction of the geometrical aberrations
  Larger at octupoles and strong sextupoles due to the change of phase Δ in IR1-5
  Larger footprint with and without octupoles (larger and )
  Smaller DA w.r.t Baseline for ON & OFF momentum beams  geometrical effect
  Difference of -1.8 σ w.r.t Baseline
No MS14F & MS14D optics :
  No change of vertical phase advance  same linear optics as Baseline
  Good correction of the geometrical aberrations
  20% increase of the sextupole strength if same ATS factor and larger off-momentum beta-beating
  Same sextupole strengths with 1.2 larger ATS factor and same off-momentum beta-beating as Baseline; implications on IR6 optics, collimation performance and machine protection that are yet to be quantified
  For same ATS factor as Baseline: difference of -0.7 σ w.r.t Baseline
  For Larger ATS factor and similar amplitude detuning: difference of -0.5 σ
The No MS14F&MS14D optics is the best alternative to the MS10 at this stage of the study but beam-beam needs to be included to conclude on the best option

## Slide 37
Further studies
Include beam-beam effects in the DA simulations: crucial to evaluate the best design
    Previous DA studies show that the No MS14F optics (HLLHCv1.3 optics) miss the DA target of 6σ by about 0.5 σ
    Should be better for the No MS14F&MS14D optics  to be checked
Does the DA behavior similar among the different optics for Beam 2?
    First DA results shows a quiet important difference between B1 & B2  needs to be understood
Does the DA behavior similar among the different optics for Flat optics?
    Simulations ongoing

## Slide 38
BACKUP

## Slide 39
DA summary table (no imperfections)
 | Off-momentum (= 2.7) |  |  |  |  | On-momentum (=0) |  |  | 
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
No MS14F (diff w.r.t Baseline) | 18.8 (-25%) | 21.7 (-24%) | 9.5 (-21%) | 13.5 (-6%) |  | 25.8 (-19%) | 37.7 (-3%) | 12.3 (-20%) | 16.9 (-10%)
No MS14F New IP15 (diff w.r.t Baseline) | 18.1 (-27%) | 20.5 (-28%) | 9.9 (-18%) | 14.2 (-1%) |  | 23.9 (-25%) | 30.2 (-22%) | 13.1 (-15%) | 18.1 (-4%)
No MS14F&MS14D (diff w.r.t Baseline) | 22.6 (-9%) | 29.5 (+4%) | 11.6 (-3%) | 14.8 (+3%) |  | 29.8 (-7%) | 41.6 (+7%) | 15.1 (-2%) | 18.9 (0.5%)
No MS14F&MS14D Larger ATS factor (diff w.r.t Baseline) | 20.0 (-20%) | 25.7 (-10%) | 10.2 (-15%) | 12.6 (-12%) |  | 27.2 (-15%) | 38.1 (-2%) | 13.1 (-15%) | 16.0 (-15%)
MO strength | 0 A |  | -570 A |  |  | 0 A |  | -570 A | 
Dispersion correction | ON | OFF | ON | OFF |  | ON | OFF | ON | OFF
Avg. DA [σ] Baseline | 24.9 | 28.4 | 12.0 | 14.4 |  | 32.0 | 38.8 | 15.4 | 18.8
No MS10 (diff w.r.t Baseline) | 11.3 (-55%) | 12.4 (-56%) | 8.7 (-28%) | 11.9 (-17%) |  | 15.8 (-51%) | 17.5 (-55%) | 12.6 (-18%) | 15.6 (-17%)
No MS14F (diff w.r.t Baseline) | 18.8 (-25%) | 21.7 (-24%) | 9.5 (-21%) | 13.5 (-6%) |  | 25.8 (-19%) | 37.7 (-3%) | 12.3 (-20%) | 16.9 (-10%)
 | 18.1 (-27%) | 20.5 (-28%) | 9.9 (-18%) | 14.2 (-1%) |  | 23.9 (-25%) | 30.2 (-22%) | 13.1 (-15%) | 18.1 (-4%)
No MS14F&MS14D (diff w.r.t Baseline) | 22.6 (-9%) | 29.5 (+4%) | 11.6 (-3%) | 14.8 (+3%) |  | 29.8 (-7%) | 41.6 (+7%) | 15.1 (-2%) | 18.9 (0.5%)
No MS14F&MS14D Larger ATS factor (diff w.r.t Baseline) | 20.0 (-20%) | 25.7 (-10%) | 10.2 (-15%) | 12.6 (-12%) |  | 27.2 (-15%) | 38.1 (-2%) | 13.1 (-15%) | 16.0 (-15%)
xing = 295 rad, = 62.31 / = 60.32, without imperfections,
Q’=15, turns, 60 angles

## Slide 40
DA summary table (with imperfections)
 | Off-momentum (= 2.7) | 
MO strength | 0 A | -570 A
Avg. DA [σ] Baseline | 11.2 | 11.3
No MS10 (diff w.r.t Baseline) | 8.9 (-21%) | 7.9 (-30%)
No MS14F (diff w.r.t Baseline) | 11.1 (-1%) | 9.2 (-19%)
No MS14F New IP15 (diff w.r.t Baseline) | 10.6 (-5%) | 9.5 (-16%)
No MS14F&MS14D (diff w.r.t Baseline) | 10.9 (-3%) | 10.6 (-6%)
No MS14F&MS14D Larger ATS factor (diff w.r.t Baseline) | - | 9.4 (-17%)
MO strength | 0 A | -570 A
Avg. DA [σ] Baseline | 11.2 | 11.3
No MS10 (diff w.r.t Baseline) | 8.9 (-21%) | 7.9 (-30%)
No MS14F (diff w.r.t Baseline) | 11.1 (-1%) | 9.2 (-19%)
 | 10.6 (-5%) | 9.5 (-16%)
No MS14F&MS14D (diff w.r.t Baseline) | 10.9 (-3%) | 10.6 (-6%)
No MS14F&MS14D Larger ATS factor (diff w.r.t Baseline) | - | 9.4 (-17%)
xing = 295 rad, = 62.31 / = 60.32, = 2.7, with imperfections,
with dispersion correction, Q’=15, turns, 60 angles

## Slide 41
Tunes vs (MO = 0 A)

## Slide 42
Tunes vs (MO = -570 A)

## Slide 43
dispersion correction before DA calculation
Baseline
No MS14F
For both optics configurations the orbit and dispersion are well corrected in the mask files before sixtrack DA calculations

## Slide 44
Orbit correction before DA calculation
Baseline
No MS14F

## Slide 45
Observations: Baseline optics
(OFF-momentum FMA)

## Slide 46
Observations: No MS10 optics
(OFF-momentum FMA)

## Slide 47
Observations: No MS14F optics
(OFF-momentum FMA)

## Slide 48
Observations: No MS14F MS14D optics
(OFF-momentum FMA)

## Slide 49
Observations: No MS14F MS14D optics
(Larger ATS factor)
(OFF-momentum FMA)

## Slide 50
FMA (no imperfections, MO=-570 A, disp. corr., 6σ)
(OFF-momentum FMA)

## Slide 51
FMA (no imperfections, MO=-570 A, disp. corr., 10σ)
(OFF-momentum FMA)

## Slide 52
Footprint (no imperfections, MO= 0A, disp. corr., 10σ)
(ON-momentum footprints)

## Slide 53
Footprint (no imperfections, MO= -570A, disp. corr., 10σ)
(ON-momentum footprints)

## Slide 54
Amplitude detuning from octupoles
No change of in IR1&5:
Same term
Change of in IR1&5:
Smaller term
Due to the change of in IR1&5 there is larger product of at the octupoles:
Larger cross term

## Slide 55
Larger at Sextupoles and Octupoles
for No MS14F

## Slide 56
Amplitude detuning vs DA (no imperfections)
 | δQx/δεx (diff. w.r.t Baseline) (w/o CA) (w. CA) [m-1] | δQy/δεy (diff. w.r.t Baseline) (w/o CA) (w. CA) [m-1] | δQx/δεy (diff. w.r.t Baseline) (w/o CA) (w. CA) [m-1] | DA (dp/p≠0) (diff. w.r.t Baseline) (w/o CA) (w. CA) | DA (dp/p=0) (diff. w.r.t Baseline) (w/o CA) (w. CA)
Baseline | -4.50e5 -3.57e5 | -4.57e5 -3.32e5 | 1.63e5 1.70e5 | 14.4 12.0 | 18.8 15.4
No MS14F (new phase) | -4.51e5 (+0.22%) -4.08e5 (+14.3%) | -4.11e5 (-11.2%) -3.11e5 (-6.8%) | 1.80e5 (+10.43%) 1.83e5 (+7.6%) | 14.2 (-1.41%) 9.9 (-21.2%) | 18.1 (-3.9%) 13.1 (-17.6%)
No MS14F & MS14D | -4.54e5 (+0.9%) -3.92e5 (+9.8%) | -4.58e5 (+0.22%) -3.40e5 (+2.4%) | 1.65e5 (+1.23%) 1.62e5 (-4.94%) | 14.8 (+2.8%) 11.6 (-3.5%) | 18.9 (+0.5%) 15.1 (-2.0%)
 | δQx/δεx (diff. w.r.t Baseline) (w/o disp. corr.) (w. disp. corr) [m-1] | δQy/δεy (diff. w.r.t Baseline) (w/o disp. corr.) (w. disp. corr) [m-1] | δQx/δεy (diff. w.r.t Baseline) (w/o disp. corr.) (w. disp. corr) [m-1] | DA (dp/p≠0) (diff. w.r.t Baseline) (w/o disp. corr.) (w. disp. corr) | DA (dp/p=0) (diff. w.r.t Baseline) (w/o disp. corr.) (w. disp. corr)
Baseline | 2.50e4 2.49e4 | 2.08e4 2.05e4 | -4.12e4 -4.19e4 | 28.4 24.9 | 38.8 32.0
No MS14F (new phase) | 2.68e4 (+7.2%) 2.87e4 (+15.3%) | 2.97e4 (+42.8%) 2.97e4 (+44.9%) | -4.60e4 (+11.7%) -4.48e4 (+7%) | 20.5 (-38.5%) 18.1 (-37.6%) | 30.2 (-28.5%) 23.9 (-33.4%)
No MS14F & MS14D | 2.15e4 (-16.3%) 2.23e4 (-11.7%) | 1.98e4 (-5%) 1.99e4 (-3%) | -3.88e4 (-6.2%) -3.71e4 (-12.9%) | 29.5 (+3.9%) 22.6 (-10.2%) | 41.6 (+7.2%) 29.8 (-7.4%)
MO = 0 A
MO = -570 A

## Slide 57
Second order Amplitude detuning
No dispersion correction
With dispersion correction

## Slide 58
Second order Amplitude detuning
No dispersion correction
With dispersion correction

## Slide 59
DA vs MO strength
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, turns, 60 angles
DA vs MO strength computed with steps of 100 A
All optics shows a significant increase of DA for MO strength of around -100 A

## Slide 60
DA vs MO strength
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, turns, 60 angles
DA vs MO strength computed with steps of 100 A
All optics shows a significant increase of DA for MO strength of around -100 A

## Slide 61
Second Order Chromaticity
No dispersion correction
With dispersion correction

## Slide 62
Off-momentum detuning with amplitude
No dispersion correction
With dispersion correction

## Slide 63
Off-momentum detuning with amplitude
No dispersion correction
With dispersion correction

## Slide 64
Chromatic sextupole RDTs (MO = 0 A)
No dispersion correction
With dispersion correction

## Slide 65
Chromatic sextupole RDTs (MO = -570 A)
No dispersion correction
With dispersion correction

## Slide 66
Chromatic coupling
Larger chromatic coupling () contribution for both options of the no MS14F optics compared to all other optics
The contribution arises with the dispersion correction bumps, with and without octupoles
Lower average linear coupling amplitude for both No MS14F optics

## Slide 67
Chromatic octupole RDTs (MO = 0 A)
No dispersion correction
With dispersion correction

## Slide 68
Chromatic octupole RDTs (MO = -570 A)
No dispersion correction
With dispersion correction

## Slide 69
DA on B2
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 70
DA on B2
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 71
DA on B2
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles

## Slide 72
DA on B2
For B2 the Baseline does no longer show the best DA
Need to understand the DA difference between B1 & B2

## Slide 73
Observations: No MS14F MS14D optics
For the Larger ATS factor option the larger at the octupoles increases the amplitude detuning terms

## Slide 74
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles
Difference of -0.4σ for Option 1 and -1.8 σ for Option 2 (with same octupole strength) w.r.t to Baseline

## Slide 75
Observations: No MS14F MS14D optics
xing = 295 rad, = 62.31 / = 60.32, = 2.7, without imperfections,
with dispersion correction, Q’=15, Laudau octupoles MO = -570 A, turns, 60 angles
Difference of -0.6σ for Option 1 and -1.9 σ for Option 2 (with same octupole strength) w.r.t to Baseline

## Slide 76
Observations: No MS14F MS14D optics
Good correction of the octupole RDTs for both options without MS14F&D w.r.t the Baseline
MO = 0 A
MO = -570 A