Transverse phase space observations
L. Ponce for the commissioning team

---
Content
Tune observations and corrections
Tune parameters and quad current
Working points tests
Coupling compensation with and without e-cooler magnetic system
Orbit measurement and kick response

---
Working point/tune measurement
Choice of the working point (Qh/Qv) to sit in “resonnance free” zone
Tunes parameters defined at the beginning of the year as a interpolation of a set of (Qh,Qv, I_QFND,I_QFNS,I_QDND) along the diagonal (simulated adding constraints on dispersion in electron cooler and max on beta function
Simulation from L. Bojtar
MADX Model

---
Tune knobs
Programmed tunes 2.42/1.42,
Mesured 2.42/1.44 OK → Qv seems to be off by 0.02
Test 1st June at injection

---
Tune knobs at 100 keV
 11st July at 100 KeV
Programmed tunes 2.35/1.455
Mesured seems to be 2.425/1.45 → Qh is really OFF

---
Tune trim @ 35MeV/c
Measured tunes: requested -0.01 on Qh, strong coupling, Qh visible in V plane → measured tune is following in relative

---
Tune trim @ 100 keV/c
Measured tunes before and after having decreased Qh and Qv on last plateau → again in relative OK

---
Tune measurement
Ok to trim Qh/Qv in 𖨬, but
Discrepency between measured tune values and programmed one increasing with momemtum decreasing:
Cannot adjust tune values with the QH/QV parameters on last plateau (due to missing interpolation values)
Need to change directly currents in the 3 Quad families:
+𖨬QFNS <=> +𖨬Qh
+𖨬QDND <=> +𖨬Qv
+𖨬QFND <=> -𖨬Qh AND +𖨬Qv
Beginning of 2nd ramp

---
First ramp
13th June 2018

---
Coupling compensation
1st of June at injection:
WP 2.40/1.43
1st method (very lenghty): Trying to bring Qh/Qv with Tune knobs on top of each other by trimming skew quads
Measured tunes with QSK35 at -1.5A : Qh/QV=0.445/0.45
Programmed values 0.447/0.44
Faster but dirty method: look at the H tune signal in V plane

---
Effect of Skew quads
QSK40 switch ON to 0.8 A at injection

---
More knobs for coupling compensation
Change of current on SOLCOMP
Change of current in QFND
9th July

---
Methodology
Based on Tune measurement, changing Quad current on the plateaus to set the desired working points:
Different WPs tried (see next 3 slides)
To correct tunes along the ramp, used AD method: add intermediate plateau to correct along the ramp
Measure tunes/orbit and look at coupling on new plateaus
Switch ON of e-cooler magnetic system during the optimization process → need to also compensate for solenoid
We’ve been quite systematic for the first ramp → but already middle of July

---
15st June
Working point Qh= 2.43/Qv= 1.45

---
11st July
New working point: Qh decreased to 2.38 along the cycle

---
Test with all QUAD OFF
Test of cycle with main quad OFF (20th July): tune measurement at injection give Qh~0.15, Qv~ 0.25
Transmission with Quad back ON for comparison

---
E-cooler magnetic system ON
Orbit corrected to reference with Kyotostyle corrector at -6A (measurement at injection)
Polarity of e-cooler OK
Comparison of transmission with e-cooler magnetic system ON (kyoto at -6A), DHZ05 and DHZ60 with constant offset and solenoid compensator ON at 10.04A
E-cool mag OFF

---
E-cool compensation (injection)
ESOLCOMP=8A
ESOLCOMP=4A
ESOLCOMP=12A
Tune measurement till intermediate plateau for different current values in the solenoid compensator

---
E-cool compensation (intermediate)
ESOLCOMP=6A
ESOLCOMP=8A
ESOLCOMP=10A
ESOLCOMP=12A
Tunes at injection with ESOLCOMP = 11 A:

---
Effect of e-cooler magnetic system
E-cooler magnetic system ON
E-cooler magnetic system OFF
@Intermediate plateau
E-cool OFF
@Injection
E-cool ON

---
Tune Adjustment June-July
First ramp starts at C=3600 to C=6300
First ramp
First ramp

---
Corresponding transmission

---
Losses along the second ramp

---
What we tried
Optimization of the working point :
All cycle changed: 0.38/0.44, 0.41/0.45, 0.44/0.38
Trying keeping K constant, changing with energy, keeping measured tunes values cosntant
Best working point for good transmission is an hybrid
Changed ramp length, rounding length
Added intermediate plateaus to optimized tunes/coupling/orbit all along the ramp
Extra points introduced finally removed →losses still there
Also many tests with radial loop (Better to ask Davide for reporting)
Start of loss is changed, but loss still there
Many attempts/data to be analysed

---
Adding intermediate plateau
Adding a plateau at 22.99 MeV to measure and correct tune/orbit
Intermediate plateau at 22.99 MeV
Intermediate plateau at 24 MeV
End of ramp
Beginning of ramp

---
13 July: second ramp
Adding a plateau at 26 MeV to measure and correct tune/orbit coupling
Comparison of transmission just adding the plateau (White trace is the cycle without the plateau)

---
Adding Plateau(s) ~ 19 MeV
 Suspect e-cooler timing not following the change of cycle length → e-beam ON during deceleration?
← Bad shot from AD show less losses during the ramp?

---
Effect of ramp length
Comparison of transmission with shortened and longer ramp time
Test done for working point Qh/Qv = 0.38/0.44 on last plateau
Test of rounding time also done
=> No clear improvement in these conditions
Shorten ramp (-1s)
Longer ramp (+1s)

---
Attempt with Qh/QV 0.44/0.42
1h test with only changed QFNS current (coupling not optimized)

---
“Constant” K along cycle
Tune along 2nd ramp
Losses at the time Qh is crossing 0.4

---
“scaled” K along cycle
Tune along 2nd ramp
Losses at the time Qh is crossing 0.4

---
Test 0.45/0.38
Tune crossing along 1st ramp → no loss

---
Comparison
Tunes Qh/Qv = 0.42/0.44
Constant K along cycle
QV changed at 35 MeV

---
Scraper measurements
No evidence of transverse blow-up during the ramp

---
Last setting in November
Qh=0.46
Qv=0.41

---
Injection mis-steering
13th June: change of DHZ35 current → bad injection steering
→ losses start earlier (larger emittance)

---
Intensity effect?
Tune measurement on last plateau for 2 consecutive shots (very low intensity on the left, nominal on the right) (9th July)

---
Test of Sextupoles effect
Sextupoles switched ON with different polarity on the last plateau, transmission not really better but much better tune signal
XFN = -23A
XDN = 45A
Sextupoles OFF

---
Orbit and kick response
Kick response checks done for all orbit correctors to validate sign convention inversion (and check no extra polarity inversion)
All data in e-logbook (14/05/2018)
YASP calibration files updated → orbit correction algorithm validated
Acquired orbit along the cycle, Orbit corrections performed
Corrections incorporation into the ramp function not easy
E-cooler bump and angle scans with YASP
Kick response measurement acquired at injection and ejection plateau

---
Orbits along cycle
Intermediate plateau
Injection
Second ramp
Ejection plateau

---
Orbit evolution in second ramp
After simplication of corrector function (linearization of the ramp in current instead of K)

---
Aloha: Kick response analysis
Standard interface between YASP measurement and MADX
Easy check of data quality
Fitting of parameters using MADX model
Thanks to K. Fuchsberger

---
BPMEC error
4th-6th July : H and V plane inverted for BPMEC.432, but still +/- error in H
Calculated orbit
+1 mm amplitude bump in H
measured orbit
H and V inverted
-1 calibration factor in H

---
Kick response 100 MeV
18 Oct 2018, Injection WP 2.385/1.455
Corresponding currents:
QFND = 22.678A
QDND = 17.642A
QFNS= 4.969A

---
Kick response 100 keV
Allow to exclude correctors 460 V and monitors 520 H (used by radial loop?)

---
Kick response 100 keV
31 Oct 2018, Injection WP 2.37/1.42
Coupling visible → added skew quad in the fit
Fit result not yet convincing
More analysis needed

---
Stability of the machine
10th-11th August: Gbar shifts

---
reproducibility
Comp with one of last meas on 20th July
First cycle after AD-ecooler problem

---
Summary
A lot of work and time invested in transverse plane observations and (empirical) corrections
Investigation of the beam loss during last ramp:
Tried many working points above and bellow diagonal for transmission optimization
Tried changing ramp length, rounding, etc…
Added intermediate plateau for tune/coupling/orbit correction
Orbit measured and corrected all along the cycle:
Model good enough for corrections
Polarity errors identified and software corrected
Good reproducibility and stability of the machine
Due to lack of beam time toward the end of the run, measurements and corrections as systematic as at injection are needed for last part of the cycle