## Slide 2: FCC-hh beam vacuum line interconnections
C. Garion

## Slide 3
Interconnection layout
Requirements:
  End absorber
  Compensation system
Preliminary “conceptual” design
Outline

## Slide 4
Cryostat vacuum vessel
Cold mass
Cold bore
Beam screen
Fixed point Cold mass/ vacuum vessel
Connection beam screen/cold bore
Beam screen bellows
Layout principle
Shielded interconnection bellows
Beam
RF fingers
Cooling tubes
Interconnection absorber
Interconnection absorber

## Slide 5
End absorber requirements
The absorbers are located on the downstream side of the magnet (upstream of the interconnection).
 The two beam vacuum lines are different.
 Shorter free space in the interconnections for the magnet installation.
Beam
Beam
Synchrotron radiation power intercepted by the end absorber is around 41 W.

## Slide 6
Compensation system requirements
The thermal expansion coefficients of the cold masses and the beam screen tube have been assumed equal to those measured in LHC.
 | Beam screen bellows | PIM
Nominal conditions | 8 | 40
Cool down | 32 | -16
Warm-up | -30 | 46
Exceptional 1 | 45 | ~0
Exceptional 2 | -30 | 30
Design value for the bellows | -30/32 | -16/46
The stroke, in mm, of the compensation system has been evaluated for different cooling/warm-up scenarii, validated on LHC string II:
 | Beam screen | Cold mass
Nominal | 40-60 | 1.9
Coold down | 293 | 150
Warm up | 150 | 293
Exceptional 1 | 293 | 70
Exceptional 2 | 150 | 293
Temperature conditions
Bellows stroke
Thermal contractions
15m long cold masses are assumed.

## Slide 7
Preliminary conceptual design
Very first design. Alternatives have to be studied:
Transition and exit of cooling tubes.
RF bridge (deformable or sliding).
Absorber
Transition
Beam screen
RF bridge

## Slide 8
Absorber integration
Contact “ring”
Interface plate
RF contact
Weld cooling tube/absorber

## Slide 9
Preliminary conceptual design
Beam screen bellows
Interconnection bellows
Continuous cooling circuit (no weld in beam vacuum)
Absorber profile to optimize?
?

## Slide 10
Copper Beryllium deformable RF bridge (based on HL-LHC design):
Circular aperture
C17410
0.1 mm thick, 3 mm width, gap: 1.4 mm
3 convolutions
6 titanium G5 springs (total prestress: ~110 N)
Static RF fingers
Longitudinal constraint, due to the finger extension limitation, is reduced thanks to the static RF fingers and the springs.
Operation
Warm up
Spring compression
Expected behaviour and working conditions of the RF bridge
Deformable RF fingers
as installed
in operation
RF bridge
Installation

## Slide 11
Conclusions
A preliminary design of the beam screen extremities and interconnections is proposed.
An end absorber, connected to the cooling tubes, is integrated.
Alternatives and detailed design have to be studied, as well as the thermal heat transfer from the absorber.

## Slide 13
Due to the high SR density at the end of the dipole, an absorber has been designed in order to reduce as much as possible power density in this area.
Thermal analysis
End dipole absorber
Preliminary end absorber design
42 W (Points with about 200 W/cm2)
100 mm
Beam direction
Temperatures in the main absorber below 100 K
Temperature (K)
75
57