## Slide 2: FCC-hh beam screen design
Marco Morrone
Cedric Garion
EuroCirCol WP4 meeting 12
18-19 March 2019
(ALBA Synchrotron)

## Slide 3
Beam screen design
  Recent design evolution at a glance
Mechanical behaviour
  Quench analysis
  Beam screen supports
Thermal behaviour
  Temperature profile due to S.R.
  Heat load to the cold bore by S.R. and the supporting system
Conclusions
Outline
NEW

## Slide 4
Beam screen design
  Recent design evolution at a glance
Mechanical behaviour
  Quench analysis
  Beam screen supports
Thermal behaviour
  Temperature profile due to SR
  Heat load to the cold bore by SR and the supporting system
Conclusions
Outline

## Slide 5
Beam Screen Design
Recent design evolution at a glance
Welding points (0.5 mm wide)
Co-laminated Cu
(thickness 100 μm )
P506 outer shell
(thickness 0.8 mm)
Co-laminated Cu
(thickness 75 μm )
P506 outer shell
(thickness 1 mm)
Welding points (0.5 mm wide)
New welding points (0.5 mm wide)
Edges reduced
(thickness 0.4 mm)
Edges reduced
(thickness 0.4 mm)
Former version
Updated version

## Slide 6
Beam Screen Design
Recent design evolution at a glance
Periodic unit
17 mm
P506
(thickness 1mm) -everywhere-
Cu OFE
(thickness 0.3 mm)
Cu OFE
(thickness 75 μm)
Updated version
12 mm
Saw-tooth profile
R 20.5 mm
28.37 mm
Cooling channel (He at 40K, 50 bar)

## Slide 7
Beam screen design
  Recent design evolution at a glance
Mechanical behaviour
  Quench analysis
  Beam screen supports
Thermal behaviour
  Temperature profile due to SR
  Heat load to the cold bore by SR and the supporting system
Conclusions
Outline

## Slide 8
Mechanical behaviour
Quench analysis
3D simulations have been carried out taking into account the Joule effect coupling with the magnetic field ().
Variation of magnetic field at quench produces currents along the beam screen.
These currents generate Lorentz forces that might endanger the mechanical integrity of the beam screen.
x
z
y
(𝑡)
Courtesy of Daniel Schoerling
(𝑡)
σMAX = 1130 MPa
σy = 1350 MPa @ 40 K

## Slide 9
Beam Screen Design
Beam screen supports
 pre-stress insertion 0.1 mm
beam screen
cold bore
1.5 mm
1.6 mm
21 mm
Beam screen supports
supports
welded on the rings
Welded ring
sliding
ring
Rings welded as two half shells on the BS

## Slide 10
Beam Screen Design
Beam screen supports
Side supports
highly loaded during quench
Cold bore
Updated version: Δx=0.65 mm Fx = 43 kN/m (per half_outer shell)
Former version:Δx=2.7 mm, not 0.9 mm Fx = 61 kN/m (per half_outer shell)
Maximum displacement and force along the horizontal plane during a quench:
Revision of the boundary conditions used to elaborate the results
of the former BS version
5 x magnfication
Deformation of the BS during a magnet quench

## Slide 11
Mechanical behaviour
Beam screen supports
Residual max stress 400 MPa
Residual deformation 20 μm < 100 μm of pre stress
Maximum BS displacement Δx=0.65 mm
Optimisation of the beam screen supports
to withstand a magnet quench with reduced plastic deformation
Support on the horizontal plane

## Slide 12
Mechanical behaviour
Beam screen supports
Vertical displacement: -32 μm
Weight: 2.16 Kg/m

## Slide 13
Beam screen design
  Recent design evolution at a glance
Mechanical behaviour
  Quench analysis
  Beam screen supports
Thermal behaviour
  Temperature profile due to SR
  Heat load to the cold bore by SR and the supporting system
Conclusions
Outline

## Slide 14
Max synchrotron radiation power ~ 42 W/m
Beam intensity: 0.5 A, 50 TeV
Thermal behaviour
Temperature profile due to S.R.
Thermal contacts according to the spot weld pattern
Heat load deposited according to a Gaussian distribution on the saw-teeth
Half beam screen has been modelled due to symmetry

## Slide 15
Thermal behaviour
Temperature profile due to S.R.
Base temperature 40 K

## Slide 16
Thermal behaviour
Temperature profile due to S.R.
Base temperature 57 K

## Slide 17
Thermal behaviour
Heat load to the cold bore [mW/m]
The contact area (0.01 mm2 ) according to the Hertzian theory.
Heat

## Slide 18
Thermal behaviour
Heat load to the cold bore by S.R.
Heat to the cold bore:
2.95 mW/m
@ base temperature of 40 K
Heat to the cold bore:
8.84 mW/m
@ base temperature of 57 K

## Slide 19: Summary of the heat loads @ 57 K (worst case scenario)
< of the threshold of 300 mW/m!

## Slide 20
Beam screen design
  Recent design evolution at a glance
Mechanical behaviour
  Quench analysis
  Beam screen supports
Thermal behaviour
  Temperature profile due to SR
  Heat load to the cold bore by SR and the supporting system
Conclusions
Outline

## Slide 21
Conclusions
Beam screen design
The thickness of the P506 outer shell has been increased to 1 mm (from 0.8 mm) while its copper thickness has been reduced to 75 μm (from 100 μm). Two welding points have been added on the outer shell. The outer diameter of the beam screen remains unchanged, i.e. 41 mm.
Thermal behaviour
The synchrotron radiation heat load leads to a maximum temperature of 81 K.
The highest heat load to the cold bore due to SR is 8.9 mW/m.
The highest heat load to the cold bore through the supporting system is 67.7 mW/m.
Mechanical behaviour
During a magnet quench, the mechanical behaviour of the beam screen remains elastic, the maximum deformation along the horizontal plane is 0.65 mm.
Supports have been designed by to ensure a good alignment of the beam screen while minimizing the permanent deformation due to a quench.

## Slide 22
Future plans
Magnet quench test at 1.9 K.

## Slide 23
Thank you for your attention

## Slide 24
Spare slides

## Slide 25
Mechanical properties
Density, ρ = 8700 (Kg/m3)
Young’s modulus, E = 110 (GPa)
Poisson’s ratio, ν = 0.35
Magnetic properties
Relative permittivity, ε = 1
Relative permeability, μ = 1
Resistivity changes with temperature
Thermal properties
Thermal conductivity, k = 700 (W/(m·K))
Heat capacity changes with temperature
Coefficient thermal expansion, α = 17E-6 (1/K)
Copper
Mechanical properties
Density, ρ = 7850 (Kg/m3)
Young’s modulus, E = 205 (GPa)
Poisson’s ratio, ν = 0.28
Magnetic properties
Relative permittivity, ε = 1
Relative permeability, μ = 1
Resistivity, ρ = 5E-7 (Ω·m)*
Thermal properties
Thermal conductivity, k = 5 (W/(m·K))
Heat capacity changes with temperature
Coefficient thermal expansion, α = 12.3E-6 (1/K)
P506 (high-Mn high-N austenitic stainless steel)
* Due to the high value of stainless steel resistivity, and its small variation with temperature, it has been considered constant with temperature.
Mechanical Design
Material properties

## Slide 26
Thermal behaviour
Temperature profile due to S.R.
The contact area between the elastic ﬁnger and the cold bore has been calculated according to the Hertzian theory of
non-adhesive elastic contact [32]. Such area turns out to
be 0.01 mm2 and it has been used to dimension a cylin-
drical element 0.1 µm