## Slide 1: Preliminary results from crystal collimation studies in 2018
M. D’Andrea, D. Mirarchi, S. Redaelli, R. Rossi, W. Scandale
HL-LHC Technical Coordination Committee meeting, 14th March 2019, CERN
Acknowledgments:
UA9 Collaboration that provided the crystals installed in the LHC
R. Losito (EN), S. Gilardoni, M. Calviani, I. Lamas (EN-STI), A. Masi, M. Di Castro, M. Butcher, P. Serrano, C. Dionisio (EN-SMM) that provided hardware and controls of LHC goniometers

## Slide 2: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook
With materials previously shown by D. Mirarchi at
International Review of the HL-LHC Collimation System

## Slide 3: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook

## Slide 4: Planar channeling
Potential between a particle and an atom described by the Thomas-Fermi model:
Continuous approximation (small ):
Potential seen by protons
from crystalline planes
Forced to oscillate in a relatively empty space
If the protons have pT < Umax
Typical values at energies
of our interest:
Critical channeling angle

## Slide 5: LHC Collimation
Circulating
beam
Primary halo
Cold magnets
Cold magnets
Warm magnets
Protection
Devices
(TCD)
Secondary halo
Tertiary halo
+ hadronic shower
Primary
Collimators
(TCP)
Secondary
Collimators
(TCSG)
Absorbers
(TCLA)
Tertiary
Collimators
(TCT)
Bottleneck
IP
Arc
Insertion
Secondary halo
+ hadronic shower & Dechanneling
Deflected halo
Massive Absorber
Bent crystal
Circulating
beam
Primary halo
IP
Arc
Insertion
Main limitations:
Single diffractive events
Small deflection
Non-negligible δp/p
Protons collimation:
Lead ions collimation:
Fragmentation and dissociation
Cleaning efficiency reduced to 10-2 (10-4 with protons)
Main promises:
Similar performance with p and Pb
Reduction of inelastic interactions
Reduced off-momentum losses in DS
Significant improvement w.r.t. present

## Slide 6: Present layout
Four crystals installed in the LHC: two per beam, one per plane
Complete layout to allow thorough investigations and operational tests
Same specifications for all crystals, two different producers and technologies
S. Redaelli
Beam 1
Beam 1
TCPCH.A4L7.B1
TCPCV.A6L7.B1
Beam 1
Beam 1
Beam 1
TCPCV.A6R7.B2
TCPCH.A5R7.B2
Beam 2
Beam 2
Pics. Courtesy of Y. Gavrikov
INFN-Fe
PNPI
PNPI
PNPI
Strip
Strip
QM
QM

## Slide 7: Milestones achieved
2015
First p channeling at the LHC: 450 GeV and 6.5 TeV
First Pb channeling at the LHC: 450 Z GeV
First channeling during energy ramp
First assessment of cleaning performance with p beams
First Pb channeling at the LHC: 6.5 Z TeV
Demonstration of improved cleaning for protons
2016
First channeling of Xe at 450 Z GeV 6.5 Z TeV, together with assessment of cleaning performance
2017
First channeling during squeeze and collision
First operational use in a physics run
Operational tests with ions: crystals part of intensity ramp up
Demonstration of improved cleaning for ions
2018
Total MD time: 58h with p, 34h with ions

## Slide 8: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook

## Slide 9: Angular scan
The crystal device is aligned to the beam halo and rotates around its axis
What we look at:
decreased losses at the crystal
increased losses at the absorber
What we look for:
optimal channeling orientation
reduction factor
Background subtracted, normalization to lost particles flux and amorphous level
AM
AM
VR
CH
Notes: Method used to establish channeling: crystal orientation changed with respect to beam direction (after beam based alignment -> crystal is primary)
In channeling orientation nuclear interactions in the crystal are reduced: we look for a reduction in losses at the crystal
Consequently, losses increase at the collimator used as absorber, which catches the channeled beam
After normalizing the signal at the crystal for the beam flux, familiar angular scan shape is reconstructed: amorphous, volume reflection, channeling
This allows to find optimal channeling orientation and losses reduction factor

## Slide 10: Linear scan
The absorber is retracted and inserted until it touches the primary beam, with the crystal in channeling orientation
Primary Beam
What we look at:
losses at the absorber as a function of its transverse position
What we look for:
multiturn channeling efficiency
characterization of channeled beam and crystal bending angle
After normalization to losses when the primary beam is touched, the height of the error function gives directly the efficiency
Distance between channeled and primary beam is converted into deflection angle using the transfer matrix
Notes: Crystal is left in channeling orientation, while the absorber is retracted and then inserted until it touches the beam: it intercepts the whole channeled beam
Losses at the absorber as a function of its transverse position allow to reconstruct the profile of the channeled beam
The profile is fitted with an error function (the integral of a gaussian): after normalization with respect to losses when the primary beam is touched allows to find the channeling efficiency
The derivative of the fitted profile is the channeled beam gaussian: distance between the mean value of the gaussian and the point where the beam is touched can be converted into deflection with the transfer matrix -> method to check the bending angle of the crystal

## Slide 11: Loss maps
Q12-13
Cold region after collimation insertion is divided in areas corresponding to dispersive peaks
Same procedure used to validate the standard system: the beam is blown up with ADT (transverse white noise) to generate controlled losses around the machine
R. Rossi
β-coll
Dump
δp/p-coll
LHCb
ATLAS
CMS
ALICE
Q12-13
Notes: The beam is blown up with the ADT to generate controlled losses around the machine: standard method used to check collimation hierarchy
This is an example of a B1 loss map with the standard collimation system The area of interest for our discussion is of course IP7, where we can see the usual collimator hierarchy: highest losses at the primary collimator and then showers downstream

## Slide 12: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook

## Slide 13: Angular scans at flat top with protons
B1H
B1V
B2H
B2V
All devices completely characterized in preparation for measurements with ions
Linear scans and loss maps with various settings also performed

## Slide 14: Channeling during energy ramp
Bent crystal
Deflected halo
Massive Absorber
➛ ➛ Beam ➛ ➛
~7 mm
~35 mrad
qc ~ 10mrad
450 GeV
Example of linear and angular functions used to follow adiabatic dumping
qc ~ 2.5 mrad
6.5 TeV

## Slide 15: Channeling during dynamic phases
Channeling conditions assessed by means of continuous loss maps
Observable: ratio of losses at absorber w.r.t. at crystals
CH
<10-2
Cry
Abs
AM
Cry
Abs
MCBs trip
AM
CH
Only B1H in 2016
All 4 crystals in 2018!
R. Rossi
Similar results during squeeze, collapsing separation, orbit corrections
Beam 1
Beam 1
Good control of channeling during dynamic phases achieved!
Ideal system with 2 crystals per plane could accommodate orbit changes better

## Slide 16: First physics run using crystals!
First ever data taking using crystal collimation during high-b* at 450 GeV!
Very challenging conditions for collimation required to suppress background
Both standard and crystal collimation schemes prepared for operations
Fully automated insertion of crystals directly in channeling deployed
Future plans:
High-b* run at intermediate energies may be requested in Run3/HL-LHC
Preference of using crystal collimation scheme during data taking
Feedback from experiments using crystals:
Significant background suppression
No need of scraping during the fill
Better data quality and more integrated lumi!
Standard
Crystal
Courtesy of TOTEM

## Slide 17: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook

## Slide 18: Multiturn CH efficiency at injection for ions
~86%
~78%
~95%
~91%
B1H
B1V
B2H
B2V

## Slide 19: Multiturn CH efficiency at flat top for ions
~82%
~20%
~91%
~84%
Radius close to critical value: high dechanneling population and low efficiency
Smaller radius: much lower dechanneling population and higher efficiency
B1H
B1V
B2H
B2V

## Slide 20
STD
CRY
Normalization to particle flux
Generally cleaner pattern
Std and Cry system comparison

## Slide 21: Operational tests with Pb beams
Adiabatic insertion of crystals in present collimation scheme
Standard system fully in place with crystals placed 0.25s tighter than TCPs
All 4 crystals inserted at top energy during intensity ramp up tests
Maximum stored intensity 648 bunches
Stable channeling kept for 2-3 hours
Constant monitoring of temperature sensors on goniometers
No temperature increase observed
Final assessment on-going by impedance team
Beam loss reduction on highest cold losses, with adiabatic insertion of crystals
D. Mirarchi

## Slide 22
Cleaning gain in operational tests
Up to a factor 10 improvement with operational settings!
Evaluation through ratio of leakage with standard collimation system and crystal collimation system for each region

## Slide 23
Fragments from TCSGs intercepted
Strip
Strip
QM
QM
Higher gain achievable with specific settings!
Detailed studies: only TCLAs moved

## Slide 24
Fragments from crystals and dechanneling intercepted
Strip
Strip
QM
QM
Detailed studies: TCSGs and TCLAs moved
Higher gain achievable with specific settings!

## Slide 25: Outline
Crystal channeling at the LHC
Methods for crystal characterization
Preliminary results with protons
Preliminary results with ions
Conclusions and outlook

## Slide 26: Conclusions and outlook
Main outcomes
Good operational experience achieved in Run2 and first use during physics
Stable channeling during entire cycle demonstrated
Improved cleaning at flat top demonstrated
Goniometers hardware and controls provided required stability
Outlook
Comparison of measurements with simulations: miscut effects to be properly taken into account
New goniometers with updated angular redundancy currently being prototyped
Ideal system would need 8 crystals: 4 per beam, 2 per plane to fully accommodate orbit oscillations

## Slide 27: Thank you for your attention!