## Slide 1: Failure cases studied so far by WP7
D. Wollmann
9th HL-LHC Collaboration Meeting, Fermilab, USA, 14 - 16 October 2019

## Slide 2: Failure cases studied or under study (1/2)
Powering failures of D1/D3 revisited for HL  existing interlocking strategy (FMCM) sufficient
Criticality of missing coherent beam-beam kick (run3 & HL) – revisited  HW linking of BIS loops required for HL-LHC
Effect of quench heater firing on circulating beam  quench heater connection schemes to cause quadrupole/higher order fields & interlocking of discharge in HL triplet  beam screen filtering to be understood
Effect of CLIQ firing on circulating beam  updated connection scheme
Crab cavity failures in combination with the loss of the beam beam kick
Quench in HL triplets  symmetric quench detection & BLMs
Criticality of the ADT – simulations & experiments  failures slow enough to allow protection via BLMS

## Slide 3: Failure cases studied or under study (2/2)
Criticality of beam-beam compensating wires (for run2 / run3)  interlocking of powering, wire temperature, positions etc., for Run 3 interlock matrix of WIC fast enough before critical losses appear  to be specified for HL
Crab cavity failures in the SPS & MP tests & fast interlocks  fast interlocks for phase and voltage
UFO dynamics studies - ongoing
Magnet component damage limits due to direct beam impact
Numerical simulations of energy deposition caused by 50 MeV - 50 TeV proton beams in copper and graphite targets
Hydrodynamic tunnelling studies
Safe disposal of the LHC beam in very unlikely case of non-working beam dumping system  batch-by-batch excitation of beam with ADT