## Slide 1: Mechanics & Cooling Challenges for the ATLAS ITk Upgrade for HL-LHC
Diego Alvarez Feito
CERN EP-DT
On Behalf of the ATLAS Collaboration
28th International Workshop on Vertex Detectors
Lopud Island, Croatia 17th October 2019

## Slide 2: ATLAS Phase II Tracker Upgrade: ITk
New ATLAS Inner Tracker (ITk)
  Finer segmentation
  Faster readout and more storage
  Increased radiation hardness
  All silicon
Current ID

## Slide 3: ATLAS ITk: Layout
Pixel
Strip
ATLAS ITk
Strip Detector
  4 active layers
  |η|~2.8 coverage
  ~18000 strip modules (~165m2)
Pixel Detector
  5 active layers
  |η|~4 coverage
  ~10000 pixel modules (~13m2)
TDR: http://cds.cern.ch/record/2257755?ln=en
TDR: http://cds.cern.ch/record/2285585?ln=en

## Slide 4: ATLAS ITk: Layout
Strip Barrel
ATLAS ITk
Strip Endcap
Pixel Outer Barrel
Pixel Endcap
Pixel Inner System
Replaceable layers
(2000 fb-1)

## Slide 5: ATLAS ITk: Overall Concept
ITk to be assembled on surface inside an Outer Cylinder (OC) closed at each end by a Structural Bulkhead (SB)
  OC & SBs form ITK humidity barrier and are part of Faraday cage
  Strip/Pixel detectors separated by Pixel Support Tube (PST)
  Fully tested ITk to be installed in inner bore of LAr cryostat (IWV) via rails/rollers
  Design to allow for fast connections in the pit → Activated environment
  Very tight installation and lowering clearances

## Slide 6: ATLAS ITk: Global Structures
Joining Flange
Outer Cylinder (3 sections)
Pixel Support Tube
(3 sections)
Structural Bulkhead
Hat Stiffener
Structural Bulkhead
PP1 Strip Detector
PP1 Pixel Detector

## Slide 7: ITk Environment & Stability Requirements
Detector Subsystem | Integrated Luminosity [fb-1] | Max Dose [Mrad] | 1 MeV neutron equivalent Fluence [1014 neq/cm2]
Pixel Inner System L0 | 2000 | 900 | 130
Pixel Inner System L1 |  | 400 | 40
Pixel Outer Barrel | 4000 | 300 | 20
Pixel Outer Endcap |  | 450 | 30
Strip Barrel | 4000 | 45 | 10
Strip Endcap |  | 70 | 16
Four separate volumes with controlled humidity
  OSV: dew point -30°C
  Strips: dew point -60°C
  Outer Pixels: dew point -60°C
  Inner Pixels: dew point -60°C
IST
PST
OC with bonded heaters
Equivalent ASD to that measured in the current detector
Timescale |  | Module Stability, RMS [µm]
Short | ~ 1 day | 2
Medium | ~ 1 day | 5
Long | ~ 1 year | Equivalent to placement accuracy
Stability requirements

## Slide 8: ITk: CO2 Cooling
B.VERLAAT
L. ZWALINSKI
Temperature drop budget:
  Plant saturation: -45°C (proven with BabyDemo)
  Hottest temperature evaporators: -35°C
Design temperatures are on the limit!
1
4
System conceived to minimise temperature @ evaporator exit (as low as -40°C at PP1)
ITk Heat removal requirements ~ 270kW (Strip~124kW; Pixel~146kW)

## Slide 9: Strip Detector

## Slide 10: Strip Local Supports
Sandwich structures with CFRP skins, CFRP honeycomb
Ti pipes embedded in carbon foam for cooling
Strip modules bonded on both skins (double sided local supports)
  Equivalent concept for Endcap and Barrel
Barrel Stave
Endcap Petal

## Slide 11: Strip Barrel
Interlink
Z-braces
OC-brackets
OC
Barrel Shell
Service module
Flange
Stiffening Ring
Cylinder Shell
Stave locking bracket
Stave services

## Slide 12: Strip Endcap
Structural Bulkhead
Stiffening Disk
Service Trays
Inner Tube
Petal
Rails
Wheels (rings + blades)
SB supports the cooling & electrical patch panels @ PP1
Electrical patch panel
(45° phi sector)
Very tight clearances for petal insertion
(complex tooling for controlled kinematics)
Strip Endcaps assembled outside CERN (challenging transport)

## Slide 13: Pixel Detector

## Slide 14: Pixel Local Supports: Endcap & Inner System
  Equivalent concept for EC and Inner System
CFRP Skin
Ti-Tube
Bus Tape
Carbon Foam
E-break
Closeouts
R2
R3
R4
L0/1 Coupled Ring
L1 Ring
Endcap Rings
L0 Stave
L0.5 Ring
L1 Stave
Sandwich structures with CFRP skins & carbon foam
Ti pipes embedded in carbon foam for cooling
Pixel modules bonded on one (staves) or two (rings) sides

## Slide 15: Pixel Local Supports: Outer Barrel
Ti cooling pipes
Base blocks
CFRP Support Structure
Soldered
(Ni-coating)
Bonded
Functional Longeron
Functional Inclined Half-Ring
CFRP Truss
Ti Pipe
Ti Pipe
CFRP Ring
Gusset
Module Cells (module bonded to TPG)
Cells screwed to FLS with TIM between blocks (re-workability!)

## Slide 16: Pixel Endcap
PST
Half Rings
Flange
Flange
IST
Beam Pipe
Half Shell
Challenging service management in very limited space
Integration in half layers
Half-rings overlap

## Slide 17: Pixel Outer Barrel
Extremely challenging service management due to very limited space
Inclined Half Ring
Longerons
Inclined Unit
Outer Barrel Half (3xHalf Layers)
Half Layer
Half-layer shell
Service support shell
Outer System integration: OB halves closed around the ECs and the IST
Half layer Type-1 Services

## Slide 18: Pixel Inner System
  Inner System designed to be replaceable in the pit (separated from Outer System by Inner Support Tube – IST)
  Inner System built around “quarter shells”
  Cooling & electrical services arranged in trays atop the quarter shells
Quarter Shell
Coupled ring
  Inner Endcap Quarter
  Inner Barrel Quarter
L0 Stave
L1 Stave
PP0 Board
Quarter shell
Support rings
IST
IPT
(beam pipe support)
Inner System rails

## Slide 19: Local Supports: Thermal Performance
  Strip Module (Barrel Stave)
Challenging heat-management requirements for local supports
Thermal-electrical FEA to estimate runaway and sensor behaviour at the end of life
Full thermal prototypes under testing for validation
  Pixel Module (OB Longeron Cell)
  G.BECK

## Slide 20: Material Qualification
Challenging material selection due to expected radiation doses, particularly in the inner Pixel region
Ongoing characterisation studies to qualify raw materials (e.g. adhesives, TIMs, potting compounds) and components (e.g. connectors)
https://maxrad.web.cern.ch/maxrad/www/home.php
Thermal Tests
Mechanical Tests
  N. PACIFICO

## Slide 21: Concluding Remarks
New Inner Tracker (ITk) will replace the current ATLAS ID in LS3.
Future all-silicon ITk will feature Strip and Pixel detectors (coverage up to |η|~4).
ITK subsystems to be assembled and commissioned on surface inside a CFRP cylinder, which will them be installed at the centre of ATLAS.
Mechanical designs of the Global Structures, the Strip and Pixel detectors are conceived to overcome the challenges imposed by HL-LHC.
Substantial prototyping effort to qualify all design elements underway.
Limited space for service routing remains a critical issue, particularly in the Pixel detector.

## Slide 22: Questions?