## Slide 1: ProteCCT (Protection of Canted-Cosine-Theta-type Magnets) 1st STEAM Workshop 13-14 June 2019
Matthias Mentink,
On behalf of the STEAM team
cern.ch/STEAM

## Slide 2: Overview
Motivation
Thermal aspects
Internal circuit / Co-simulation
User interface
Complexities + correction factors:
  Oversimplified model of eddy currents in the formers  Correction factor fLoopFactor
  Additional helium present between the (non-bonded) formers and outer cylinder  Correction factor addedHeCpFrac
Simulation vs. experimental observations
Running the model
Demonstration
Summary

## Slide 3: Motivation
Eddy currents in formers surrounding CCT coils during discharge
(Field, courtesy J. van Nugteren)
CCT coils
Formers
Eddy currents in the formers
Canted-Cosine-Theta (CCT) magnets: superconducting strand inside slots in conductive former [1]
Insulated
Nb-Ti/Cu strand
Aluminum former
Why STEAM-ProteCCT?
Canted Cosine Theta Magnets: Concentric superconducting coils held in place by conductive aluminum formers
Quench protection of MCBRD Twin Aperture Orbit Correctors for HL-LHC upgrade and other future CCT-type magnets
  Magnet is discharged over energy extractor
  Eddy currents in the conductive formers  Heating in formers  Fast development of normal zone throughout superconducting coils (Quench-back)
  Complex three-dimensional geometry
 Quench simulation with STEAM-ProteCCT
[1] G. Kirby et al. IEEE Trans. on Appl. Supercond. 28, p. 4002205 (2018)

## Slide 4: Thermal aspects
Three-dimensional thermal propagation in simplified geometry [2]
Longitudinal heat propagation along length of strands, insulation, and formers
Transverse heat propagation
  Individual thermal elements for strands, insulation, formers, former insulation
  Heat flow to the bath: 1.9 K: Kapitza + film boiling cooling, 4.5 K: Nucleate + film boiling
  Periodic boundary condition: Simulation of single turn per former to simulate entire magnet
Non-linear magnetic-field- and temperature-dependent properties taken from STEAM library and LEDET material database
Turn-to-turn periodic boundary condition
Thermal layout [1]
[2] M. Mentink et al. IEEE Trans. on Appl. Supercond. 28, p. 4004806 (2018)

## Slide 5: Internal circuit / Co-simulation
Circuit types:
  Internal circuit: inductance of CCT coils, internal resistance, crowbar, dump resistor + switch
  External circuit: ProteCCT takes external current waveform (co-simulation)
  Both cases: Main circuit (CCT coils) inductively coupled to formers and outer cylinder
Adaptive time-stepping (constraints on maximum dT/dt, maximum dI/dt in formers, user-specified dt)
Main circuit with CCT coils: Inductance, internal resistance, crowbar and dump resistor
Formers + outer cylinder: Inductively coupled to main circuit
M
Representation of internal circuit

## Slide 6: User interface
ProteCCT user manual [3]
All user input is taken from a single Excel file (inspired by LEDET user interface)
Co-simulation: Tool exchanges information through text-files
For the most part, easy-to-understand parameters (Conductor RRR, Operating current, etc.)
Model input: Excel file
[3] M. Mentink, “STEAM-ProteCCT User manual”, EDMS nr. 2160020, (2019)

## Slide 7: Complexity & correction factor #1: fLoopFactor
Coupling matrix: Calculated in Comsol, assuming simplified 2D geometry with cos-θ current distribution in the coils, formers, and outer cylinder [3]
Assumption: Eddy current flows axially through formers
Reality: Eddy current model is oversimplified, so global correction factor fLoopFactor needed that augments the effective path lengths of the eddy currents
fLoopFactor determined by matching discharge to experimental result at low current without quench-back
Coupling-matrix calculated in Comsol, assuming simplified 2D geometry with cos-θ current distribution
[3] M. Mentink, “STEAM-ProteCCT User manual”, EDMS nr. 2160020, (2019)
Determination of fLoopFactor by matching to experimentally observed low-current discharge (no quench-back)

## Slide 8: Complexity & correction factor #2: addedHeCpFrac
In addition to helium to bath cooling: Additional liquid helium present between non-bonded formers and outer cylinder  Slows down quench-back onset
Extra helium heat capacity: 0.13 MPa liquid + gas, with inclusion helium gas enthalpy
Added as global correction factor addedHeCpFrac  Additional heat capacity in formers (~0.6%)
Determination of correction factor by matching quench back onset tQB at I0 = 400 A, 1.9 K, 1.43 Ω  Used as a global parameter
Simulated vs. Observed onset of Quench back (Measurement data: Courtesy F. Mangiarotti)
Sliding and deformation of formers during powering (Courtesy Martin Novak)
Liquid helium between formers

## Slide 9: Simulation vs. Experimental observation
Comparison between simulation and experimental (MCBRD prototype apertures and short models):
High degree of consistency between simulations and experimental observations
Checked for: Different magnetic lengths, former material types, operating temperatures, varying dump resistors + Metrosil varistors, operating currents
Two fixed global correction parameters fLoopFactor and addedHeCpFrac for all cases
Measurement data: Courtesy F. Mangiarotti
MCBRDp1 prototype, discharge over 1.43 Ω dump resistor
MCBRDp1 prototype, discharge over Metrosil varistor
MCBRDs1b short model, discharge over Metrosil varistor

## Slide 10: Running the simulation
Voltage-to-ground calculation
(During simulation, t = 50 ms)
Strand temperature development
(During simulation, t = 50 ms)
Very fast: Typically no more than few minutes to run
Free-to-use standalone executable, no license required (Does require MCR installation)
During simulation: Optional plotting of voltage-to-ground and strand temperature for each time-step
Simulation output written to excel file: Time-dependent Current, hot-spot temperature, voltage-to-ground of selected turns, etc

## Slide 11: Demo: MCBRDp1
Strand temperature development
during simulation, t = 50 ms
Voltage distribution in magnet during simulation, t = 50 ms
Command prompt output
ProteCCT is found on STEAM website: cern.ch/steam
Manual: EDMS Nr. 216002 (link of STEAM website)
Simulation tool available of steam website
Running requires installation of Matlab runtime (see Matlab runtime.txt)

## Slide 12: Summary
ProteCCT
Simulation tool for evaluating discharge of CCT-type magnets (With quench-back from conductive formers)
Very fast, standalone executable
User-interface: Input from Excel, output to Excel (plus optional plotting during execution)
Available on STEAM website (cern.ch/steam)
Free to use, but please reference to ProteCCT manual when used for publications / presentations
Future development
  User interface development
  Automatically generated reports
  Suggestions?
CCT coils
Formers
Eddy currents in the formers