## Slide 2: Agenda
LHCb Containers Network overview
  LHCb Containers: why?
  Physical infrastructure overview
  Network topology
DWDM setup using PAM4 optics
  Feasibility test for shared HLT
  DWDM and PAM4 optics
  DWDM setup for experiments
Q&A

## Slide 3: LHCb Containers Network overview
Daniele Pomponi
Communication Systems Group
Information Technology Department

## Slide 4: LHCb containers: why?
End of Wigner contract
LHCb Containers
5 and 6
2nd Network HUB Prevessin site
Computer Center Meyrin site
WIGNER CAPACITY

## Slide 5
Computer
Center
Containers
2nd Network HUB

## Slide 7
4 Routers providing
  161 broadcast domains for LCG domain
  24 broadcast domains for management
  19 broadcast domains for intelligent PDUs
364 Switches attached to the routers
  185 data switches (LCG)
  179 management switches
What do we have at Wigner?

## Slide 8
What do we migrate to CERN?
 |  | Quad servers (CPU) |  | JBODs (Disk) |  | 
 |  | Units | Pallets | Units | Pallets | Total pallets
#1 | February | 150 | 12 | 0 | 0 | 15
#2 | April | 54 | 5 | 72 | 12 | 19
#3 | May | 129 | 11 | 144 | 18 | ~33
#4 | June | 150 | 13 | 104 | 13 | ~29
#5 | October | 174 | 14 | 120 | 15 | ~33
#6 | December | ~183 | 16 | 0 | 0 | ~20
TOTAL |  | 840 quads (3360 nodes) |  | 440 JBODs |  | 

## Slide 9: Physical infrastructure overview

## Slide 10: Rack layout
2x Management switches – HP 2920
2x Data switches – Ruckus ICX 7750-48C
20x Quad CPU 2U
1x Management router - Ruckus ICX 7750-48C
1X Data router – Juniper QFX10008
4 line-cards 30x100G
Server rack (23 per container):
Network rack (1 per container):

## Slide 11: Cabling and Optics
Data switches to LCG/ITS distribution router:
  Multimode Fiber OM4 LC-LC
  40GBidi Optics
MGMT switches to MGMT distribution router:
  UTP Cat. 5E
Data Router to CORE LCG/ITS routers:
  Single-mode fibers LC-PC
  100G-LR4 Optics
MGMT Router to MGMT core routers:
  Single-mode fibers LC-PC
  10G-LR Optics

## Slide 12: Network topology
The setup is exactly the same as the one currently used at Wigner
  The only difference is on the switch uplink (2x40Gbps, instead of 2x10Gbps)
8 new broadcast domain, each of them having:
  6 switches (except the last one with 4 switches only)
  240 physical servers - 40 per switch (except the last one with 160 servers)
  960 Virtual Machines - 4 per node (except the last one with 640 VMs)
Each switch connect 40 servers (40x10Gbps) and 2x40Gbps uplink
  Switch Blocking factor = 1:5 (compare to 1:20 on Wigner current setup).
  Initial uplink of the router (to go out of the container) is 4X100G

## Slide 14: Data and Management routers
MGMT
NETWORK
CORE
NETWORK
1X10G
1X10G
DATA ROUTER
MGMT ROUTER
1X100G
1X100G
1X100G
1X100G

## Slide 17
LCG/ITS CORE
3
GPN CORE
LCG/ITS CORE
GPNCORE
Prevessin 2nd Network hub
Meyrin Computer Center
LHCb Containers
MGMT
DATA
2
2X100G
2X100G
1
2
1
1X10G
1x10G
~ 8.4KM
~ 5.3KM
~ 3.7KM

## Slide 18
Rack units: 13
PSUs: 6 16200 W AC
Cooling: Front-to-back airflow
Weight: 146Kg
System throughput: Up to 48 TBs

## Slide 20: Looking at the stats …
LHCb Container data router to datacenter core router #1 [LCG-ITS vlans]
LHCb Container data router to datacenter core router #2 [LCG-ITS vlans]
200G
200G

## Slide 21: DWDM Setup
PAM4 technology for Tbps transmission lines

## Slide 22: Feasibility test for shared HLT
Feasibility of a shared facility for the High Level Trigger farms of the four LHC experiments was reviewed in 2017
Advantages:
re-purpose of servers when no data taking
shared cost of infrastructure and operations
Challenges:
Very high data rates from detectors to HLTs:
  RUN 3
  ALICE: 4Tbps
  LHCb: 40Tbps
  RUN 4
  ATLAS: 40Tbps
  CMS: 40Tbps

## Slide 23
20x 10G-SR
Juniper
QFX5200-32C
4x 100G-LR4
LHCb detector - Prevessin
IT datacentre - Meyrin
nb-n044-01
Ruckus ICX 7750
nb-n044-02
=
=
=
=
=
=
nb-n044-12
Juniper
QFX5110-48S
20x 10G-SR
nb-n040-01
Ruckus ICX 7750
nb-n040-02
=
=
=
=
=
=
nb-n040-12
Rack N044
Rack N040
DATA + MGMT VLANs
DATA
12x 40G
MGMT
1x 40G
MGMT
12x 10G
DATA
12x 40G
VMGMT
1x 40G
MGMT
12x 10G
LHCb online
system
DATA-VLANs
MGMT VLANs
Credit: Edoardo Martelli - CERN
Logical test-setup

## Slide 24: Transmission results
LHCb online commented: “Operationally and performance-wise, it seems to be the same as running a sub-farm at Point 8” [LHCb pit]
Local HLT
Local and Remote HLT

## Slide 25: DWDM using PAM4 optics
The PAM4 optics are not tunable 1 wavelength = 1 optic
Support for high power consumption optics is mandatory (similar case to ER4)
PAM4 lines were loaded with sustained 150Gbps traffic for several hours with no transmission errors

## Slide 26: DWDM setup for experiments
High throughput link using WDM (PAM 4 system)
Up to 40 channels (40x100G) transported over a single pair of fiber (up to 40Km)
QSFP28 PAM4 (Pulse Amplitude Modulation) 100G optics used directly on Juniper devices (small specific configuration required)
4x100G installed between ALICE and Cern Computer Centre (will evolve to 1Tbps)
On-going installation between LHCb and Cern Computer Centre
Experiment
network
Datacentre Network

## Slide 27
DWDM Physical setup
DWDM PAM4 channels to QFX5200
DCP-M-PAM4
Fiber to ALICE

## Slide 28: DWDM Conclusion
WDM PAM4 is an affordable and ready to use technology for Tbps transmission lines
Taking into account that during RUN 3/4 we expect a substantial increase in the data sent by the experiments up to 40Tbps we believe that this technology can be a very valid solution to increase the bandwidth between the CERN data centers and the experiments sub-farm.
According with the vendor this technology will be ready to support 400G channels using the same equipment (PAM4 optics have to be developed in the coming years). This would allow transmission of up to 16 Tbps using a single pair of fibers.

## Slide 29: Questions?
Daniele Pomponi – d.pomponi@cern.ch
Communication Systems Group
Information Technology Department