## Slide 1: DB generation Phase coding, satellite bunches, R&D results and planning, CTF3 measurements
Introduction
CTF3 experimental results
PHIN Photoinjector
Conclusion
Current from Linac
Current after Delay Loop
Current in the ring

## Slide 2: CTF 3 – CLIC Test Facility
demonstrate CLIC RF power source Drive Beam generation (fully loaded acceleration, bunch frequency multiplication 8x)
Test CLIC accelerating structures
Test power production structures (PETS)aaaa .
CLEX
Linac
Delay Loop 42m
Combiner Ring – 84m
Injector
TL1
TL2
RF deflector
Laser
3.5A – 1.2µs 150 MeV
28A 140ns 150 MeV
Califes
TBL
TBTS
Test Beam Line - TBL
Two Beam Test Stand - TBTS
Probe Beam - CALIFES

## Slide 3: CTF3 base line programme
CTF3 – R&D Issues - where
fully loaded acceleration
recombination x 2
phase-coding
bunch length control
recombination x 4
bunch compression
PETS on-off
two-beam acceleration
structures 12 GHz
structures 30 GHz
Deceleration stability
R1.1 – structures R1.2 – DB generation R1.3 – PETS on-off R 2.1 – structure materials R 2.2 – DB decelerator R 2.3 – CLIC sub-unit
R.Corsini

## Slide 4: TBTS – Two beam test stand
Combined beam of Combiner Ring extracted (up to 15A/28A), transported to CLEX used for power production in TBTS and TBL
TBTS: Line for Two-beam acceleration studies
both Drive Beam and Probe Beam to the end
Optics and first breakdown kick measurements
170 MW (peak) RF power reached in PETS power production structure total pulse length ~200 ns
=> reached nominal CLIC power (135 MW)
acceleration structure is being installed now

## Slide 5: TBL - Test Beam Line / Califes
Califes: Probe beam photo-injector
Laser performs well, nominal bunch charge reached, accelerated to 140 MeV
Beam transported to the end with ~100% transmission, reliable beam to TBTS
Detailed optics studies
TBL: Line for deceleration studies
Installation of beam line with all magnets and BPMs finished, 1st PETS prototype installed (several more this year)
Beam transported to the end
10A beam generated 20 MW RF power in the PETS structure, follows expectation
CTF3/CLIC collaboration: increased to 35 institutes

## Slide 6: Comparison CLIC - CTF3
Still considerable extrapolation to CLIC parameters
Especially total beam power (loss management, machine protection)
Good understanding of CTF3 and benchmarking needed
 | CTF3 | CLIC
Energy | 0.150 GeV | 2.4 GeV
Pulse length | 1.2 µs | 140 µs
Multiplication factor | 2 x 4 = 8 | 2 x 3 x 4 = 24
Linac current | 3.75 A | 4.2 A
Final current | 30 A | 100 A
RF frequency | 3 GHz | 1 GHz
Deceleration | to ~50% energy | to 10% energy
Repetition rate | up to 5 Hz | 50 Hz
Energy per beam pulse | 0.7 kJ | 1400 kJ
Average beam power | 3.4 kW | 70 MW

## Slide 7: Full beam-loading acceleration in CTF3
MKS03
MKS07
MKS06
MKS05
Spectrometer
10
Spectrometer
4
RF pulse at structure output
RF pulse at structure input
analog signal
1.5 µs beam pulse
Measured RF-to-beam efficiency 95.3%
Theory 96% (~ 4 % ohmic losses)
high current routine operation demonstrated

## Slide 8: Beam current stability
operation sensitive to beam current variations
current stability ~ 0.15% end-of-linac, ~ 0.16% combiner ring
current variation over the pulse, also due to SHB phase switch => different energy
=> feed-forward will be implemented this run
badly phased SHB

## Slide 9: RF / Beam energy stability
  RF phase stabilisation for klystrons put into operation => slow phase variation down to ~ 0.5 degree
  phase jitter ~ 0.1 – 0.2 degree (after compression)
  short term energy jitter from RF presently measured ~ 0.6 10-3
  slow power variation (from RF pulse compression) several % => temperature feed-back will be implemented this run
σ
Klystron | PKI σ | PKI σ | PSI σ | PEI σ
 | MW | deg | deg | MW
MKS03 | 0.075 | 0.11 | 0.079 | 0.100
MKS05 | 0.115 | 0.16 | 0.074 | 0.089
MKS06 | 0.222 | 0.28 | 0.441 | 0.157
MKS07 | 0.080 | 0.41 | 0.083 | 0.187
MKS11 | 0.109 | 0.39 | 0.064 | 0.232
MKS12 | 0.154 | 0.28 | 0.069 | 0.154
MKS13 | 0.119 | 0.24 | 0.195 | 0.117
MKS15 | 0.080 | 0.19 | 0.215 | 0.066
Total |  |  |  | σ=0.59 µ=475
Total RF power

## Slide 10: Delay Loop operation
2005
2004
CLEX
CR
TL1
DL
TL2
SHB
SHB
SHB
gun
buncher
2 accelerating structures
1.5 GHz sub-harm. bunching system
1.5 GHz RF deflector

## Slide 11: SHB system – Phase coding
Key parameters for the SHB system: 1) time for phase switch < 10 ns (15 1.5 GHz periods)
2) satellite bunch population < 7 %
(particles captured in 3 GHz RF buckets)
phase switch:
satellite bunch population:
Phase switch is done within eight
1.5 GHz periods (<6 ns).
Satellite bunch population was
estimated to ~8 %.
main bunch
satellite bunch

## Slide 12: Delay loop status
factor 2 combination re-established after 2 years
current about doubled, up to ~7 A (~0.5 A in satellites)
Current from Linac
Current after Delay Loop
Current in the Delay Loop
7A
DL
CR

## Slide 13: Demonstration of frequency multiplication

## Slide 14
3rd
lo/4
4rd
2nd
Cring = (n + ¼) l
injection line
septum
local
inner orbits
1st deflector
2nd deflector
1st turn
lo
RF deflector
field
RF injection in combiner ring
combination factors up to 5 reachable in a ring

## Slide 15: Combination setup procedure
Developed a setup procedure to optimize combination
5 parameters
  Amplitude and phase in each deflector
  Ring path length (wiggler for path length tuning)
Monitor trajectory differences over various turns
s

## Slide 16: Isochronicity Tuning
ring optics needs to be isochronous to keep short bunch length => high power extraction efficiency
Streak Camera observations
isochronous – 60th turn
non-isochronous – 2nd turn
momentum compaction αp < 10-4

## Slide 17: CR RF deflectors => Instability
Old deflectors, undamped
New deflectors, damped
damping loads
BPM signals shoving vertical instability
current
horizontal
vertical
RF deflectors had a vertical mode that deflected the beam
Could be minimized by proper phase advance – not done
effect perfectly understood, reproduced in simulation => not an issue
BPM signals, no instability

## Slide 18: Combiner ring status
2nd turn of 1st pulse and 1st turn of 2nd pulse
1st turn of 1st pulse
3rd turn of 1st pulse, 2nd turn of 2nd pulse, 1st turn of 3rd pulse
All 4 pulses
280 ns
280 ns
routinely factor 4 combination achieved with 15 A, 280 ns (without DL)
Current from Linac
Current in the ring
15 A
CR

## Slide 19: Factor 8 combination (DL+CR)
~28 A combined achieved, nominal 140 ns pulse
30A
DL
CR
Current from Linac
Current after Delay Loop
Current in the ring

## Slide 20: Factor 8 combination (DL+CR)
Current from Linac
Current after Delay Loop
Current in the ring

## Slide 21: Recombination studies
Turn 1
666 ps initial bunch spacing
emittance measurement (vertical plane) combined 4x beam < 150 π mm mrad
streak camera measurements
Turn 2
Turn 3
Turn 4
83 ps final bunch spacing
from DL
orbit closure well controlled
combination to be optimized
dispersion/isochronicity

## Slide 22: Adjustment of the path length
DL: correct length accessible =>
Measured Lfrac = - 1/CF lRF
CF 5, - 1/5 lRF
CF 4, - 1/4 lRF
Expected ring length for nominal wiggler current
About 1.5 mm
Wiggler behaviour as expected
CR: ~1.5 mm difference only
control to better than 0.5 mm

## Slide 23: State of the art today
ongoing Drive Beam generation demonstration in CTF3.
  Full beam loading (95% transfer), high current (up to 5A) in DBA
  Sub-Harmonic bunching, phase coding (7% satellites)
  Bunch train recombination factor 2 in Delay Loop (up to ~7 A)
  Bunch train recombination factor 4 in Combiner Ring (3.8 to 15 A)
  Recombination 2x4 DL/CR achieved ~ 28 A
  Isochronous operation of ring, ap < 10-4
  Transverse rms emittance 100 π mm mrad (end of linac only) 150 π mm mrad (vert., 4x combination)
  Bunch length control to < 1 mm rms (end of linac only)
  Control of ring length to better than 0.5 mm
  Beam current stability ~ 0.15% end-of-linac, ~0.16% combiner ring

## Slide 24: To be addressed …
Dispersion / isochronicity in DL/CR
Full bunch length manipulations in TL2 after combination (we see from RF that the form factor is close to 1)
full beam (28 A) to users (new TL2/CLEX BPM readout)
RF power production in CLEX
Two-beam operation in TBTS (relevant CLIC sub-unit) (we started with CCC operator supervision)
Deceleration stability
Loss management, machine protection system
Satellite bunches
Photo injector option
…

## Slide 25: PHIN Photo-injector
Smaller transverse emittance, shorter bunches, no energy tails, no satellites
Bunch charge lower than present injector shown up to 2.5 nC, above nominal!, also 2.3 nC for long train reached
Beam energy ~ 5-6 MeV
Emittance measured ~7 π mm mrad
Very good agreement with simulations
started to measure laser/beam stability: better than requirements
δ=0.35mm
E-beam size: x=1.53mm
δ=0.15mm
Laser size: x=0.74mm

## Slide 26: Laser system status
setup significantly improved (beam path, optical crystal,…)
For PHIN all laser main target parameters fulfilled !!!
0.8% beam current stability (without feedback on the laser)
long term studies (cathode response, …) to be done
Laser phase coding to be demonstrated this year
  Booster amplifier needed (~ June)
fulfilled PHIN photo injector requirements |  | 
micro bunches repetition rate | ns | 0.667
Synch to external rf @ 1.5GHz | ps | <1
micro bunch width (FWHH) | ps | <10
micro bunch energy (@ cathode) | nJ | 370
laser pointing stability std | mm | 0.5

## Slide 27: Validation of DB scheme
Parameter | Unit | CLIC nominal | Present state | Objective 2010 | Objective 2012
I initial | A | 7 | 5 | 5 | 5
I final | A | 100 | 28 | 30 | 30
Qb | nC | 8.4 | 4 | 2.5 | 2.5
Emittance, norm rms | p mm mrad | ≤ 150 | 100 (end of linac) ≤ 150 (y, comb. beam) | ≤ 150 (comb. beam) | ≤ 150 (comb. beam)
Bunch length | mm | ≤ 1 | ≤ 1 (end of linac) | ≤ 1 (comb. beam) | ≤ 1 (comb. beam)
E | MeV | 2400 | 120 | 120 | 150
Tpulse initial | ms | 140 | 1.4 | 1.4 | 1.4
Tpulse final | ns | 240 | 140 (240) | 140 (240) | 140 (240)
Beam Load. Eff. | % | 97 | 95 | 95 | 95
Deceleration | % | 90 | - | 30 | 50
Phase stability @ 12 GHz | degrees | 0.2 | - | ? | 
Intensity stability |  | 7.510-4 to few 10-5 | few 10-3 | 10-3 | 

## Slide 28: Conclusion
Drive Beam generation very well covered
  fully loaded operation demonstrated and routinely used
  full bunch train combination 2x4 shown (DL+CR)
  optimization procedures developed
  started to address performance and stability
next major steps:
  two beam tests in TBTS
  drive beam deceleration in TBL
CTF3 experimental program + plans for 2010 => see Roberto’s talk
Many THANKS to all collaborators!

## Slide 29: Reserve

## Slide 30: 2009 CTF3 experimental program
30 GHz: One structure test (TM02) + breakdown studies
PHIN Beam characterization, reach ½ of nominal bunch charge
CALIFES Beam characterization, beam to TBTS (most likely still reduced current)
Delay Loop Back in operation, retrieve combination x 2 (~ 7 A)
Combiner Ring Final optics checks, isochronicity, put together with DL (> 24 A)
TL2 Complete commissioning (tail clipper), bunch length control, > 20 A to users
TBTS PETS to nominal power/pulse length (15 A, recirculation)
Beam commissioning of probe beam line
First accelerating structure tests (one structure ? – CLIC G)
Two-beam studies (deceleration/acceleration), initial breakdown kicks studies
TBL PETS validation (100 MW, need > 20 A), beam line studies (2-3 PETS ?)
Others CDR studies in CRM, beam dynamics benchmarking, stability studies, control of beam losses…
Goals