## Slide 1: Cold diodes for HL IT circuit: implications on cryostat design
Y.Leclercq, D.Ramos, V.Parma, E.Todesco for WP3
TCC meeting: 11 Apr. 2019

## Slide 2: Context
Objective : integrate 4 diodes at cold, connected to:
  Q1 to Q3 main circuit (2 connections)
  Trims circuits (3 connections)
2018: Preliminary studies
  Interfaces between WP3 and WP6a, WP3-WP6a joint meeting 23.01.18 Indico693807
  Cold diodes module : Conceptual integration proposal, HL-MCF meeting 7.08.18 Indico745287
  Cold diodes module : Conceptual Integration studies, 8th HL-LHC collaboration meeting, 17.10.18 Indico742082
For illustration
Courtesy S. Yammine
wp3
wp6a
D1
CP
Q3
Q2b
Q2a
Q1
IP
Power converters area
SCLink
DFHX
DFX
≈80m
≈50m
≈8m
Service tunnel
Transverse tunnel
LHC tunnel
Courtesy S.Maridor

## Slide 3: Location of diodes in the tunnel
Courtesy S.Maridor
Diode must be as close as possible to the circuits (minimize additional bus bars)
 after D1 to allow access to the 5 cable
Diodes must be compatible with radiation levels and available space:
   Location between D1 and DFX :
    Lowest Neutron Fluence level
    Cables accessibility
    Integration space availability
Diodes must be accessible for replacement
D1
Courtesy R.Garcia, G.Lerner
Access location
to the 5 cables

## Slide 4: Diodes ideal location in D1-DFX zone
Radiation levels and large gradients (future FLUKA simulations will provide more accurate results):
   Diodes location has to be outside cryostat envelope
Integration space constraints
  Cables accessibility only above the beam
  Transport & Survey reservations exclude passage side
   ideal location identified
D1
MBXF
D1
MBXF
Courtesy Ruben Garcia Alia
Autumn 2018 values
CP
CP
D1
MBXF
Beam
28 cm
60 cm
80 cm
100 cm
83 m
Cables to connect
to the diodes
Ideal location
High radiation area
Transport & survey reservations
Ideal location
Accessibility
Courtesy C.Eymin

## Slide 5: Technical systems constraints and implications on conceptual design  proposal of a Cold Diode Module (CDM)
Vacuum equipment
D1 cryostat interface complexity:
  Beam tubes and associated equipment (BPM, CWT, etc.)
  Cryogenic lines routing and connections
  Bus bars interconnection
  Vacuum and pressure loads
Several options studied
We propose a dedicated cryostats for the cold diodes  Cold Diodes Module (CDM)
D1
MBXF
83 m
Ideal location
Beam alignment + Sector valve
No access for bus bars connection
Cryo pipe integration
Beam alignment + sector valve
Beam alignment + sector valve
Splice access + radial integration
Beam alignment + sector valve
  Indico693807
<3m
Beam
Plug
To
SCLink

## Slide 6: Layout evolution towards a CDM unit
Cold Diodes Module starting point:
60 kGy as boundary with today’s simulations
Design focuses on optimising position
Quick replacement feasible
CDM interfaces with splices and plug
D1
MBXF
CP
Layout 2018
Working layout 2019
Courtesy R.Garcia, G.Lerner

## Slide 7: Conceptual design of the CDM
CDM preassembled with diode pack, bus bars with plug and qualified before tunnel installation
Some technical features
  In superfluid helium, common volume with magnets
  Same insulation vacuum as triplets cryostats
  Actively cooled thermal shield
  Diodes replaceable (aimed at being done with a YETS)
 study led to a 1st concept as an acceptable compromise
Further iteration will be necessary with various work-packages
Plug
Diodes
Splices
KhFh
D1
Jumper
Superfluid vol.
4.5K LHE
NbTi leads
Cu Leads TBC
Splices
Actively cooled th. shield
Vacuum envelope
DFX
D1
Vacuum
equipment
19 NbTi-NbTi
splices
Plug
Replaceable
Cold Diodes
Supports
19 Bus bars

## Slide 8: How to proceed and plans
Cost estimate of CDM unit prepared and being discussed within WP03
Contribution to the ECR with the required information (technical, resources and schedule)
Proceed from conceptual study to engineering design
Detailed design by end of 2019 (build-to-print)
Construction and qualification of a full prototype for the String (could be used as spare)
Supply of components in industry
Assembly at CERN (service contract)
Equipping with diode pack and qualification testing (but no cold testing) before installation
4 units + 1 spare to be produced in 2021-2023

## Slide 9: Summary
Layout considerations require integration of the cold diodes in individual cryostat units (CDM) equipped with dedicated bus bars and a diode package
The CDM are located between the D1 and the DFX, with an accessibility for replacement of the diode package, aimed at allowing replacement within a YETS
The positioning of the CDM is constrained longitudinally and transversally by technical systems and integration considerations, a proposed solution has been found as a compromise with radiation resistance
A cost estimate has been done and is being discussed within WP03
An ECR will have to validate the proposal
Further iterations with other WPs will have to accompany the evolution of the conceptual design towards a final design by the end of 2019
It is proposed to build and qualify a prototype for the String
4 units + 1 spare to be produced in 2021-2023

## Slide 10: Spare slides

## Slide 11: Iterations
Diodes assembly assumptions:
  Volume Ø175 x 600 mm
Preliminary Concept :
  1Mev neutron fluence ≈1.4x1014 cm-2
  Dose:≈60 kGy
Request to review position of cold diodes toward D1 to minimise dose
Other concepts being analysed
Iterative work in progress
D1
MBXF
D1
MBXF
Concept | 1 Mev neutron fluence | Dose
 | [cm-2] | [kGy]
#1 | ≈ 1.4 x 1014 | ≈ 60
#2 | ≈ 1.5 x 1014 | ≈ 30
#3 | ≈ 1.4 x 1014 | ≈ 35
#4 | . | .
D1
MBXF
Concept #2
Replacement issues
D1
MBXF
Concept #3
Assembly issues
D1
MBXF
Concept #4
High dose level
Courtesy Ruben Garcia Alia

## Slide 12: Cold Diodes Module integration
Integration boundaries extrapolated from EDMS 1991506
Cold diodes preliminary location:
  84-86 m from IP
  Radially : ≈0.7m to 1.0 m from beam axis
EDMS1991506 WP15
M.Mendes, M.Gonzalez
Courtesy M.Gonzalez
Indico 683600
DFX
D1
Vacuum & beam equipment
BPM
Beam axis
Diodes axis
Splices to D1
Plug
83m
84m
86m
From IP
0.7 to 1.0m