## Slide 1
D. Attié, P. Colas, M. Dixit, M. Riallot, W. Wang
Micromegas tests
̶ Test beam 2010 plans ̶
RD51 Mini Week - CERN
Notes: I’m here to present a TPC review

## Slide 2: Data taking diagram
T2K electronics
1728 channels
Back-end electronic
(ML405)
PC
T2K DAQ on Linux
500 Go
HDD
TCP/IP via ethenet
Optical
fibre
Beam trigger
Lemo
LV-TTL
LV
(+5 V)
SHV cables
Vmesh = 380 V
Vdrift =1 kV
Control room
Hall
Goliath magnet
T2K gas
(5L/h)
CAEN 471A
(NIM)
Standard PC
Power supply

## Slide 3: Detector description 1/2
24 rows x 72 columns; <pad size> ~ 3.2x7 mm2
17 cm
23 cm
1726 pads Micromegas resistive Kapton bulk

## Slide 4: Detector description 2/2
Total weight: ~20 kg
Radiation length: 40% (2×1.8 cm of aluminium)
27 cm
40 cm
35cm
11 cm
B field
Bottom
Top

## Slide 5: Requests for the beam tests
Detector placed in the centre of the magnet for homogeneous B field
Goal: precision tracking and performance measurement of the resistive Kapton coverlay with hadrons at different beam intensities in TPC mode
Duration: 3-4 days
Particles: muons preferably, the rest can be hadrons, from low to very high rates
Intensity: scan necessary.
Gas: premix bottle of T2K gas (ArCF4Iso) at 5 L/h
Status:
  optical fiber, SHV cables, gas tube already installed
  improve the box installation: secured small lift table
  own beam trigger as close as possible to the gas box but out of the B field