## Slide 1: Remote handling of ultra-high vacuum beam pipe connections in high-radiation zones
Lukasz Krzempek, Cedric Garion
TTC CERN 06.02.2020

## Slide 2: Outline
Introduction to flanges with knife for ultra-high vacuum applications;
Present applications of ‘Quick chain clamps’;
HL-LHC connection concept for VAX;
Summary.
TTC CERN 06.02.2020

## Slide 3: ConFlat (CF) flanges for Ultra High Vacuum (UHV)
Bolts + standard gasket OFHC
Leak tests
Laboratory use
Not compatible with bake out
Bolts + silver coated gasket OFS
Accelerators (LHC, LEIR,…)
Compatible with bake out
CF knife
Cross section of a typical assembly
TTC CERN 06.02.2020
Typical tightening torque – 33Nm (M8 screws for DN100)
350N/mm – force acting on gasket

## Slide 4
ConFlat (CF) quick flanges for Ultra High Vacuum (UHV)
Chain clamp segment
CF knives
Courtesy of MKT Tschann
Cross section of a typical chain clamp assembly
Tightening screw
Overview chain clamps CF | 
Material | Stainless steel 1.4435
Temperature range | -200 to +350°C
Tightening torque | Depends on clamp size (30Nm for DN100 chain clamp) and coating conditions
UHV | 10^-12mbar
Available sizes | DN16 – DN250
TTC CERN 06.02.2020

## Slide 5: Examples of present applications – chain clamps and chain clamp assemblies
TTC CERN 06.02.2020
Horizontal actuation of tightening screws
Combination of chain clamp and bellows compression tool
LHC
Booster
Preparation (drawings, pictures, simulations)
Dose mapping;
Work planning (where and how long);
Mock-ups and training;
Tooling (electrical wrenches, extension rods, etc.)
*
*
*
*
*
Manual handling with optimized intervention tooling
Chain clamp in close position
Chain clamp in open position
Guiding grooves
[1]
[2]

## Slide 6: Vacuum Assembly for eXperimental areas (VAX) in HL-LHC phase
Priority to radiation transparent aluminium;
Transparent to a strong external magnetic field;
Robust equipment ensuring long term system reliability;
Quick, standard and unified connection between the VAX components;
Vertical remote handling maintenance.
ATLAS
CMS
Access to VAX equipment at Point 1 (on the left) and Point 5 (on the right)
VAX relocation into experimental area
VAX relocation into experimental area
TTC CERN 06.02.2020

## Slide 7: Vacuum Assembly for eXperimental areas (VAX) in HL-LHC phase
MODULE 1:
Vacuum sector valve
DN100 chain clamp assemblies
MODULE 2:
Instrumentation to pump down and control vacuum
MODULE 3:
Vacuum sector valve
DN100 chain clamp assemblies
Tunnel
Point 1 IP
TTC CERN 06.02.2020
Combination of chain clamp and bellows compression tool

## Slide 8: VAX Module 1 maintenance - DN100 chain clamp
TTC CERN 06.02.2020
Bellow compression tool arrive to its position;
Jaws grab the collar of bellows;
First tightening screw of chain clamp DN100 is wound out to its maximum;
Second tightening screw of chain clamp DN100 is wound out to its maximum;
Chain clamp DN100 assembly is pivoted backwards to free some space;
Bellows is compressed by compression tool;
(Chain clamp DN100 assembly on the opposite side of Module 1 is opened by the same 3 screws (2x tightening screw and 1x pivoting screw). However, the chain clamp is hidden for the purpose of this video);
The equipment in VAX Module 1 is shifted backwards and Module 1 is ready for transport.

## Slide 9: VAX maintenance – DN40 chain clamp
TTC CERN 06.02.2020
Bellow compression tool arrive to its position;
Jaws grab the collar of bellows;
First tightening screw of chain clamp DN100 is wound out to its maximum;
Second tightening screw of chain clamp DN100 is wound out to its maximum;
Chain clamp DN100 assembly is pivoted backwards to free some space;
Bellows is compressed by compression tool;
(Chain clamp DN100 on the opposite side of Module 2 is opened in the same sequence. It is skipped for the purpose of this video)
First tightening screw of DN40 chain clamp is wound out to its maximum;
Second tightening screw of DN40 chain clamp is wound out to its maximum;
Chain clamp DN40 assembly is shifted backwards to free some space and Module 2 is ready for transport.

## Slide 10: VAX prototype and tests
Torque control;
Tightening screw’s turns control;
Robot friendly interface;
Minimum number of steps for the robot to operate the tightening (locking) screws;
Chain clamp size determines number of segments (chain links) so that working conditions potentially could be affected by the gravity.
intervention of robot (gripper or gripper with extension tool);
Intervention of personnel from ‘safe’ area using extension tool.
VAX Module 2 – chain clamp DN40
VAX Module interconnection – chain clamp DN100 in b.112
VAX Module 1 – remote handling in b.186
VAX chain clamps:
VAX remote operation:
VAX Module 3 – chain clamp DN100 in b.186
TTC CERN 06.02.2020

## Slide 11: Summary
Remote handling:
Cost;
Accessibility;
Time consuming;
  To remove 1 chain clamp at 5mSv/h
  Robot: 15-30 min (0µS);
  Torque wrench: 3 minutes (250µS);
No dose to personnel;
Robot vs. human leverage to be always considered.
Chain clamp connection assembly:
Quick solution to ‘bolted’ connections in terms of remote handling;
Simple and robust solution;
Design depends on:
  maintenance scenario;
  available space (space required for the surrounding mechanical system);
  Accessibility;
Disadvantage to grease the clamp.
TTC CERN 06.02.2020
[3]

## Slide 12: Thank you
lukasz.piotr.krzempek@cern.ch
+41 22 76 62101
CERN 112/1-015
TTC CERN 06.02.2020

## Slide 13: References
TTC CERN 06.02.2020
[1] J. Chauré - Intégration de blindages mobiles en LSS7 pour YETS et Long Shutdown 10th October 2018;
[2] J. Hansen – LIU PSB Work package description&Project status 18th June 2012;
[3] J. A. Ferreira – CERN experience: Vacuum design, interventions and operation in radioactive environment 22nd-24th November 2017