## Slide 1
STEAM Architecture Workshop 13-14 June 2019
Michał Maciejewski
on behalf of the STEAM team
cern.ch/STEAM

## Slide 2: Superconducting Accelerator Circuits – Numerical Challenges
PI
Iref
-
+
Network model of a circuit
Differential-algebraic equations
Varying time constants ~1 ms (switch) - ~10 min (circuit discharge)
Varying geometric scales ~10 cm (diode) - ~10 km (circuit)
~10 k elements
Non-linear behaviour
Field/network model of a magnet
Controller Model
Differential-algebraic equations
Fixed frequency of operation
10-100 elements
Non-linear behaviour
Partial differential equations
Varying time constants ~10us (quench) - ~10ms (losses)
Varying geometric scales ~10 um (filaments) - ~10 m (magnet)
~10 k degrees of freedom
Highly non-linear material properties and equations
R
U
A
M2
M154
Multi-Domain, Multi-Physics, Multi-Rate and Multi-Scale Problem
Busbar Model
Partial differential equations
Varying time constants
Adaptive mesh refinement
~1k elements
Non-linear behaviour

## Slide 3: Simulation of Transient Effects in Accelerator Magnets - Our Solution
Multi-domain – dedicated, domain-specific numerical tools
Multi-physics – strong coupling in single model, weak coupling of independent models
Multi-rate – interaction, coupling of two or more models
Multi-scale – interaction, coupling of two or more models
No free lunch theorem – One tool can not simulate it all!
LHC
We use our models for performance evaluation of SC magnets and circuits for

## Slide 4: STEAM Overview
STEAM is a simulation framework to study transient effects in SC magnets.
STEAM consists of five pillars:
Numerical tools  standalone, co-simulation
Model generation API
Tool adapter API
Meta-Methods co-simulation, optimization
Front-end to interact with APIs
4. Meta-Methods (Co-simulation, optimization)
2. Model-Generator
APIs
5. Frontends (Jupyter, Matlab)
3. Tool Adapter APIs
1. Tools
(BBQ, ProteCCT, LEDET, ANSYS, COMSOL, PSIM, PSpice, LTSpice, QLASA)
We believe that with STEAM there is place for everything
and everything is in place

## Slide 5: Presentation Outline
Introduction - Challenges
STEAM Architecture
STEAM Tools
STEAM Model-Generator APIs
STEAM Tool Adapter APIs
STEAM Meta-methods: Co-simulation
STEAM Frontends: Notebooks
Conclusion

## Slide 6: 1. Model Completeness
Model
completeness
Model completeness
Computation time
0D
1D
2D network
2D FEM
3D Analytical
3D FEM + Analytical
3D FEM
Considering thermal models:

## Slide 7: 1. Qualities of good models
High Fidelity
Model Credibility
Linked to Decision Support
Understandable and Well-Organized
Well formed for Optimization
Clear Scope
Course on Architecture and Systems Engineering: Models and Methods to Manage Complex Systems, MIT Professional Education
Internally Consistent
Elegant
Analyzable and Traceable
Data Extrapolation
Availability of Interfaces
Reusable

## Slide 8: 1. Available Tools
Models are subject to continuous verification and validation
 | Power Converter Controller | Superconducting Circuit | Superconducting Busbar | Superconducting Magnet
Equation type | Differential-algebraic | Differential-algebraic | Partial-differential | Differential-algebraic (network) Partial-differential (field)
Time-stepping | Fixed | Adaptive | Adaptive | Fixed Adaptive
# DOF | ~10 | ~10-10k | ~1k | ~1k-10k
Dimension | 0D | 0D | 1+1D | 0D, 1D, 2D
Physical Domains | - | Electric | Thermal | Magnetoquasistatic Thermal Mechanical

## Slide 9: 1. Available Tools
Models are subject to continuous verification and validation
 | Power Converter Controller | Superconducting Circuit | Superconducting Busbar | Superconducting Magnet
Equation type | Differential-algebraic | Differential-algebraic | Partial-differential | Differential-algebraic (network) Partial-differential (field)
Time-stepping | Fixed | Adaptive | Adaptive | Fixed Adaptive
# DOF | ~10 | ~10-10k | ~1k | ~1k-10k
Dimension | 0D | 0D | 1+1D | 0D, 1D, 2D
Physical Domains | - | Electric | Thermal | Magnetoquasistatic Thermal Mechanical
ProteCCT
LEDET
QLASA
We use proprietary tools for the sake of their verification and long-term support.
We use in-house tools due to their efficient implementation of custom physics.
Proprietary
In-house

## Slide 10: 2. Model-Generator APIs - Single source of truth
Our goal is to provide a tool-independent, versionable model description.
- A. Verweij, project owner
Inevitably models reflects engineer’s style  How to standardize them?
Differences in GUI models are difficult to capture  How to compare them?
In-house tools typically developed by a single person  How to maintain them?
In-house tools typically implement own equations, solver, etc  How to verify them?

## Slide 11: 2. Model-Generator APIs - Single source of truth
Magnet modelling
Excel files difficult to version (can contain math)
Difficult to visualize geometry
Dependency on ROXIE field maps
Scripted geometry and parameters
Automatic generation of models
COMSOL open for modifications
Circuit modelling
PSpice GUI difficult to version
GUI models difficult to interpret
No API for GUI models
Netlist – scripted circuit description
Reusability of static libraries
Automatic generation of models and post-processing
Input model parameters are separated from the tool itself.
(WYSIWYG approach)
STEAM-SING
STEAM-SIGMA
STEAM-LEDET

## Slide 12: 2. Library of Material Properties
Repository of material properties in:
  C
  MATLAB
Automated testing routine
References to existing measurements
https://gitlab.cern.ch/steam/steam-material-library
Input model parameters include also a subset of material properties.

## Slide 13: 3. Tool Adapter API
Tool Adapter is a model-independent interface for simulation tools capable of
Setting/getting parameters
Controlling simulation time
Writing input
Reading output
Such an interface can be used for:
Cooperative simulations
Parametric studies
Optimization

## Slide 14: 4. Cooperative Simulation - Motivation
Suitable to study interaction of models characterized by different
dynamical behavior: fast vs slow, fixed vs adaptive time stepping
mathematical formulation: ordinary vs partial differential equations
geometrical scales: phenomena occurring at micro vs macro scales, different mesh
physical phenomena: migration between tools can be time consuming
Iteration until convergence is reached

## Slide 15: 4. Cooperative Simulation: STEAM CoSim
Co-simulation
Scenario
TA1
API
Ports
TA2
API
Ports
TAn
API
Ports
List of Tool Adapters
Co-simulation time and iteration loops
t
T1
T2
T3
Tw
Time Window
Definition
Hierarchical
Co-simulation
…
1
2
t
T1
T2
Tw
Supported tool adapters:
PSIM
LTspice
PSpice
COMSOL: SIGMA&BBQ
ANSYS
LEDET
ProteCCT
QLASA
Supported co-simulation methods:
One-way coupling
Weak coupling
Strong coupling
Waveform relaxation

## Slide 16: 4. Cooperative Simulation: Mesh-Based Interpolation
M. Maciejewski, et al., "Coupling of Magnetothermal and Mechanical Superconducting Magnet Models by Means of Mesh-Based Interpolation", IEEE Transactions on Applied Superconductivity
Mesh-based interpolation
Magneto-thermal model
Mechanical model
Mesh-based interpolation
Coupling Environment
Magneto-thermal models are solved with COMSOL and problem-specific mesh
Mechanical models are solved with ANSYS and problem-specific mesh
Magneto-thermal load on the magnet during the energy discharge is relevant for Nb3Sn superconductors
MpCCI supports many other numerical codes: JMAG, Flux, Abaqus, MSC, …

## Slide 17: 4. Simulation Scheme for Intermittent Short Analysis
PSpice: Solves Netlist Provided by MATLAB (3 simulations in total)
MATLAB: - Main Loop Interface
- Numerical Integration
- Simulation data exchange using STEAM PSpice Manager
Courtesy A. Liakopoulou

## Slide 18: 5. STEAM Frontend Notebooks - Models as repositories of data
A typical modelling work includes
creation of model,
running some simulations
post-processing results
summarizing results (paper, report, presentation)
Especially important while working for future magnets when we only have models
Often times the link between the model, its results and report is broken.
With the use of APIs and scripts, part of this process can be integrated into a notebook.
This way model becomes a repository of data queried to provide relevant information.
Models
Results
Analysis scripts

## Slide 19: Presentation Outline
Introduction - Challenges
STEAM Architecture
STEAM Tools
STEAM Model-Generator APIs
STEAM Tool Adapter APIs
STEAM Meta-methods: Co-simulation
STEAM Frontends: Notebooks
Conclusion
STEAM Code Conventions
STEAM Continuous Integration Pipeline
STEAM Application – FCC Design

## Slide 20: STEAM Code Convention - Implementation
9 c 2015, Clean code development workshop, jointly with MPE-MS
13 Aug 2015, Object-oriented programming workshop, jointly with MPE-MS
Stand-up meetings @10AM
Shared coding convention became a language for the team work and discussion with experts
https://espace.cern.ch/steam/_layouts/15/start.aspx#/SitePages/Naming%20conventions.aspx
Our naming convention:

## Slide 21: STEAM Continuous Integration Pipeline – Implementation*
git commit
build_job
dependencies
build image
fatJar
uploadArchives
sonarqube
Project versioning
Project
development
External
dependencies
Internal
dependencies
Code analysis
Testing
Frontends
STEAM APIs
model inputs
The pipeline automatically executes project build, testing, sharing, and analysis.
This ensures the maintainability of the project.
*Strong cooperation with TE-MPE/MS (K. Król, JC. Garnier)

## Slide 22: STEAM Application – FCC Main Dipole Circuit Layout and Protection Design
FCC Week 2018: https://indico.cern.ch/event/656491/
Models: PSpice, COMSOL, LEDET, ANSYS
Model generator API: SING, SIGMA
Meta-methods: CoSim, mesh-based interpolation
Frontends: PSpice Manager, CoSim viewer
Circuit model
2800 components
PSpice
PC
Rfilt
Cfilt
REE
M1
M2
M22
M44
M43
M23
Mn
Lfilt
Mn+1
CLIQ
QDS
Electro-thermal magnet model
400 turns
Quenching magnet:
CLIQ simulation
Neighbouring magnet:
Simulation of voltage response
Courtesy
M. Prioli

## Slide 23: STEAM Application – FCC Main Dipole Circuit Layout and Protection Design
FCC Week 2018: https://indico.cern.ch/event/656491/
Courtesy
M. Prioli
  Cos-theta
  Block coil
  Common coil
Protection design involved, among others, T. Salmi, B. Auchmann

## Slide 24: Design phases for the FCC dipole magnets
Electromagnetic design
Objectives:
Peak field
Field quality
Simulation Tools
Physical Domains
Final
Magnet
Design
Electro-magnetic
Roxie
LEDET
Courtesy
M. Prioli

## Slide 25: Design phases for the FCC dipole magnets
Electromagnetic design
Objectives:
Peak field
Field quality
Mechanical design
Objectives:
Peak stress during various phases (assembly, cool-down, powering)
Simulation Tools
Physical Domains
Final
Magnet
Design
Mechanical
ANSYS
LEDET
Courtesy
M. Prioli

## Slide 26: Design phases for the FCC dipole magnets
Electromagnetic design
Objectives:
Peak field
Field quality
Mechanical design
Objectives:
Peak stress during various phases (assembly, cool-down, powering)
Quench protection design (CLIQ)
Objectives:
Hot-spot temperature
Peak voltage to ground
Simulation Tools
Physical Domains
Final
Magnet
Design
Electro-magnetic
Thermal
COMSOL
LEDET
Courtesy
M. Prioli

## Slide 27: Design phases for the FCC dipole magnets
Electromagnetic design
Objectives:
Peak field
Field quality
Mechanical design
Objectives:
Peak stress during various phases (assembly, cool-down, powering)
Quench protection design (CLIQ)
Objectives:
Hot-spot temperature
Peak voltage to ground
Circuit design
Objectives:
Discharge time
Peak voltage to ground
Simulation Tools
Physical Domains
Final
Magnet
Design
Electro-magnetic
Thermal
COMSOL
PSpice
LEDET
M. Prioli et al.: “The CLIQ quench protection system applied to the 16 T FCC-hh dipole magnets”, IEEE Transactions on Applied Superconductivity, accepted for publication
Courtesy
M. Prioli

## Slide 28: Design phases for the FCC dipole magnets
Electromagnetic design
Objectives:
Peak field
Field quality
Mechanical design
Objectives:
Peak stress during various phases (assembly, cool-down, powering)
Quench protection design (CLIQ)
Objectives:
Hot-spot temperature
Peak voltage to ground
Circuit design
Objectives:
Discharge time
Peak voltage to ground
Quench mechanics
Objectives:
Peak stress during quench protection
Simulation Tools
Physical Domains
Final
Magnet
Design
Electro-magnetic
Mechanical
Thermal
COMSOL
ANSYS
LEDET
M. Prioli et al.: “The CLIQ quench protection system applied to the 16 T FCC-hh dipole magnets”, IEEE Transactions on Applied Superconductivity, submitted for publication

## Slide 29: Conclusion
A solid base of the STEAM framework is now established and ready to be used for all kinds of simulations on SC circuits for actual and future accelerators.
STEAM has already been used for many studies, especially:
    Fault scenario’s in the LHC
    HiLumi triplet circuit
    FCC magnet and circuit protection
    “RB+11T” circuit
We have acquired a lot of competence in the MPE-PE section in co-simulation and individual tools