## Slide 1
STEAM-SIGMA Workshop 13-14 June 2019
Michał Maciejewski, Carmelo Barbagallo, Barakat-Ullah Bokhraie
on behalf of the STEAM team
cern.ch/STEAM
Notes: Truly inspiring intellectual journey

## Slide 2: STEAM Integrated Generator of Magnets for Accelerators
LHC – MB
Hi-Lumi – MQXF
FCC – Cos
Test station – FRESCA2
Other models: 11 Tesla, D1, … and many more!
FCC – Common coil
FCC – Block coil
Magneto-thermal 2D models provide a good approximation of magnet behavior during transients.
Need for automatic model generation
Many different magnet types
Implementation of custom equations requires model updates
Manual model creation prone to errors
Magnet designs for new magnets under continuous modifications

## Slide 3: Outline
Introduction
Physics
Architecture
User input
Conclusion
LHC – MB
Hi-Lumi – MQXF
FCC – Cos
Test station – FRESCA2
Other models: 11 Tesla, D1, … and many more!
FCC – Common coil
FCC – Block coil

## Slide 4
IFCC
ISCC
Eddy
Magnetic Vector Potential
Thermal Balance Equation
Helium
Heaters
CLIQ
STEAM-SIGMA – Physics Overview
COMSOL models generated with STEAM-SIGMA implement strongly coupled magnetoquasistatic, thermal and network equations.
Models provide an interface for co-simulation in a current- and voltage-driven modes.

## Slide 5
CERNcourier.com
How to discretize a superconducting cable?
~100 um
Wilson / Verweij equivalent magnetization
Formulation
Equivalent Tau formulation
Constitutive law
Ampere-Maxwell Law
If the eddy-currents paths are known a priori, the equivalent magnetization effect can be directly related to the change of magnetic flux density
Faraday-Lenz + Ampere-Maxwell
Currents’ paths don’t have to be resolved anymore!
We found an issue in this formulation.
Suitable for external field without imposed current
See next slides.
STEAM-SIGMA – Physics: Inter-Filament Coupling Currents

## Slide 6
Given a Rutherford cable, is decomposed in three contributions
A generic turn cross-section, with its local reference system
The three contributions are formulated as
The symbol indicates the average of along
The equivalent tau are in first approximation function only of the cable parameters, and they are given as
STEAM-SIGMA – Physics: Inter-Strand Coupling Currents
Notes: Focus on LHC scale (Mt. Blanc, Airport)

## Slide 7
The iron yoke is laminated
Only the structural copper wedges are considered
Wedges do not form a closed loop. A constraint is necessary, to prevent a net current.
COMSOL in-built Coil feature
The Coil feature is stable
The figure shows the eddy currents patters during a CLIQ discharge in an MB magnet
STEAM-SIGMA – Physics: Eddy Currents

## Slide 8
Inter-filament and inter-strand coupling losses are associated to the magnetic energy density function
Losses in wedges are calculated using the Joule’ Law
CLIQ discharge
STEAM-SIGMA – Physics: Electromagnetic Losses

## Slide 9
[9] Russenschuck, Stephan. Field computation for accelerator magnets: analytical and numerical methods for electromagnetic design and optimization. John Wiley & Sons, 2011.
Losses are calculated using the Joule’ Law
The transition across the critical surface is smoothened with the use of a Sigmoid function
is averaged over the turn domain
calculate with the peak of and the average of
(y0*exp(xc*r0)+y1*exp(r0*x))/(exp(xc*r0)+exp(r0*x));
Current sharing
[Ωm]
[K]
STEAM-SIGMA – Physics: Heat Balance Equation
Thermal Balance Equation

## Slide 10
Materials C library (versioning, storage)
C compiler: Visual C++ Build Tools
Dynamic Link Library (immutability)
COMSOL external function
T [K]
B [T]
J [A/mm2]
k [W/m/K]
T [K]
B [T]
Cp [J/kg/K]
T [K]
B [T]
STEAM-SIGMA – Physics: Nonlinear Materials

## Slide 11: STEAM-SIGMA - Architecture
Functional layers
INPUT: The user defines the magnet’s model, in terms of
domains (geometry, materials, cables).
FORMULATION: the magnet object is built in Java
as a generic array of domains.
IMPLEMENTATION: The magnet built in COMSOL.
Definitions Magnet Composition of Domains
Domain Composition of Elements sharing the same material
and physics laws
Element Geometrical object with unique label

## Slide 12
STEAM-SIGMA – Geometry Module
Point
Area
HyperArea
HyperLine
Elliptic Arc
Arc
Geometry
Halfturn
Coil
Winding
Line
Polygon
Pole
Strand
Block
Interface
translate
rotate
mirror - X
mirror - Y
Cable
Geometry module
Two logic sub-groups:
  fundamental geometrical objects
  coil-dedicated objects, specific for magnets
Circumference
coil
Pole
Winding
Block
Halfturn
Strands
HyperArea made of HyperLines [] Points []
Element
label
Pillars
Immutability
Encapsulation
Getters
Interface

## Slide 13
Handling
Geometry is automatically handled via the FEM workflow.
Geometrical objects are defined in Java, then implemented via the API
The elementary entity is a turn cross-section
Turns implemented as polygons
Entities
no Of Turns
User
STEAM-SIGMA – Geometry Module

## Slide 14: STEAM-SIGMA – Verification

## Slide 15: Construction of a High-Field Dipole Magnet - Geometry, Materials, Physics
Coil Insulation (Polymide, Glass Fiber )
Ampère's Law Linear
Thermal Balance (Passive)
Wedges ( Copper, Steel, )
Ampère's Law Linear
Weak constraint (Itot = 0)
Thermal Balance (Eddy Currents)
Coil (Nb3Sn, Copper, )
Ampère's Law Equivalent Magnetization
Persistent Magnetization
Thermal Balance (Dynamic Losses)
Quench transition

## Slide 16: Construction of a High-Field Dipole Magnet - Geometry, Materials, Physics
Outer Shell (Steel – Aluminum, )
Ampère's Law Linear
Thermal Balance (Eddy Currents)
Iron Yoke (Laminated Iron, )
Ampère's Law Non Linear
Thermal Balance (Hysteresis)
Collars (Laminated Steel )
Ampère's Law Linear
Thermal Balance (Passive)

## Slide 17: Validation of a High-Field Dipole Magnet

## Slide 18: Validation of a High-Field Dipole Magnet

## Slide 19: Model Construction with SWAN - demo

## Slide 20: STEAM-SIGMA – Documentation
Minor updates
Documentation of the public API (demo)

## Slide 21: New features
Enhanced Automation of Model Generation - Barakat-Ullah Bokharaie
Inter-Filament Coupling Currents Modelling – Carmelo Barbagallo

## Slide 22: Enhanced Automation of Model Generation
Author: Barakat-Ullah Bokharaie
Supervisors: Matthias Mentink
STEAM workshop, 13th June 2019

## Slide 23: Revision of STEAM’s SIGMA Tool
Purpose of revision:
  Reduction of computation times
  Increased usability
    Automatic definition of Quench Heaters
    Automatic creation of correct study settings
    Automatic creation of mesh
Reduction of computation times:
  General:
    ↑ Complexity  ↑ Variables  ↑ Time
  Global description rather than individual
  Results:
    Reduction by a factor of up to 15

## Slide 24
Geometry
Materials
Thermal properties
Low-field Quench Heaters =
High-field Quench Heaters =
MQXF magnet model for High-Lumi LHC
Increased usability Automatic definition of Quench Heaters

## Slide 25
Correct study settings:
  Stationary study
  Time dependant study
  Relevant physics
  Solver settings
25
Increased usability Automatic creation of correct study settings and mesh
Mesh settings:
  Mapped
  Triangular
Meshed MQXF magnet model

## Slide 26: Inter-Filament Coupling Currents Modelling
Author: Carmelo Barbagallo
Supervisors: Matthias Mentink and Arjan Verweij
STEAM workshop, 13th June 2019

## Slide 27: Introduction
Strand magnetization
Finite Element Method is used to solve the following MQS equation for individual strands:
Inter-filament coupling currents (IFCCs) in the strands of a superconducting cable are modelled by using an additional magnetization term (in Am-1):
is due to small closed current-carrying loops;
The magnetizing current is divergence-free.
Magnetoquasistatic (MQS) PDE
Rutherford cable (real image)
Aim of the study: how does homogenization affect IFCCs behavior on superconducting cables and magnets.

## Slide 28: Stack of four Rutherford cables – Homogeneous vs Multi-strand model
Stack of four Rutherford cables submitted to an external varying magnetic field;
Dstrand=0.9 mm, ;
Homogenisation density factor to compensate discretization error in the homogenised model;
Multi-strand model: same field amplitude but lower time constant than the homogenised model.
Multi-strand model
Homogenised model

## Slide 29: Future studies for IFCCs modelling on superconducting magnets
Equations were implemented in COMSOL by using Dode (Domain ODEs and DAEs) module;
Same field amplitude and time constant for homogenised and multi-strand model.
Modified Homogenisation Formulation
Equivalent Resistivity Formulation
COMSOL coil feature:
(coil excitation);
Strand border electrical conductivity applied to the conductive border of thickness :
Field amplitude and time constant in accordance with expectations;
The implementation on cable stacks is under study.
→
equivalent
Decay term
Driving term
because
(in S/m)
where is the resistivity of the border and Rs the strand radius.

## Slide 30: Magneto-thermal analysis with CLIQ protection system for FRESCA2 magnet
FRESCA2 Nb3Sn dipole magnet
(developed within a collaboration between CERN and CEA Saclay)
Magnetic field: 13 T;
Block coil design with 4 double pancake coils: 42 turns outer layer, 36 turns inner layer;
Cable: 40 strands of 1 mm;
Bladder and key concept for loading;
Homogenised model
(based FRESCA2 model created by L. Bortot)
Image: G. Willering
Multi-strand model
Magnetic flux density is in agreement with expectations;
IFCCs losses are different in the two models.

## Slide 31: Magneto-thermal analysis with CLIQ: Homogenised model vs Multi-strand model
The slopeis 35% lower in the multi-strand model. Furthermore, after the initial fluctuation, the discharge in the two models is similar. This outcome explains why we have noticed so far a higher than expected in all homogenised models of magnets;
Losses due to IFCCs are, as consequence, lower of a factor two in the multi-strand model than in the homogenised one;
Results are encouraging, however further studies are required to understand the differences noticed between the two models.

## Slide 32: Conclusion
We can automatically generate COMSOL models
We are extending this approach to build LEDET and ANSYS models
We are enhancing automatic model generation capabilities
We identified an issue with equivalent magnetization and work on a solution
We used STEAM-SIGMA for LHC, HL-LHC and FCC magnet studies

## Slide 34: STEAM-SIGMA – Code Quality
Feature | 26.09.18 | 05.02.19
Bugs | 117 | 0
Vulnerabilities | 97 | 2
Code smells | 8.2 k | 36
Tech. debt | 85 d | 3 d
LoC (code+doc) | 15 k | 15 k
Most frequent issues:
No documentation
Coding conventions violated
Logic errors
Code duplications
Missing and failing tests