## Slide 1: SLS booster emittance exchange
Jonas Kallestrup :: PhD student :: Paul Scherrer Institut
Advanced Low Emittance Rings Technology workshop, 11-07-2019

## Slide 2: Outline
Motivation
Emittance redistribution
SLS booster overview
Measurements
  Coupling
  Tune along ramp
  Emittance exchange
Damping effects
Outlook
Summary

## Slide 3: Motivation
The new generation of storage ring-based light sources are be based on Multi-Bend Achromat (MBA) lattices with very strong focusing and low dispersion achieving < 250 pm∙rad horizontal emittance.
A common consequence is a rather limited dynamic aperture of typically ~5-10 mm.
  SLS 2.0 CDR: 5 mm dynamic aperture when including errors for m
Existing 3th generation storage ring often inject using horizontal off-axis injections
  Low dynamic aperture of new rings makes this challenging!
  Upgrade projects often reuse injector complex! (Boosters w. nm∙rad)
New on-axis injection schemes under development
  Technology not mature yet…
  Off-axis still pursued as a „safe“ choice: we know how to do it!

## Slide 4: Motivation
Several tricks can be used to improve off-axis injection efficiency or give safety margin
  High-β region for injection
  „Anti-septum“
  See previous talk by M. Aiba
Booster and transfer line initiatives
  Reduction or Redistribution of booster emittances
Bump on
Bump off
Aperture required

## Slide 5: Motivation
Several tricks can be used to improve off-axis injection efficiency or give safety margin
  High-β region for injection
  „Anti-septum“
  See previous talk by M. Aiba
Booster and transfer line initiatives
  Reduction or Redistribution of booster emittances
New aperture required!

## Slide 6: Emittance redistribution: sharing
The transverse emittances can be redistributed by using the nonzero coupling of the machine
Round beam is achieved by moving tunes to the coupling difference resonance:
Leads typically to a ≈50% reduction of horizontal emittance
ESRF Booster: From 120/5 nm∙rad to 60/60 nm∙rad!
Vertical dynamic aperture is plentiful
  Move all horizontal emittance to the vertical plane!

## Slide 7: Emittance redistribution: exchange
A complete exchange of transverse emittances can be achieved by crossing the coupling resonance
  Observed at the Proton Synchrotron (2001)
When Δ decreases, decreases, increases
When Δ = 0, =
When Δ increases on the other side of the resonance
Goal: Cross the coupling resonance quickly and extract immediately after!
How: Rapid modification of quadrupole family ramp
Δ: betatron tune separation |C|: coupling coefficient

## Slide 8: Emittance redistribution: exchange
A complete exchange of transverse emittances can be achieved by crossing the coupling resonance
  Observed at the Proton Synchrotron (2001)
When Δ decreases, decreases, increases
When Δ = 0, =
When Δ increases on the other side of the resonance
Goal: Cross the coupling resonance quickly and extract immediately after!
How: Rapid modification of quadrupole family ramp
Δ: betatron tune separation |C|: coupling coefficient

## Slide 9: SLS booster: overview
Highlights
First booster built specifically for top-up operation
Mounted on inner wall of Storage Ring tunnel
  ≈ same circumference as SR
Low horizontal emittance
  Vertical emittance probably ~2-3 nm.rad while minimum is 0.05
Tune are relatively close
Digital magnet power supply control
Dipoles with quadrupole + sextupole components
  Quadrupole families for dispersion and tune control
Relatively weak and inexpensive magnets
Extremely flexible and easily controllable!

## Slide 10: SLS booster: overview

## Slide 11: SLS booster: QF family
Digitally controllable in 4000 steps along full ramp
  ≈ 88 turns / step ≈ 79 μs / step.
  Quite nice resolution!
Maximum current: 140 A

## Slide 12: Closest Tune Approach measurements
Coupling is measured using the Closest Tune Approach at the top of the ramp
‘Natural’ coupling is substantial:
  |C| = 0.019
  No need for additional skew quadrupoles
=|C|

## Slide 13: Tune along ramp
Goals:
Cross the coupling resonance quickly to achieve the emittance exchange
Extract beam shortly after to avoid damping
Waterfall plot of FFT of Turn-by-Turn BPM data

## Slide 14: Tune along ramp
Goals:
Cross the coupling resonance quickly to achieve the emittance exchange
Extract beam shortly after to avoid damping
Waterfall plot of FFT of Turn-by-Turn BPM data

## Slide 15: Tune along ramp
Goals:
Cross the coupling resonance quickly to achieve the emittance exchange
Extract beam shortly after to avoid damping
Waterfall plot of FFT of Turn-by-Turn BPM data

## Slide 16: Results
Beam size measured on OTR in Booster-to-Ring transfer line
Emittance Exchange process measured by extracting at earlier times over many ramp cycles
Assuming β, η constant during quadrupole sweep
Not a “big” change but remember: nm∙rad

## Slide 17: Results
Test of injections with limited aperture by inserting horizontal scraper
Scraper can be inserted further without loss of charge when using emittance exchange
Fitting Cumulative Distribution Function

## Slide 18: Emittance redistribution: Radiation damping
Damping is a necessary evil for emittance exchange
  Quadrupole power supplies must ‚beat‘ the damping
  Rule of thumb (1):
                5-15 ms
To gain maximum emittance exchange, the tune sweep must start and end far away from the resonance
  Rule of thumb (2):
  Our measurements:
  ms, ms
          ,

## Slide 19: Emittance redistribution: Radiation damping
  Rule of thumb (1):
                5-15 ms
  Rule of thumb (2):
Crossing time depends on ramping speed and the total tune shift:
Relief constraints on power supplies
  Decrease |C|
  BUT: smaller |C| needs longer crossing time to do the exchange adiabatically*
   Increased radiation damping
* See averaging of single particle emittance in: A. Franchi, E. Métral, R. Tomás, “Emittance sharing and exchange driven by linear betatron coupling in circular accelerators” eq. 20 & 21

## Slide 20: Improvements for future measurements
Rule of thumb (2) was not fulfilled:
  Starting point too close to resonance
  Damping already plays a role decreasing efficiency of exchange
Currently no reliable measurement of emittances
  Betatronic and dispersive beam size contributions approximately equal
   standard quadrupole scans not useful
  Attempts with multi-quad, multi-screen scans in progress
Minimization of  larger reduction of
  Currently, 2-3 nm∙rad and we hope to get < 1 nm∙rad
  Orbit correction: currently only 2 BPMs in booster

## Slide 21: Outlook
Emittance exchange successfully tested: many future and existing facilities might apply this technique depending on their booster and injection scheme
High-emittance (≥ 50 nm) boosters can have a significant relaxation of required horizontal acceptance, since vertical emittance is typically less than 5 nm
  Large emittance does not imply longer crossing times
Easy to implement:
  Does (should) not require modifications of booster or transfer line hardware
  Exploits ‘natural’ coupling of the machine

## Slide 22: Summary
Upgrade projects tend to reuse existing injector complex
Small dynamic aperture make off-axis injections challenging
The booster emittance can be redistributed through emittance exchange by coupling resonance crossing before extraction
A factor 4 (3.6) decrease (increase) in horizontal (vertical) emittance achieved in SLS booster
  Close to full exchange!
  Can be useful for other existing and future facilities and (almost) immediately applied

## Slide 23: Summary
Thank you for your attention!

## Slide 24: Extra slides

## Slide 25: Crossing speed dependency
Best exchange for the crossing with a “crossing time” of ≈2200 turns.
Small machine coupling: Longer crossing time needed
  Radiation damping becomes important
    Additional coupling needed
      Additional skew quadrupole needed
Power supply can’t follow

## Slide 26: Crossing speed dependency
Consequences of low coupling: mismatch of emittance
  If coupling is small, then a longer crossing time is needed to do a proper emittance exchange without mismatch of the emittance.
  If crossing time is too short, the emittance exchange becomes nonadiabatic.
  If crossing time is too long, radiation damping & quantum excitation will play a role.
  Skew quadrupoles might be needed if coupling is too small.

## Slide 27: Results
Movie of measured beam profile
  Emittance exchange is not very visible due to large dispersion at OTR monitor
  ( m measured