## Slide 1: CMS HGCal: Research Update
Gwen Gardner
May 20th, 2019

## Slide 2: Review
PetaLinux
Zynq/Zedboard
GBTSCA
Last time:
Using scp’d scripts + on-Zynq development to communicate with GBTSCA
scp’d scripts
Notes: I’m sure you guys remember what I’ve been up to.
This setup has mostly just been for practice -- the important part is learning how to work with the Zynq SoC.

## Slide 3: Further I2C Progress
Can write and read successfully, and scripts return read values
  Requires two directions of communication
Tested running commands in immediate succession
  Some issues with EEPROM
GBT-SCA
I/O Expander
ADC
Temp Sensor
EEPROM
3
LEDs
I2C
Zynq
Zedboard
GBT-SCA
FMC
HDLC

## Slide 4: New kind of root filesystem!
“Stationary” rootfs
Before: “INITRAMFS” | Now: SD card
Linux kernel contains a “zipped” version of the rootfs Rootfs is “unzipped” at boot On-Zynq development does not survive reboot Limited size | Partitioned SD card BOOT, rootfs Kernel directly mounts rootfs partition On-Zynq development survives reboot Size only limited by SD card

## Slide 5: Automating the build process
Some challenges:
Bypassing the PetaLinux configuration “menu”
Incorporating someone else’s code
The fragile nature of PetaLinux