## Slide 1: DFM Safety aspects (cryogenic safety only)
Y.Leclercq, V.Parma, TE-MSC
Th.Otto (TE DSO and HL LHC Safety Officer)
CERN, Technology Department
DFM Conceptual Design Review, CERN 21 June 2019

## Slide 2: Contents
DFM configuration
Cryogenic safety
  Risk assessment and sizing of safety
Summary

## Slide 3: DFM configuration and cryo safety parameters
MgB2-NbTi
Splices
Ø250 x 600
MgB2-NbTi splices
Top splices
Fill reservoir
Nominal level
+50mm
-50mm
10 min @ 2g.s-1
10 litres
16 min @ 20 W
8 litres
Fill reservoir
LHe inlet
Plug
Interlink
To D2 
← SCLink
to DFHm
100
Heaters volume
1020
Inlet reservoir
14 litres
100
20°
Vac. Inst.
∆P
IFS
Cold inst.
Vac. Inst.
Cold inst.
Electrical Heater
T-sensor
L-gauge
VB
plug
Helium vessel protection:
Pressure relief devices
    One burst disc (safety relief device)
    One pressure relief device sized to static heat loads
Vacuum vessel protection:
2 Pressure relief plates (on either side of VB)
Helium cold volume (V): 360 litres
Helium cold surface: 3.5 m2
PS = 2.5 bara
Pt = 3.5 bara
PSxV900  PED Cat.2.

## Slide 4: Scale of pressures, helium vessel
Pn Nominal pressure
Ps: Design pressure
Ptest: Test pressure
Pt: burst disk set press.
bar(a)
1.3 bar(a)
2.5 bar(a)
3.5 bar(a) (1.43 x Ps); 4.6 bar(a) in atm.
≤ 2.5 bar(a) (1.5 barg)

## Slide 5: PED category
Article 4, paragraph 3
Ps x V = 900 bar.L
With updated figures from CDR we are still in Cat.2
2.5
360

## Slide 6: Risk assessment matrix (as for DFX)
Remarks:
causes of excessive pressure are considered to be unrelated (single jeopardy theory) unless cause/effect exists
 | High Risk
 | Medium Risk
 | Low Risk:

## Slide 7: Retained pressure hazards (same as for DFX)
A) Accidental air venting of insulation vacuum with sudden condensation on cold surfaces, helium boil-off and pressure build-up  sizing of burst disk
C) Accidental release of cryogenic fluid from helium vessel to insulation vessel due to arc bursting helium envelope, helium pressurized at burst disk pressure, spill of helium inventory to vacuum vessel  sizing of vacuum vessel relief plate

## Slide 8: Safety relief devices sizing for DFM
Helium vessel burst disk:
Data:
  Cold surfaces exposed to Vacuum : 3.5 m2 (2.2 m2 wet surface)
  30 layers MLI on helium vessel
  Design Pressure = 2.5 bara
  Saturated liquid in nominal configuration
  Helium volumes in nominal operation : 210 litres liquid + 150 litres gaseous
Inputs:
  Vacuum break on 10 MLI layers : 6.2 kW/m2
  Power dissipated in liquid : 21 kW
Relief device sizing according to ISO21013-3
  ISO21013-3  Qm = 1.4 kg/s
  EN4126-6  Drelief > 28 mm
Insulation vacuum relief plates:
Preliminary sizing:
Assume orifice: DN50
Pt= 2.5 bara; Pb=0 bara; Trel= ~5 K
  Qmvessel = ~5 kg/s to the vac.vessel
Relief plate to limit ΔP to 0.5 barg (opens at 1.5 bara)
Assuming continuity of mass relief (conservative): Qmvessel = Qmrelief
   ~DN100  2 DN100 on either side of VB

## Slide 9: Summary
The equipment is Cat.2 of the PED
Preliminary sizing of burst disks and relief plates done
The location of the burst disk/rated valve and relief plates needs to be confirmed by the integration study with WP15

## Slide 10: Thank you ! Q/A