## Slide 1: Impact of flux jumps on orbit stability
D. Gamba, L. Fiscarelli, M. Martino, J. Coello de Portugal
150th HiLumi WP2 – 11 June 2019

## Slide 2: MBH HYBRID - Residuals and differential voltage
Current shows peaks related to voltage spikes σ = 0.3 units.
The difference of current minus flux shows changes σ = 0.2 units.
Gradient (up/dw) shows changes σ = 0.14 units.
σ is computed in the interval [2kA, 4kA]
MBH HYBRID
From L. Fiscarelli– 144th WP2 Meeting (indico)
Flux jumps seems to be concentrated at “low energy”

## Slide 3: Lucio’s conclusions
  We have tested many short models and we have data for the first full-size aperture (MBH HYBRID)
At the field levels (2-4 T) where there is more activity from flux jumps and during ramps at nominal ramp-rate (10 A/s) we see:
  fluctuations of the current (σ = 0.2 units)
  changes on the main field not related to the current (σ = 0.2 units)
  changes of the up-down gradient (σ = 0.15 units)
The spectral density of the flux jumps is mainly concentrated in the interval 0.1-10 Hz
From L. Fiscarelli– 144th WP2 Meeting (indico)
In this range PC don’t have a detailed specification!
-> still under discussion how to use “Noise”
From circuit point of view, we consider “linearity” and “Short term stability – 20 min” as boundary of “tracking” performance
This is the contribute of flux jumps according to Lucio

## Slide 4: Inductance Jump Model – O/C Voltage Loop
From M. Martino – 144th WP2 Meeting (indico)
I guess this value is computed in the 0.1 – 100 Hz range
11T Trim

## Slide 5: Inductance Jump Model – O/C Voltage Loop
From M. Martino – 144th WP2 Meeting (indico)
Main dipoles circuit

## Slide 6: Putting numbers together (11T)
flux jumps given in unit – worst case (in equivalent ppm) at top energy
PC specs given in ppm of Irated – worst case at injection
Impact of PCs in units computed as [ppm] * 10-2 * IPC rated/Idipoles(inj./nom.)
 | 11T Magnet/Trim | Main Dipoles
PC class | 3 | 1
Irated [A] | 600 | 13000
Iinjection [A] | (0) | 728
Inominal [A] | (250) | 11850
Short term stability [r.m.s. ppm] | 1 | 0.2
Linearity [r.m.s. ppm] | 4.6 | 1.2
Flux jump -> PC -> circuit [rms ppm] | 6.04 | 0.01
Flux jump [rms units of 1e-4] | 0.2 | -
Tot. PC [rms units] inj. / nom. | 0.063 / 0.004 | 0.217 / 0.013
Concerns here: flux jump on itself has an about 50 times bigger effect than PC stability at top energy
performance dominated by short term stability and linearity
Comparable values!

## Slide 7: Comparison: flux jumps statistics for RQX
From J. Coello de Portugal – 147th WP2 Meeting (indico)
MQX regulation response simulation
MBH measured flux jumps
145 jumps measured in the error of the magnetic flux ().
Average Std strength: 0.20.1 units.
Average Std length: 4010 ms.
244 jumps seen in the current deviation () of the regulation circuit.
Average Std strength: 0.060.03 units.
Average Std length: 6040 ms.
From a manual selection. Very probably biased towards larger strengths (easier to spot…).
Comparable effect as 11T trim
(due to comparable inductances?)

## Slide 8: Putting numbers together (Triplet)
Impact of PCs in units computed as [ppm] * 10-2 * IPC rated/IRQX(inj./nom.)
 | RQX | RTQX1/3 | RTQXA1
PC class | 0 | 2 | 4
Irated [A] | 18000 | 2000 | 60
Iinjection [A] | 1059 | (0) | (0)
Inominal [A] | 16470 | (1647) | (35)
Short term stability [r.m.s. ppm] | 0.2 | 0.6 | 2.5
Linearity [r.m.s. ppm] | 1.2 | 2.9 | 5.2
PC Short + Lin. [rms units] inj. / nom. | 0.207/0.013 | 0.056/0.004 | 0.003/ <0.001
Flux jump -> PC -> circuit [rms units] | 0.06/ <0.06? | ??? | ???
Tot. PC [rms units] inj. / nom. | 0.22/ <0.06? | ??? | ???
Circuit performance still dominated by PC stability (at least for RQX)
Values to be compared with 0.2 units flux jump expected in each single magnet, independently
  Comparable at injection for RQX circuit

## Slide 9: 11T: impact on B1 orbit at 15 cm β*, 7 TeV
P7
Main observation:
< 0.2 σbeam/unit @ TCPs
Main dipoles have a stronger local impact
same result for 40 cm β* at top energy
At injection:
Not very different behavior
  Optics around P7 is basically constant
about x4 less sensitive due to scaling of beam size with energy
x4 wrt injection
TCPs
Main dipole circuits

## Slide 10: Feed-down from IR1/5 triplet: impact on orbit
Beam 1
Point 1
Assuming pessimistic case of 295 urad half-crossing for all optics
  Kick linear with crossing angle
The lower the β* the most sensitive to ”jumps”
  Kick goes like sqrt(β) in the quadrupole
  40 cm β* is x1.6 less sensitive than 15 cm β*
Dominated by Q2.L1 (for B1)
  ~0.25 σbeam/unit @ TCPs
    per Q2L magnet!
  (~0.15 σbeam/unit @ TCPs per Q3R magnet)
B1 - 15 cm β*
RQX.L1
RQX.R1
MQX.2L1
TCPs
Notes: MQXFA.B3R1 with 15 cm beta*
TCP.D6L7.B1 (s=1.31e+04 [m] betx=1.47e+02 bety=7.21e+01 dx=6.68e-01): 1.81e-01
TCP.C6L7.B1 (s=1.31e+04 [m] betx=1.39e+02 bety=7.60e+01 dx=6.49e-01): 1.51e-01
TCP.B6L7.B1 (s=1.31e+04 [m] betx=1.32e+02 bety=8.02e+01 dx=6.30e-01): 1.46e-01
TCPCV.A6L7.B1 (s=1.32e+04 [m] betx=3.35e+01 bety=2.55e+02 dx=1.63e-01): 1.44e-01
TCPCH.A4L7.B1 (s=1.33e+04 [m] betx=3.42e+02 bety=6.49e+01 dx=-5.10e-01): 1.44e-01
TCP.6L3.B1 (s=2.65e+04 [m] betx=1.31e+02 bety=1.46e+02 dx=2.08e+00): 1.42e-01

## Slide 11: D1/D2: impact on B1 orbit at 15 cm β*, 7 TeV
P7
D1/D2 other main players for orbit stability
Based on Ni-Ti technology
  No flux jumps expected
Class 0 PC; 13 kA Irated
  Basically, same performance as RQX
TCPs

## Slide 12: Conclusion: impact on orbit at TCP @ inj / 15 cm β*
 | TCP orbit var. from optics [σbeam/unit] | Expected jitter [rms units] | Expected TCP orbit var. [rms e-3 σbeam]
11T magnet (flux jump) | 0.02 / 0.07 | 0.2 | 4 / 14
11T trim circuit | 0.04 / 0.14 | 0.063/0.004 | <1 / <1
RB.A78 circuit | 0.06 / 0.21 | 0.217/0.013 | 13 / 3
Q1 single magnet | <0.01 / 0.06 | 0.2 | <2 / 12
Q2 single magnet | 0.01 / 0.28 | 0.2 | 2 / 56
Q3 single magnet | <0.01 / 0.18 | 0.2 | <2 / 36
RQX main circuit | 0.01 / 0.48 | 0.22 / <0.06? | 2 / 29*
Q1 trim circuit | <0.01 / 0.10 | ~0.056? / ~0.004? | < 1? / < 1?
Q3 trim circuit | 0.01 / 0.33 | ~0.056? / ~0.004? | < 1? / 1?
D1/D2 circuit | 0.02 / 0.63 | 0.205 / 0.013 | 4 / 8
Thanks for your questions and comments!
The impact of flux jump at top energy for a 15 cm β* with 295 urad half crossing can reach up to 5.6% σbeam (MQX2) or 1.4% σbeam (MBH)
At injection energy dominated by main dipole PC (1.3% σbeam)
  in this case it should be a slow variation (<< 1 Hz), which can be corrected by orbit feedback, while a flux jump is a sudden variation (a few Hz)!
* Note: during stable beam, PC “linearity” should not play a role, i.e. about x6 better stability.

## Slide 13: Appendix

## Slide 14: 11T: impact on B1 orbit at injection
P7
TCPs
Assuming 1 unit variation on RTB8L7 circuit (2x11T magnets), RB.A78 and RB.A67 circuits, single MBH.A8L7 magnet
Impact on orbit at TCPs within factor 2 to 4 for a given amplitude.

## Slide 15: 11T: impact on B1 orbit at 15 cm β*, 7 TeV
P7
Not very different behavior than at injection
about 4 times more sensitive due to smaller beam size
x4 wrt injection
TCPs

## Slide 16: 11T: impact on B1 orbit at 40 cm β*, 7.5 TeV
P7
Computed on more recent optics with 11T in cell 9 instead of cell 8
No major differences wrt 15 cm β*
(In all cases, optics is the same around P7)
x4 wrt injection
TCPs

## Slide 17: Feed-down from IR1/5 triplet (295 urad xing)
15 cm β*
Injection

## Slide 18: Feed-down from IR1/5 triplet (295 urad xing)
15 cm β*
40 cm β* - 7.5 TeV

## Slide 19: Impact of D1/D2 elements
15 cm β*
Injection