## Slide 1
Status of the PIP-II project at FNAL
In partnership with:
India/DAE
Italy/INFN
UK/STFC
France/CEA/Irfu, CNRS/IN2P3
Eduard Pozdeyev
PIP-II Project Scientist
4th ICFA Mini-Workshop on Space Charge CERN, November 4-6, 2019

## Slide 2: Outline
LBNF/DUNE/PIP-II: Context and science objectives
PIP-II Project Overview and Design Highlights
PIP2IT – Testbed For PIP-II Critical Technologies
Recent Progress
Summary

## Slide 3: Fermilab at a Glance
Core expertise areas:
Particle Physics
  Neutrinos (LBNF/DUNE)
Accelerator technology and SRF
Detector development
High performance computing
Quantum computing
Outreach and education
America's particle physics and accelerator laboratory
6,800 acres of federal land
~1,800 staff
4,000 scientists from >50 countries use Fermilab facilities

## Slide 4
LBNF / DUNE / PIP-II
Powerful proton beams (PIP-II)
  1.2 MW upgradable to multi-MW (2.4 MW Phase 2) to enable world’s most intense neutrino beam with wideband capability
Dual-site detector facilities (LBNF)
  Deep underground cavern (1.5 km) of 70kt liquid argon fiducial volume
  A long baseline (1300 km)
Deep Underground Neutrino Experiment (DUNE)
  Liquid Argon – the next-generation neutrino detector
PIP-II ACCELERATOR

## Slide 5: DUNE Science Objectives
Neutrinos – most ubiquitous matter particle in the universe, yet the least understood. Opportunities for game changing physics discoveries:
Origin of matter Investigate leptonic CP violation, mass hierarchy, and precision oscillation physics
  Discover what happened after the big bang: Are neutrinos the reason the universe is made of matter?
Neutron Star and Black hole formation Ability to observe supernovae events
  Use neutrinos to look into the cosmos and watch the formation of neutron stars and black holes in real time
Unification of forces Investigate nucleon decay targeting SUSY-favored modes
  Move closer to realizing Einstein’s dream of a unified theory of matter and energy

## Slide 6
Fermilab Accelerator Complex
750 kW, 120 GeV
Fermilab operates the largest US particle accelerator complex, producing the world’s most powerful n beams, along with muon and test beams.
DUNE n beam
Booster n beam
SBN program
NuMI n beam
NOvA, MINERvA, MINOS+

## Slide 7
Fermilab Accelerator Complex
750 kW, 120 GeV
Fermilab operates the largest US particle accelerator complex, producing the world’s most powerful n beams, along with muon and test beams.
DUNE n beam
Booster n beam
SBN program
NuMI n beam
NOvA, MINERvA, MINOS+
P5 Recommendation: Upgrade the Fermilab proton accelerator complex to provide proton beams of >1 MW by the time of first operation of the new long-baseline neutrino facility.

## Slide 8: Fermilab’s Path to 1.2 MW on LBNF Target
Increase the number of protons per Booster pulse from 4.3e12 (present) to 6.5e12
Increase Booster rep. rate from 15 Hz to 20 Hz
Reduce Main Injector cycle from 1.33 s to 1.2 s
Implementation
PIP-II SRF linac, 800 MeV, 2 mA beam, painting injection
  Increased energy, reduced space charge, improved beam quality in the Booster
Increase in Booster injection energy, pulse intensity and repetition rate require upgrades to Booster, Recycler Ring (RR), and Main Injector (MI).

## Slide 9: PIP-II Scope Overview
800 MeV H− linac
  Warm Front End
  SRF section
Linac-to-Booster transfer line
  3-way beam split
Upgraded Booster
  20 Hz, 800 MeV injection
  New injection area
Upgraded Recycler & Main Injector
  RF in both rings
Conventional facilities
  Site preparation
  Cryoplant Building
  Linac Complex
  Booster Connection
The PIP-II scope enables the accelerator complex to reach 1.2 MW proton beam on LBNF target.

## Slide 10: PIP-II Site at Fermilab

## Slide 11: PIP-II Performance Requirements Defined
Linac | PIP-II | Current Performance (PIP)
Beam Energy (kinetic) | 800 MeV | 400 MeV
Particles per Pulse | 6.7 × 10 12 | 4.5 x 10 12
Average Beam Current in the Pulse | 2 mA | 25 mA
Pulse Length | 550 s | 30 s
Pulse Repetition Rate | 20 Hz | 15 Hz
Bunch Pattern | Programmable | CW pulsed
Booster | Value | 
Injection Energy (kinetic) | 800 MeV | 400 MeV
Extraction Energy (kinetic) | 8 GeV | 8 GeV
Particles per Pulse (extracted) | 6.5×1012 | 4.2x1012
Beam Pulse Repetition Rate | 20 Hz | 15 Hz
Recycler Ring / Main Injector | Value | 
Injection Energy (kinetic) | 8 GeV | 8 GeV
Extracted Beam Energy | 60-120 GeV | 120 GeV
Beam Power (120 GeV) | 1.2 MW | 0.75 MW
Cycle Time (120 GeV) | 1.2 sec | 1.33 sec
Potential Upgrades |  | 
Upgrade potential | 2.4 MW | N/A
Linac | PIP-II | Current Performance (PIP)
Beam Energy (kinetic) | 800 MeV | 400 MeV
Particles per Pulse | 6.7 × 10 12 | 4.5 x 10 12
Average Beam Current in the Pulse | 2 mA | 25 mA
Pulse Length |  | 
Pulse Repetition Rate | 20 Hz | 15 Hz
Bunch Pattern | Programmable | CW pulsed
Booster | Value | 
Injection Energy (kinetic) | 800 MeV | 400 MeV
Extraction Energy (kinetic) | 8 GeV | 8 GeV
Particles per Pulse (extracted) | 6.5×1012 | 4.2x1012
Beam Pulse Repetition Rate | 20 Hz | 15 Hz
Recycler Ring / Main Injector | Value | 
Injection Energy (kinetic) | 8 GeV | 8 GeV
Extracted Beam Energy | 60-120 GeV | 120 GeV
Beam Power (120 GeV) | 1.2 MW | 0.75 MW
Cycle Time (120 GeV) | 1.2 sec | 1.33 sec
Potential Upgrades |  | 
Upgrade potential | 2.4 MW | N/A

## Slide 12: PIP-II 800 MeV Linac 5 Types of Cavities, 23 Cryomodules, 119 Cavities
HWR
1 CM
8 Cav
162.5 MHz
SSR1
2 CM
16 Cav
325 MHz
SSR2
7 CM
35 Cav
325 MHz
LB650
9 CM
36 Cav
650 MHz
HB650
4 CM
24 Cav
650 MHz
RFQ
2.1 MeV
10 MeV
32 MeV
177 MeV
516 MeV
833 MeV

## Slide 13: SRF Linac Lattice Developed
End-to-End tracking simulations performed with realistic 3D fields
  TraceWin and TRACK give nearly identical results
No loss, no halo growth detected
Design is fault-tolerant
Beam Energy | 833 MeV
Beam Current | 2 mA
Emittance (trans/long) | 25 / 32 mm・mrad
Simulations with 3D fields
show no significant halo growth

## Slide 14: Booster Injection Optimized to Reduce Peak Charge Density and Space Charge Tune Shift
Longitudinal Painting
First 4 turns
After 270 turns
Bunches injected only if phase fits the offset dashed box.
Phase (rad)
dp/p
dp/p
Phase (rad)
Painted distribution after 270 turns has low longitudinal emittance, less tails, lower peak density, and lower transverse space charge than
Phase (rad)
Intensity (arb. units)
Transverse Painting
Orbit trajectory relatively to the foil during painting
Nearly uniform distribution
after injection
4-D distribution is similar to KV-distribution
Foil
Final
Beam

## Slide 15: Presently, Losses in Booster Limit Beam Intensity [2]
W. Pellico,
S. Nagaitsev
See Jeff Eldred’s talk

## Slide 16: PIP-II Higher Injection Energy and Painting Mitigate Losses at Booster Injection
The space charge tune shift to be reduced by a factor of 2.5 (~0.4 → 0.15) comparatively to present. We expect no space-charge-driven losses at PIP-II Injection.
  Space charge scales as where is the r.m.s. beam emittance and are relativistic factors. Ratio of is a factor 2
  Painted distribution is more uniform reducing peak space charge by factor of 2.
  Thus, the space charge with Np=6.5e12 at 800 MeV, painted, will be equivalent to that of Np=1.7e12 presently.
Direct bucket injection and the higher injection energy will eliminate longitudinal losses associated with adiabatic capture and RF noise

## Slide 17
Bunch-by-Bunch chopping – Demonstrated in 2017-2018
SRF
  High Q0 and high gradient HB650 MHz cavities
  LB650 cavities, procedures to apply nitrogen doping have to be optimized for the cavity shape
  Suppression of Microphonics and LLRF
Booster
  Intensity limits need to be understood
  The Booster is an old machine not originally designed to run this intensity
    Magnet pole tips are directly exposed to beam field.
    Operation of Booster systems with new parameters requires upgrades and modifications of ancillary systems
PIP-II Technical Challenges

## Slide 18: PIP2IT Serves As Testbed for Critical Technologies
RFQ
MEBT
HWR
SSR1
30 keV
HEBT
22 MeV
PIP2IT is used to demonstrate critical technologies:
RFQ ✔️
Bunch-by-bunch chopper ✔️
Beam dynamics in Front End ✔️
HWR and SSR CMs with cavities
LLRF
Laser wire profile monitor
HWR and SSR1 - Fall-Winter 2019-2020
Beam Test test to April to Oct 2020
CM test facility after beam test
10 MeV
2.1 MeV
PIP2IT

## Slide 19: PIP2IT Serves As Testbed for Critical Technologies
RFQ
MEBT
HWR
SSR1
30 keV
HEBT
22 MeV
PIP2IT is used to demonstrate critical technologies:
RFQ ✔️
Bunch-by-bunch chopper ✔️
Beam dynamics in Front End ✔️
HWR and SSR CMs with cavities
LLRF
Laser wire profile monitor
HWR and SSR1 - Fall-Winter 2019-2020
Beam Test test to April to Oct 2020
CM test facility after beam test
10 MeV
2.1 MeV
PIP2IT
Tested with beam
In 2017-2018
Added in
2019

## Slide 20: Schedule Overview
FY27
FY26
FY25
FY24
FY23
FY22
FY21
FY20
FY19
FY18
FY17
CD-2
CD-3a
FY28
DOE and International Partners
Receipt of largest
single in-kind contribution
Retirement of several high technical risks
CD-1
Approval
CD-3
Tier 0 - CD-4
FY29
FY 30
Cryoplant Building Construction
PIP2IT Program
Procurement of components
Installation & Commissioning
Linac Complex Civil Construction
PDR Complete
Beneficial Occupancy of the Linac Tunnel
Planned Project Complete (early CD-4)
DOE Activity
DOE and International Partners
HWR procurement

## Slide 21
Subsystem (count) | Cavities | Cryomodules | RF Systems & Cryoplant
HWR (1) |  | US (ANL) | US
SSR1 (2) |  | US | DAE
SSR2 (7) |  |  | DAE
LB650 (11) |  |  | DAE
HB650 (4) |  |  | DAE
Cryoplant (1) |  |  | DAE
UKRI
CNRS/IN2P3
INFN
DOE
DAE
CEA
PIP-II First US Project with Major In-Kind Contributions
International partnerships are essential for the success of the
PIP-II Project

## Slide 22: PIP-II Groundbreaking – 15 March 2019

## Slide 23: Conventional Facilities
Cryogenics Plant Building
Design Complete;
Ready for Procurement
Site Clearing Complete
Under special authorization
prior to CD-2/3a granted by DOE

## Slide 24: HWR Cryomodule Moved to PIP2IT
Developed and Built by Argonne National Lab
8 x 162.5 HWR, up to 2 MeV energy gain per cavity, 8 solenoids
Delivered to Fermilab in August 2019
Cooldown in December
Beam acceleration planned in April

## Slide 25: SSR1 Will be Moved to PIP2IT in December 2019
Developed and built at Fermilab
8 x 325 MHz Single Spoke Resonators, up to 2.05 MeV energy gain per cavity, 4 solenoids
  Includes Partner cavity
To be moved to PIP2IT in December
Beam acceleration in Summer

## Slide 26: SSR1 – Indian Cavity Meets Performance
High Q at high gradient and field emission free
BARC cavity has the best cavity Q performance up to date
Data by A. Sukhanov

## Slide 27: Cavity Processing Recipe Optimized, HB650
Optimization of the processing procedure (EP) for the nitrogen
doped cavities resulted in cavities exceeding requirements

## Slide 28: Joint PIP-II/AD Booster Intensity Studies Team and Task Force Were Formed
Joint PIP-II/AD studies team has been created
  Numerical and experimental studies of high intensity effects in Booster at injection and transition
  PyOrbit and Synergia for injection
  Locally developed codes for transition as well as Synergia
AD formed a task force
  Understand impact of the PIP-II interfaces on the accelerator complex
  Investigate beam dynamics issues associated PIP-II in details

## Slide 29: Summary
The project makes good technical progress towards completing the preliminary design and with prototyping of critical technologies. The main focus is
  Cryoplant building
  SRF and Cryomodules
  Test of HWR and SSR1 prototype with beam at PIP2IT
  Interfaces with the Booster
DOE baseline review (CD-2) is scheduled in January 2020
  Scope
  Cost
  Schedule

## Slide 30: Backup slides

## Slide 31: Neutrinos to Minnesota…generation 2  3 (DUNE)
NOvA…our present flagship neutrino experiment

## Slide 32: Linac Design is Robust, Fault-Tolerant
Fault studies were performed using TraceWin
Linac can tolerate loss of any single element, and meet requirements after retuning
  Last one or two HB650 cavities can be used to compensate loss of cavities and keep the energy constant
Linac can operate if cavities of one single type underperform by 20%.
  There is little effect on the beam dynamics if cavities underperform by 10%
Linac can meet KPPs with one of following cryomodules lost: 1) last SSR2 CM, 2) first LB650 CM, 3) last LB650 CM, 4) last HB650

## Slide 33: Accelerator Complex Upgrades
Upgrades to Booster, Recycler, and Main Injector (MI) required to accommodate:
  increased injection energy (400 MeV to 800 MeV)
  increased intensity (4.3E12 to 6.5E12 Booster, 5E13 to 7.5E13 MI)
  higher repetition rate (15 Hz to 20 Hz)
Scope of Ring upgrades:
  New Booster Injection girder
  New 53 MHz Recycler cavities
  Upgraded Main Injector RF Cavities
    Two Power Amplifiers (PA) operation of MI RF cavity
New beam line from the superconducting Linac to the Booster, new beam absorber line and beam dump
MI Cavity Model with two PAs

## Slide 34: Bunch-by-Bunch Chopping Demonstrated
Arbitrary chopping patterns out of 162.5 MHz bunch trains at 20 Hz can be obtained
Kicked bunches intercepted with a scraper → passing bunches recorded with Resistive Wall Current Monitor (RWCM)
50-Ohm Kicker
200-Ohm Kicker
DPI
F-scraper

## Slide 35: Beam in Dynamics in MEBT Meets Expectations
Beam dynamics in PIP2IT closely matches simulations. Beam quality meets requirements
Measured transverse emittance 0.22 mm*mrad
Measured longitudinal emittance 0.34 mm*mrad
Transverse Beam Envelopes
Simulated and Measured
Bunch length vs. buncher cavity voltage
Charge 1.b,c
Garcia

## Slide 36: Presently, Losses in Booster Limit Beam Intensity [1]
Majority of intensity losses happen in 5 ms after injection
Losses below 5E12 are likely longitudinal, related to not optimal adiabatic capture and feedback performance
Losses significantly increase after intensity exceeds 5E12.
C. Bhat